## Slide 1: WF on multiple ending positions in a UL subframe in FeLAA
Broadcom, CableLabs, Charter, Comcast,...
3GPP TSG RAN WG1 Meeting #92 R1- 1803044
Athens, Greece, 26th Feb – 2nd Mar 2018
Agenda item: 6.2.2.1

## Slide 2: Background (1)
Partial subframes ending at symbol 3 can be used to transmit a significant amount of data due to the very high SINR observed in typical 5GHz small cell configurations.
This is evident from the UL SINR cdf of the 3GPP Indoor simulation model
It can be seen from the above SINR CDF, 70% of the LAA users in the 3GPP Indoor model can support 64 QAM and 50% of the users can support 256QAM.

## Slide 3: Background (2)
The following is a table of the number of UL interlaces to the number of bytes that can be carried in 3 UL symbols considering both 64 QAM and 256 QAM for LAA
From the above table, it is clear that a significant amount of data can be transmitted over 3 UL symbols for a large proportion of UEs.

## Slide 4: Background (3)
In addition, even Best Effort traffic with large IP packets can have smaller Transport Blocks due to segmentation and (re)assembly at the RLC and MAC. So, a large number of such smaller packets can be carried in an UL end partial subframe ending at symbol #3.
Subframes ending at symbol #3 and symbol #10 will also increase channel utilization and spectral efficiency of LAA.
  The LAA eNB or UE can win the channel at any time instant. However, COTs are in integer multiples of 1ms and UL transmissions can only start at 0.5ms boundaries. So, LAA can waste up to 0.5ms of transmission opportunity.
  Definition of a partial subframes ending at symbol #3 or symbol #10, will enable LAA to utilize an additional 3 symbols of transmission every time it wins the COT at or after the end of symbol #3 and before the end of symbol #6 or after the end of symbol #10 and before the end of the subframe.
Increase in the number of ending positions in UL subframes will also reduce the chances of the UE having to transmit lower priority data or padding in order align the end of the SF to the available choices
Partial subframes ending at symbol #3 and symbol #10 have already been defined for the LAA DL, much for the same reasons as discussed above. So, it is only natural to define them for LAA UL too, especially since defining such subframes does not introduce any significant implementation complexity.

## Slide 5: Proposal
UL subframes ending at the end of symbol 3 and symbol 10 respectively shall be supported. (full subframe symbol numerology: 0, 13)