## Slide 1: Way Forward on cell confirmation and RRM measurement
Huawei, HiSilicon, ….
3GPP TSG RAN WG1 Meeting #92
Athens, Greece, 26 Feb – 2 March 2018
Agenda item 6.2.6.1.1.1
R1-1803063

## Slide 2: Background
It is discussed in contributions from a couple of companies regarding the cell confirmation and RRM measurement when WUS is used for synchronization.
The following alternatives are identified based on the input from companies:
  If WUS/DTX is adopted:
    Alt.1:
      Cell confirmation is based on NPSS/NSSS/NRS with a longer cycle compared with DRX cycle for low to medium mobility case;
      Cell confirmation is based on NPSS/NSSS/NRS on every DRX cycle for high mobility case;
    Alt.2:
      Cell confirmation is based on NPSS/NSSS/NRS on every DRX cycle for all mobility;
  If WUS/GTS is adopted in addition to WUS/DTX:
    Cell confirmation can be based on WUS/GTS for all mobility;

## Slide 3
Proposals:
If WUS/DTX is adopted,
  Cell confirmation can be based on NPSS/NSSS/NRS with a longer cycle compared with DRX cycle for low to medium mobility case;
  Cell confirmation is based on NPSS/NSSS/NRS on every DRX cycle for high mobility case;
Consider relaxing the serving cell RRM measurement period to achieve power saving gain from WUS