## Slide 1: Way Forward on sub-grouping for WUS in NB-IoT
Huawei, HiSilicon, ….
3GPP TSG RAN WG1 Meeting #92
Athens, Greece, 26 Feb – 2 March 2018
Agenda item 6.2.6.1.1.2
R1-1803064

## Slide 2: Background
It was agreed in RAN1#90bis:
  RAN1 assumes that introduction of WUS does not alter PO/PF definition
  At least in a UE’s DRX cycle:
    WUS supports at least being applied to all the UEs monitoring WUS associated to a PO in a cell NB-IoT carrier;
      FFS: eNB can configure WUS being applied to a group of more than one of the UEs associated to a PO in a cell NB-IoT carrier
      Send LS to request RAN2 input on feasibility of UE groups for WUS. (Xiaolei, HiSilicon, prepare draft LS in R1-1719102, which is endorsed and approved in R1-1719207)
RAN2 replies the LS in RAN1#92 in R1-1801306, in which RAN2 confirms the feasibility of configuring the WUS to be applied to a group of UEs associated to one PO :
  RAN2 had an e-mail discussion and reached to the following conclusions for NB-IoT and eMTC:
  From RAN2 perspective, it is feasible to configure the WUS to be applied to a group of UEs associated to one PO. It should be noted that some companies have raised concerns about the benefit and added complexity.

## Slide 3
Proposals:
eNB can configure WUS being applied to a group of more than one of the UEs associated to a PO in a NB-IoT carrier
eNB configures UE the number of WUS associated to one PO in a DRX cycle from the set {1, 2, 4, 8}.