## Slide 1: Summary of offline discussion on synchronization for CA
Ericsson
3GPP TSG RAN WG1 Meeting #92 R1-1803097
Athens, Greece, 26th March – 2nd March 2018
Agenda item – 6.2.3.1.2

## Slide 2: ISSUE 1
I1: If two or more potential synchronization carriers are present [in Set-B], FFS how the UE selects one of the carrier to be used as the synchronization carrier.
Proposal for offline consensus:
Down-select between options:
  Opt 1. Select the carrier in Set-B with highest Rel-14 priority sync reference. Carrier is not reselected unless synchronization is lost. Rel-14 procedure applies to the selected carrier.
  Opt 2. Select the carrier in Set-B with highest carrier priority
    New priorities are introduced

## Slide 3: ISSUE 2
I2: Is DFN value common to all aggregated carriers?
Proposal for offline consensus:
Note: It is RAN1 understanding that the DFN value is common to all aggregated carriers.
RAN1 assumes that the DFN offset value is common to all aggregated carriers from a UE point of view.

## Slide 4: ISSUE 3
I3: Are SLSS resources configured in the same way for all aggregated carriers?
Proposal for offline consensus:
UE may assume number and location of SLSS resources is the same in all the aggregated carriers.
RAN1 assumes a UE may be configured a non-synchronization carrier by defining the location of the SLSS resources and by configuring the UE to not transmit SLSS on that carrier.
  FFS how to ensure it when using preconfiguration.

## Slide 5: ISSUE 4
I4: On which carriers is SLSS transmitted?
Proposal for offline consensus:
The UE is configured one of the following options:
  SLSS is transmitted (based on Rel-14 procedure) on selected sync carrier from Set-B
  SLSS is transmitted on all carriers from Set-B
  FFS: how to handle limited TX capabilities, and details such as SLSS id, PSBCH contents, etc.
Each option is an independent UE capability
On top of this, Release-14 configuration applies to each carrier individually