## Slide 1
3GPP TSG RAN WG1 Meeting #92 R1-1803129
Athens, Greece, February 26th – March 2nd, 2018
Agenda item: 6.2.6.1.1.3
WF on WUS Sequence Design
Qualcomm, Samsung, LGE, ZTE, SaneChips

## Slide 2: Background
Agreement
WUS sequence is based on ZC-sequence
  When designing WUS sequence, negative impact on legacy NSSS detection should be avoided.
Agreement
Confirm the working assumption that the WUS sequence is a sequence mapping within one subframe as a basic unit and repeated/extended for multiple subframes to support larger coverage.

## Slide 3: Proposal
WUS sequence is a NSSS-like sequence as
  FFS RE-based cover codes c(m) using
    Hadamard codes
    Gold sequences
    M sequences
  FFS phase shift
  FFS time-varying design
In every subframe mapped with WUS sequence, the number of WUS sequences is at least 504, and every cell ID corresponds to at least one unique WUS sequence.
  FFS: whether WUS sequence is generated also based on UE group ID or other information.
,