## Slide 1: On Channel Access Study for 6 GHz
Ericsson
3GPP TSG RAN WG1 Meeting #92
Athens, Greece, 26th February – 2nd March, 2018
Agenda item: 7.6.5
Source: Ericsson
R1-1803259

## Slide 2: Scope
Two fundamental issues to consider for the 6 GHz band are the following:
  How to protect incumbent services operating in the band, e.g., fixed services (FS), fixed satellite services (FSS)?
    This is discussed in separate regulatory bodies, e.g., FCC, CEPT
  Introduction of unlicensed operation into the band
    If the 6 GHz band is opened for unlicensed operation, then it is important to ensure technology neutrality
In this document we consider #2

## Slide 3: Background: Channel Access for 5GHz Band
In 5 GHz (for a 20 MHz channel), IEEE 802.11 standard requires Stations
  [PD Clause] Defer to other transmission containing IEEE 802.11a preamble at a sensing level ≥ −82dBm
  [ED Clause] Defer to transmissions without a detected IEEE 802.11a preamble at a sensing level > −62dBm
Observation: the two-level channel access scheme is inherently unfair toward different technologies in the same operation band
EN 301 893 version 2.1.1
  Requires an LAA node deferring to all other transmissions at a sensed level ≥ −72dBm (for a 20 MHz channel)
  Grants exemption for IEEE 802.11a/n/ac compliant products to practice the two-level ED + PD scheme
Observation: Current EU regulatory exemption grants IEEE 802.11a/n/ac compliant products preferential 10 dB ED operation advantages over all other technologies in 5 GHz
  This exception was agreed to be phased out in the next revision of EN 301 893 such that all technologies are harmonized to a single ED threshold of −72 dBm (for a 20 MHz channel) for technology neutral access [1]
    Various companies are now proposing to perpetuate the exemptions for IEEE 802.11a/n/ac and to further extend the exemption to IEEE 802.11ax
    Some companies are proposing mandating the use of a single (existing) preamble scheme for channel coordination
    These proposals violate technology neutral access to the unlicensed spectrum

## Slide 4: Background: 6 GHz for unlicensed operation
6 GHz band is currently under consideration for unlicensed use in EU and US
  Potentially large amount of bandwidth
    Frequency ranges of 5925-6425 MHz and 5925-7125 MHz had been proposed by different parties
Next generation IEEE 802.11 systems are expected to include the 6 GHz spectrum as operating band
  The 802.11 WG already modified the IEEE 802.11ax Project Authorization Request to consider future 6 GHz license-exempt bands without further technical modifications (e.g., maintain two-level channel access scheme)

## Slide 5: Background: Channel Access for 6 GHz band
6 GHz is a greenfield spectrum without prior use of license-exempt technologies
  Therefore, same regulatory rules shall apply to all technologies and no technology shall warrant preferential exception
Essential for new unlicensed spectrum to be technology neutral
  Allowing continued innovation and competition to bring technology improvements
Regulation is expected to be finished in 2019-2020
  Essential for 3GPP community to provide technical inputs to regulatory discussion in 2018

## Slide 6: Introduction
In the following we provide brief highlights on
  The benefits of single unified ED threshold for both Wi-Fi and LAA
  The usefulness of PD in addition to ED for Wi-Fi channel access

## Slide 7: 3GPP Indoor Scenario
2 operators
1 channel of 20 MHz in the unlicensed band
One building:
  4 nodes per operator
  20 UEs per operator
Node TX power in unlicensed band: 18 dBm
3GPP FTP 3 traffic model with the file size of 500 kB
  50/50 traffic split in downlink and uplink
  UL ACK for Wi-Fi modelled
Sensing threshold
  IEEE 802.11: -82 dBm (PD) for another 802.11, -62 dBm (ED) for non-802.11
  LAA LTE: -72 dBm (ED) for every system
CAT4 settings: [15, 1023]
TXOP duration: 6 ms
Notes: Picture:
3 isolated buildings. In each building nodes of two operators are deployed. Blue color is for one operator, red for the second operator.
Circles represent APs, Points represent a subset of the considered UEs. User and AP positions are randomly generated every seed and performance in this study is based on average of multiple seeds.

## Slide 8: Wi-Fi + LAA LTE
LAA LTE applies only ED detection at −72 dBm
Wi-Fi network applies three different PD/ED settings
  Legacy
  ED lowered to −72 dBm
  ED and PD set to −72 dBm

## Slide 9: Findings on coexistence analysis
Single unified ED threshold @ -72 dBm for all technologies
  Improves performance for BOTH Wi-Fi and LAA
PD @ -82 dBm with ED @ -72 dBm
  Does not provide material performance improvement to Wi-Fi

## Slide 10: Conclusions
Proposal 1: 3GPP should study channel access techniques for efficient and technology-neutral unlicensed spectrum sharing for 6 GHz band
Proposal 2: 3GPP should provide technical input to regulatory bodies to ensure fair access to unlicensed spectrum in 6 GHz

## Slide 11: References
[1] O. Pellay, "Outcome from BRAN86 on coexistence," ETSI TC BRAN Submission BRAN(16)35r1, Feb. 15th, 2016. [Online]. Available: https://docbox.etsi.org/BRAN/BRAN/05-CONTRIBUTIONS/2016/BRAN(16)000035r1_Outcome_from_BRAN86_on_coexistence.pptx

## Slide 12: Annex: Wi-Fi + Wi-Fi
Network A always applies legacy settings
Network B applies three different PD/ED settings
  Legacy
  ED lowered to −72 dBm
  ED and PD set to −72 dBm