## Slide 1
3GPP TSG RAN WG1 Meeting #92 R1-1803288
Athens, Greece, February 26th – March 2nd, 2018
Agenda item: 7.1.3.1.1
Summary of PDCCH DMRS Sequence
Samsung

## Slide 2: Background
Summary of proposals
Company | Tdoc # | of DMRS
Samsung | R1-1801973 | 
Vivo | R1-1801530 | 
ZTE | R1-1801621 | 
MediaTek | R1-1801645 | 
Intel | R1-1802406 | 
DOCOMO | R1-1802479 | 
Nokia | R1-1802536 | 
Qualcomm | R1-1802833 | 
Ericsson | R1-1802902 | 

## Slide 3: Evaluation Results
Evaluation is based on RMSI parameters
  The ID in all proposals is cell ID with respect to RMSI evaluation
  q=1 in Vivo’s proposal
  SFN=0 in Intel’s proposal for fair comparison
 | 72 REs |  | 144 REs |  | 288 REs | 
 | Mean (dB) | Max (dB) | Mean (dB) | Max (dB) | Mean (dB) | Max (dB)
Samsung | -18.5703 | -7.2789 | -21.5998 | -10.5905 | -24.6470 | -12.8010
Vivo | -17.7984 | -7.1466 | -21.0197 | -10.4955 | -23.8467 | -12.7027
ZTE | -18.1729 | -6.8875 | -20.8986 | -9.9076 | -23.8460 | -11.8867
MediaTek, DOCOMO, Nokia, Qualcomm, Ericsson | -17.9704 | -6.9293 | -20.9195 | -9.1942 | -23.8291 | -11.6428
Intel | -17.9947 | -6.8875 | -20.8986 | -9.9076 | -23.8460 | -11.8867
TABLE: Normalized cross-correlation of PDCCH DMRS sequences