## Slide 1: Offline Summary on CA Aspects
Samsung
R1-1803300
3GPP TSG RAN WG1#92
Athens, Greece, Feb. 26 – March 2, 2018
Agenda item 7.1.3.4.2

## Slide 2: Semi-static HARQ-ACK Codebook - Components
Consider the superset of possible HARQ occasions over all configured BWPs?
  HARQ-ACK codebook is not carried over when active UL BWP switches but for paired spectrum, active UL BWP may not switch when active DL BWP switches
  For either paired or unpaired spectrum, active DL BWP on SCells can switch without the active UL BWP on the PCell switching
  Alternatives are: (a) DL association set corresponds to one BWP per cell, (b) DL association set corresponds to one BWP and one DL DCI format (either 1_0 or 1_1) per cell
Consider the minimum of {number of candidate PDSCH occasions, configured number of HARQ processes} in determining the HARQ association set?
  There is benefit but was argued it can be achieved by different means through gNB implementation – no consensus
Consider the minimum of {number of candidate PDSCH occasions per slot, number of PDSCH a UE can receive in a slot} in determining the HARQ association set?
  Consensus to support determining the HARQ association set based on the minimum of {number of candidate PDSCH occasions per slot, number of PDSCH a UE can receive in a slot}
Consider CBG configuration per DL BWP (also in conjunction with BWP A.I.)?
Should dynamic SFI be used to determine PDSCH reception occasions?
  Consensus is that dynamic SFI is not used to determine PDSCH reception occasions.

## Slide 3: Semi-static HARQ-ACK Codebook - Components
Restrict HARQ-ACK timings and pdsch-symbolAllocation table for DCI format 1_0 to be a subset of ones configured for DCI format 1_1 in order to reduce the HARQ-ACK codebook size?
  Consensus to support restricting HARQ-ACK timings and pdsch-symbolAllocation table for DCI format 1_0 to be a subset of ones configured for DCI format 1_1
  Example: Configured HARQ-ACK timing for DCI format 1_1 are {2, 6, 9}  then, possible timings for DCI format 1_0 are {2, 6}.
    UE should not expect to be indicated by DCI format 1_0 a HARQ-ACK timing other than {2, 6}.
UE always reports 2 HARQ-ACK bits for all DL BWPs of a cell if configured with Number-MCS-HARQ-DL-DCI =2 in at least one DL BWP of the cell.
  Yes, if the HARQ-ACK codebook can carry over different DL BWPs of the cell when the DL BWP part switches within the DL association set
  No, otherwise.
  Will be resolved depending on the resolution of the first bullet in the previous page

## Slide 4: Semi-static Codebook: Fallback Operation
Working assumption – RAN1 NR AH 1801: In case a UE is configured for semi-static HARQ-ACK codebook determination, when the UE detects to receive only one PDSCH on the Pcell, the UE reports HARQ-ACK only for the one PDSCH
  FFS whether additional constraints are necessary for the above operation
Proposals to achieve fallback for semi-static HARQ-ACK codebook
  Option1: If DCI format 1_0/1_1 indicates PUCCH resource for PUCCH format 0 or 1 for UE to transmit 1-2 HARQ-ACK bits (R1-1802108, R1-1801740, R1-1802217)
    Supported by OPPO
  Option2: If UE detects DCI format 1_0 with counter DAI value of 1 (R1-1801627, R1-1801827, R1-1801989)
    Same but also add 1-bit counter DAI to DCI format 1_1 (R1-1802418)
    Supported by Nokia, Samsung, Huawei, HiSi
  Option3: If UE detects only one PDSCH in the first slot of DL association set (R1-1801740, R1-1802573)
    Similar but have the k1 value for fallback HARQ-ACK codebook indicated by RRC (R1-1802845)
    Supported by CATT, LGE, Interdigital, Sharp, and Qualcomm
  Option4: Do nothing – no need to resolve ambiguity, gNB implementation issue
    Supported by Docomo, Nokia

## Slide 5: HARQ-ACK Codebook
Default HARQ-ACK codebook: Dynamic (R1-1802418, R1-1802917) or semi-static (R1-1802540)?
  Doesn’t matter due to agreement from last meeting for single HARQ-ACK bit before RRC setup – no need to define default HARQ-ACK codebook type

## Slide 6: HARQ-ACK Codebook
Should Phase 1 support multiple PDSCHs at different time instances on a same BWP/cell being scheduled from same PDCCH monitoring occasion?
  E.g. both same-slot and cross-slot scheduling from same PDCCH monitoring occasion
  Consider/Yes (R1-1801740, R1-1801989), No? (R1-1802917)
How to select PUSCH for UCI multiplexing in time domain
  First PUSCH transmission in slot indicated for HARQ-ACK (R1-1802217, R1-1802418)
  PUSCH scheduled by first received UL grant in slot indicated for HARQ-ACK (R1-1801348)
  Transmit in PUCCH or PUSCH, whichever occurs earlier in slot (drop PUSCH if it is the PUCCH)
HARQ-ACK for SPS PDSCH in multiple cells
  Specifications only allow configuration for a PUCCH format 0/1 resource but HARQ-ACK bits can be more than 2
  Option 1: Update RRC parameters to include configuration for a PUCCH format 2/3/4 resource
  Option 2: Bundle HARQ-ACK bits

## Slide 7: Other
PUSCH selection for HARQ-ACK multiplexing
  Based on the agreement from RAN1 NR AH 1801, UCI is multiplexed on PUSCH transmission [that starts at same or later symbol than corresponding PUCCH transmission in corresponding slot] on cell with the smallest index
  Additional proposals: Prioritize grant-based over grant-free PUSCH, prioritize PUSCH with smaller SCS or longer duration (R1-1801545, R1-1802108)
Support HARQ-ACK multiplexing of two PDSCHs before RRC setup by using C-DAI in DCI 1_0 (R1-1801740)
Semi-static HARQ-ACK codebook: If UE reported HARQ-ACK for a PDSCH reception occasion in a previous PUCCH slot, UE reports NACK for the PDSCH reception occasion in current PUCCH slot (R1-1802108)
Dynamic HARQ-ACK codebook: Whether to reorder counter DAI for a given PDCCH monitoring occasion to first count DCI 1_1 transmissions in first loop and then count DCI 1_0 transmissions in second loop (R1-1802217, R1-1802938)
No TB-based sub-codebook if all cells are configured for CBG-based HARQ-ACK (R1-1802217)
Semi-static HARQ-ACK codebook: 1-bit UL DAI indicates “less than or equal to 2 HARQ-ACK bits” or “maximum HARQ-ACK payload size“(R1-1802217)

## Slide 8: Other
Semi-static HARQ-ACK codebook: UEs capable of simultaneously receiving 2 PDSCHs, report 2 HARQ-ACK bits for a PDSCH reception occasion (R1-1802540)
  Introduce corresponding UE capability indication
Introduce RRC parameter to indicate interpretation of total DAI either according to current/LTE interpretation or with a predictive nature (R1-1802540)
Always pad TB-based HARQ-ACK bits for one (or two) PDSCH(s), if UE receives only CBG-based DCI format 1_1 (R1-1802845)
Semi-static HARQ-ACK codebook: Divide slot interval into N sub-intervals and reserve N entries for each slot and cell. HARQ-ACK for a PDSCH starting in sub-interval i is inserted in the i-th entry (R1-1802917)
Jointly consider counter DAI, DL total DAI, and UL total DAI to determine HARQ-ACK codebook in PUSCH (R1-1802697)
TA for carriers with multiple numerologies
Multi-slot scheduling: Is there anything missing from the current specifications other than UE not being expected to be scheduled PDSCH over more than 4 slots (otherwise, a larger bit-field for the DAIs is needed)
Whether to support PUCCH on a Scell for a UE

## Slide 9: References