## Slide 1: Way forward on UL DCI-Triggered CSIRS resource set for tracking
Qualcomm, Nokia, NSB, Intel, Ericsson, Orange, IITH, IITM, CEWiT, Tejas, ZTE, Sanechips, Apple, Sprint
3GPP TSG RAN WG1 Meeting #92 R1-181xxxx
Athens, Greece, February 26th – March 2nd, 2018
Agenda Item: 7.1.2.3.6

## Slide 2: Background: Why DCI-triggered CSIRS resource set for tracking is an essential feature for Rel-15?
Aperiodic TRS is essential given we have many aperiodic events as well as some periodic events which may not be aligned with periodic TRS
Aperiodic events
  SCell activation
    Without aperiodic TRS, SCell activation can be delayed further up to TRS periodicity (max 80 ms on top of SCell activation procedure delay).
    For SCell activation, network can activate SCell followed by aperiodic TRS, aperiodic CSI-RS. After SCell activation, UE can perform tracking based on TRS and CSI estimation and reporting based on CSI-RS. Network would be able to start data transmission based on reported CSI.
  BWP switching
    Upon BWP switching especially including RF retuning, a new reference signals for tracking is desirable before starting proper data reception.
    Similar to SCell activation, BWP switching can exploit aperiodic TRS and aperiodic CSI-RS for faster link adaptation.
  Multi-beam change
    Without aperiodic TRS, data reception can be delayed up to TRS periodicity in addition to other delays involved with beam change.
      Practically it is assumed that UE is not tracking TRS from multiple beams simultaneously
    With PDSCH beam change, proper data transmission can start after tracking and CSI reporting based on aperiodic TRS and aperiodic CSI-RS.
Periodic events
  Connected mode DRX
    Without aperiodic TRS, it requires UE to wake up in the middle of CDRX off when periodic TRS is not aligned with CDRX on-duration, not desirable for CDRX feature from UE power saving perspective.
  Idle mode DRX
    Without aperiodic TRS, it requires UE to wake up before paging occasion when SSB is not aligned with paging occasion, affecting standby time reduction roughly to 1/2.
From: R1-1802831 Remaining issues on TRS Qualcomm Incorporated
See also: R1-1802563 Remaining details of TRS design Nokia, Nokia Shanghai Bell

## Slide 3: Background: Huge overhead in FR2 due to the having only periodic CSIRS for tracking (I)
Using a UE specific periodic TRS’s would result in extreme amounts of overhead and scheduling restrictions for large numbers of UE’s in connected mode. Note that 500 UEs in connected mode is not uncommon in LTE cells.
Using a shared set of periodic TRS beams leads to large levels of overhead and scheduling restrictions at high frequencies where large numbers of antenna elements and correspondingly narrow PDSCH beams are needed for coverage. PDSCH beams based on 256 antenna elements would require 256/4=64 TRS beams that are power boosted with 6dB and thus can’t be FDM with data. We note that a 256 antenna elements antenna is something that can easily be implemented in the near future while NR should be designed for the coming decade and even larger numbers of antenna elements.
From: R1-1802757 Corrections related to TRS Ericsson

## Slide 4: Background: Huge overhead in FR2 due to the having only periodic CSIRS for tracking (II)
It has been agreed that the periodicity of TRS is 10ms, 20ms, 40ms and 80ms, and the PDSCH beam can be updated by MAC CE. So new TCI states may be considered as active TCI after receiving the MAC CE.
However the UE may not be able to track the beam immediately since there is no TRS for this new TCI states.
  Thus one possible way is to reserve some gap for the beam indication so that the UE can wait until the TRS transmission and the RRC reconfiguration of the TRS to change the TRS beam.
  However as shown in Figure 2, this may result in large latency.
  Another possible way is to support aperiodic TRS so that the gNB can schedule the aperiodic TRS for new beam tracking to reduce the latency of beam indication.
R1-1802404 Remaining Issues On TRS Intel Corporation

## Slide 5: Background: DCI-triggered CSIRS for for SCell tracking
Periodic TRS has been already agreed and the periodicity is one of 10, 20, 40, or 80 ms. In NR, SCell activation is done via MAC CE. It takes a long time for UE to demodulate the signaling from MAC layer.
In SCell activation scenario, periodic TRS can’t provide robust tracking results since UE has to wait for the next TRS cycle to receive TRS burst for Scell tracking.
SCell activation could be delayed further up to TRS periodicity . There are some options to solve this problem:
  Option1 :MAC CE activates ‘semi-persistent TRS’ when activating SCell. The ‘semi-persistent TRS’ can be scheduled for time/frequency tracking at the begining of SCell activation. Therefore UE can obtain accurate synchronization with SCell in time.
  Option2 :MAC CE triggers ‘aperiodic TRS’ when acivating SCell.
  Option3 :DCI triggers ‘aperiodic TRS’ when SCell is being activated. The DCI triggering happens at PCell, and then the aperiodic TRS happens at SCell during activation. However, the signalling for activating the SCell is the MAC layer signalling, and the demodulation time is long and indefinite.
    The DCI signalling is physical layer signalling, and the demodulation time is fast.
    Therefore the ‘aperiodic TRS’ happens earlier than the time when SCell activation is completed. This results in the behavior that the UE can receive the aperiodic TRS in the non-activated SCell, but this behavior has not been agreed.
R1-1801528 Remaining issues on TRS vivo

## Slide 6: Background: Does it require significant spec changes or increases gNB or UE complexity?
Rel-15 already supports UL DCI-triggered CSI-RS resource sets for L1-RSPR, and CSI feedback
  No RRC change is needed to enable a CSIRS resource set with TRS=‘ON’ to be triggered within exactly the same framework
  Just “one sentence” in the 38.214 is enough.
No additional gNB complexity or UE complexity since already aperiodic CSI-RS transmission occur for other purposes.

## Slide 7: Proposal
NR Rel-15 supports UL DCI-based triggering of a CSI-RS resource set containing CSI-RS resources with TRS-INFO set to “ON”.
A CSI-RS resource set for tracking is associated with a reporting setting ReportConfig with the higher layer parameter ReportQuantity set to 'No Report’.

## Slide 8: Appendix: Example TP