## Slide 1: Remaining issues for 7.1.3.3.4
NTT DOCOMO
R1-1803390
3GPP TSG RAN WG1#92
Athens, Greece, February 26th – March 2nd, 2018
Agenda item 7.1.3.3.4

## Slide 2: CR Correction

## Slide 3: Background (1)
The periodicity table SR was removed from subclause 9.2.4 of TS38.213 and only present in 38.331.

## Slide 4: Proposal
Remove the periodicity table for configured grant PUSCH transmission in subclause 6.1.2.3 of TS 38.214 to avoid the double specification
[…] A set of allowed periodicities P are defined in table 6.1.2.3-1 [38.331]. Table 6.1.2.3-1: Allowed periodicities P for uplink transmission without grant
 | CP | Possible values of periodicities P [symbols]
0 | Normal | 2, 7, n*14, where n={1, 2, 5, 10, 20, 32, 40, 64, 80, 128, 160, 320, 640}
1 | Normal | 2, 7, n*14, where n={1, 2, 4, 10, 20, 40, 64, 80, 128, 160, 256, 320, 640, 1280}
2 | Normal | 2, 7, n*14, where n={1, 2, 4, 8, 20, 40, 80, 128, 160, 256, 320, 512, 640, 1280, 2560}
2 | Extended | 2, 6, n*12, where n={1, 2, 4, 8, 20, 40, 80, 128, 160, 256, 320, 512, 640, 1280, 2560}
3 | Normal | 2, 7, n*14, where n={1, 2, 4, 8, 16, 40, 80, 160, 256, 320, 512, 640, 1024, 1280, 2560, 5120}

## Slide 5: Repetitions

## Slide 6: Discussion points
Proposed agreements
  Data mapping type A does not support more than one repetition within one slot.

## Slide 7: Discussion points
For configured grant,
  Whether to support more than one repetition within one slot
    Yes: LG, MTK, ZTE, CATT, Intel, vivo, DCM, OPPO, HW, TCL, Xiaomi, Spreadtrum
    No: Ericsson
  For data mapping type B, repetitions can be performed in consecutive symbols other than DL symbol(s) / in a time-domain consecutive way
    FFS: if semi-static DL/UL assignment configuration of a TO has direction confliction with scheduled PUSCH assigned symbols, the PUSCH transmission in that TO is cancelled or postponed
    FFS: conditions, e.g. transmission duration and/or starting symbol, Orpha UL symbol
    FFS: handling when one repetition is going to cross the slot boundary
  Supported by: MTK, DCM, CATT, HW, LG, vivo, OPPO, (Xiaomi), Intel, Spreadtrum

## Slide 8: Discussion points
In case of PUSCH mapping Type B repetition is going to cross the slot boundary
  Option 1: it is postponed to the same symbol allocation used across slots.
  Option 2: it is postponed to the first valid symbol can be used for UL transmission in the next slot.
  Option 3: It is invalid configuration

## Slide 9: Back-up

## Slide 10
Agreements:
Transmission direction implied by cell-specific RRC configuration cannot be overwritten by dynamic SFI to the other direction
Transmission direction implied by cell-specific RRC configuration for SCell/PSCell delivered in UE-specific manner cannot be overwritten by dynamic SFI to the other direction
For DCI granted multi-slot transmission (PDSCH/PUSCH/PUCCH) vs semi-static DL/UL assignment
  If semi-static DL/UL assignment configuration of a slot has no direction confliction with scheduled PDSCH/PUSCH/PUCCH assigned symbols, the PDSCH/PUSCH/PUCCH in that slot can be transmitted
  If semi-static DL/UL assignment configuration of a slot has direction confliction with scheduled PDSCH/PUSCH/PUCCH assigned symbols, the PDSCH/PUSCH/PUCCH transmission in that slot is cancelled

## Slide 11
Agreements:
For UL transmission without UL grant,
  The n-th transmission occasion of a K repetitions is associated with the (mod(n-1,4)+1)-th value in the configured RV sequence {RV1, RV2, RV3, RV4}, where n=1, 2, …, K.
  For RV sequence {0, 2, 3, 1},
    The initial transmission of a TB shall start at the first transmission occasion of the K repetitions.
  For RV sequence {0, 3, 0, 3},
    The initial transmission of a TB can start at any of the transmission occasions of the K repetitions that are associated with RV=0.
  (working assumption) For RV sequence {0, 0, 0, 0},
    The initial transmission of a TB can start at any of the transmission occasions of the K repetitions when K=1, 2 or 4;
    The initial transmission of a TB can start at any of the transmission occasions of the K repetitions, except the last transmission occasion when K=8.
  For any RV sequence, repetition end at the last transmission occasion within the period P.
  Note: The transmission occasion (TO) refers to the time domain resource allocation of one repetition in an aggregation with factor K where the aggregated transmission occasions start in resources configured by the offset and the period.
FFS: interaction with SFI

## Slide 12: Agreements
Agreements:
For grant-based DL or UL, transmissions where a TB spans multiple slots or mini-slots can be composed of repetitions of the TB
  The repetitions follow an RV sequence
    FFS how the sequence is defined in specification
  FFS if there is one repetition of the TB per slot in the case of repetitions using mini-slots
  FFS for grant-based DL or UL transmissions, if a TB can span multiple slots without repetitions
Agreements:
In case of slot-aggregation is configured
  the same symbol allocation is used across slots in UL
    Note: this aligns with the DL case
  the TB is repeated across the slots
  Discuss further offline the RV order for the DL/UL transmission (scheduled by DCI) spanning multiple slots (also checking the existing agreements made in the coding session)
In case of slot-aggregation is configured, the configuration is limited to rank 1 only for both DL and UL

## Slide 13: Agreements
Agreements: For PDSCH:
Supported combinations for PDSCH mapping type A:
  Starting symbol can be symbol index #0, 1, 2, 3 in a slot.
  Length of the PDSCH is at least X symbols, up to 14 symbols within a slot, such that slot boundary is not crossed
    FFS the value of X
Supported combinations for PDSCH mapping type B:
  Length of the PDSCH can be 2, 4, or 7 symbols.
  Starting symbol can be any position within a slot, such that slot boundary is not crossed.
Agreements: For PUSCH
PUSCH mapping type A:
  Starting symbol is symbol index #0 in a slot.
  Length of the PUSCH is at least Y symbols, up to 14 symbols
    FFS the value of Y
PUSCH mapping type B (All 105 combinations)
  Length of the PUSCH can be 2 through 14 symbols, and with 1 symbol as a working assumption
Starting symbol can be any position within a slot, such that slot boundary is not crossed.

## Slide 14: Agreements
Agreements:
Regarding “Length of the PDSCH is at least X symbols” (PDSCH mapping type A), X=3
Regarding “Length of the PUSCH is at least Y symbols” (PUSCH mapping type A), Y=4

## Slide 15: Repetition construction for PUSCH mapping type B

## Slide 16: Proposal 1
Resource allocation for configured grant PUSCH mapping Type B repetition within one slot:
  The first PUSCH TO is determined based on joint indication of starting symbol and length of the PUSCH.
  The resources for the following repetitions that are consecutive to the first PUSCH and have the same duration, i.e. are allocated back-to-back

## Slide 17: Proposal 2
In case of PUSCH mapping Type B repetition within one slot is going to cross the slot boundary
  Option 1: it is postponed to the same symbol allocation used across slots.
  Option 2: it is postponed to the first valid symbol can be used for UL transmission in the next slot.
  Option 3: It is invalid configuration