## Slide 1: WF on UE capability on CSI reporting and relaxation
LG Electronics, Ericsson, [InterDigital, VIVO, Qualcomm, Intel, MediaTek, ZTE, …]
3GPP TSG RAN WG1 Meeting #92 R1-180xxxx
February 26th – March 2nd, 2018
Athens, Greece
Agenda item: 7.2.2.2

## Slide 2: Proposals
  When A-CSI reporting on CSI only PUSCH with single CSI report is triggered, UE is not required to calculate/update the CSI for the A-CSI report in following cases.
    AP/P/SP CSI-RS is used for channel/interference measurement and M-L-N < Z.
    AP CSI-RS is used for channel/interference measurement and M-O-N < Z’.
      Alt 1: Z’=Z, Alt 2: Z’Z
    FFS: If M-L-N < Z, UE drops CSI
    Note.
      L=the last symbol of PDCCH triggering the A-CSI reporting
      M=the starting symbol of the PUSCH
      N= the TA value in unit of symbols (e.g., TA=1.4 symbol)
      O= the later symbol between the last symbol of AP CSI-RS resource for CMR and the last symbol of AP CSI-RS resource for IMR

## Slide 3: Proposals (con’t)
  Time offset of the CSI reference resource is derived from Z’ for a given CSI latency and numerology as follows:
      nCQI_ref is the smallest value greater than or equal to, such that slot n- nCQI_ref corresponds to a valid downlink slot.
        This is applied for AP/P/SP CSI reporting.
        This is applied when AP/P/SP CSI-RS is used for CSI calculation.
  When P/SP CSI-RS is used for channel/interference measurement for AP CSI reporting, UE is not required to measure channel/interference on the CSIRS received 0 to Z’ symbols before transmission time of first OFDM symbol of AP CSI reporting.
  FFS: When P/SP CSI-RS is used for channel/interference measurement in case of AP CSI reporting, UE does not expect that the latest CSIRS no later than CSI reference resource is received before triggering PDCCH.

## Slide 4: Proposals (con’t)
In Table I, (Z,Z’) values are baseline values which shall be supported by all UEs.
  All Z values in Table I are TBD.
  FFS whether (Z,Z’) values for low latency and high latency CSI in Table I are the same for a given numerology, in case of normal UE.
      Note. If those two values are the same for all numerology, then low and high latency is merged for normal UE.
Alt 1: In Table II, the (Z,Z’) values are reported as a UE capability for a given numerology and CSI latency, .
  For a given numerology and CSI latency, the (Z,Z’) value in Table II should be equal to or smaller than (Z,Z’) value in Table I.
  Note. all Z values in Table II are not specified.
Alt 2: In Table II, for a given numerology and CSI latency, whether or not to support the (Z,Z’) value in Table II is reported as a UE capability.
  For a given numerology and CSI latency, the (Z,Z’) value in Table II should be equal to or smaller than (Z,Z’) value in Table I.
  All Z values in Table I are TBD.
CSI latency | Units | 15 KHz SCS | 30 KHz SCS | 60 KHz SCS | 120 KHz SCS
Low latency CSI | Symbols | (Z1,1, Z’1,1) | (Z1,2, Z’1,2) | (Z1,3, Z’1,3) | (Z1,4, Z’1,4)
High latency CSI | Symbols | (Z2,1, Z’2,1) | (Z2,2, Z’2,2) | (Z2,3, Z’2,3) | (Z2,4, Z’2,4)
Table I. CSI calculation time Z for normal UE
CSI latency | Units | 15 KHz SCS | 30 KHz SCS | 60 KHz SCS | 120 KHz SCS
Low latency CSI | Symbols | (Z1,1, Z’1,1) | (Z1,2, Z’1,2) | (Z1,3, Z’1,3) | (Z1,4, Z’1,4)
High latency CSI | Symbols | (Z2,1, Z’2,1) | (Z2,2, Z’2,2) | (Z2,3, Z’2,3) | (Z2,4, Z’2,4)
Table II. CSI calculation time Z for advanced UE

## Slide 5: Appendix

## Slide 6
t
CSI reference resource
(slot n)
CSI reporting on PUSCH
t
(slot n)
CSI reporting on PUSCH
CSI reference resource
(slot n-1)
CSIRS locations where UE cannot conduct channel/interference measurement
(slot n-1)
CSIRS locations where UE can conduct channel/interference measurement
CSIRS locations where UE cannot conduct channel/interference measurement
CSIRS locations where UE can conduct channel/interference measurement
AP CSI trigger
nCQI_Ref=
nCQI_Ref=
Z’=5
Z=8
Z’=5
Z=8
<An example of Y =0>
UE cannot measure channel during the time between CSI trigger and PUSCH transmission

## Slide 7
t
(slot n)
Z’=15
CSI reporting on PUSCH
CSI reference resource
(slot n-2)
CSIRS locations where UE cannot conduct channel/interference measurement
CSIRS locations where UE can conduct channel/interference measurement
AP CSI trigger
t
(slot n)
CSI reporting on PUSCH
CSI reference resource
(slot n-1)
CSIRS locations where UE cannot conduct channel/interference measurement
CSIRS locations where UE can conduct channel/interference measurement
AP CSI trigger
nCQI_Ref=
nCQI_Ref=
Z=22
Z’=15
Z=22
<An example of Y =1>
UE cannot measure channel during the time between CSI trigger and PUSCH transmission