## Slide 1: Performance Analysis between existing PF0 mapping and improved mapping for SR and A/N
Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #92
Athens, Greece, 26th February – 2nd March 2018
AI: 7.1.3.2.5
R1-1803451

## Slide 2: Detection performance for PUCCH Format 0
 | 30 ns | 100 ns | 1000 ns
Old mapping | 6.2 dB | 6.4 dB | 6.5 dB
New mapping | 6.2 dB | 6.4 dB | 6.5 dB
Observation: For PUCCH format 0, the new mapping can supply same detection performance as the old mapping.
 | N,N | A,N | A,A | N,A
Old mapping | CS 0 | CS 9 | CS 6 | CS 3
New mapping | CS 0 | CS 6 | CS 9 | CS 3
Parameter | PUCCH format 0
Carrier Frequency | 3.5 GHz
System bandwidth | 20 MHz
Subcarrier spacing | 15 kHz
No. of subcarriers per PRB | 12
Number of symbol | 1
antenna configuration | 1Tx * 2 Rx
Channel model | TDL-C (30ns, 100ns, 1000ns delay spread)
UE velocity | 3 km/h
Payload size | 2 bits
Modulation | QPSK
Performance metric | DTX -> ACK < 10e(-2) ACK missing < 10e(-2) NACK->ACK < 10e(-3)

## Slide 3
As proposed in R1-1802727, to avoid misunderstanding between gNB and UE for certain scenarios, the new mapping for PUCCH format 0 should be adopted
Proposal
 | N,N | A,N | A,A | N,A
Initial CS | 0 | 6 | 9 | 3