## Slide 1: Proposals for AI7.1.3.3.4
DOCOMO
R1-1803471
3GPP TSG RAN WG1#92
Athens, Greece,
Agenda item 7.1.3.3.4

## Slide 2: Proposal 1
For PUSCH mapping type B with configured grant,
  When the periodicity is not larger than one slot, the repetitions should be performed in consecutive symbols other than DL symbol(s)
    i.e., more than one transmission occasion (TO) within one slot
  Otherwise, the repetition should be performed using the same symbol allocation across the consecutive slots and there is only one transmission occasion (TO) in each slot

## Slide 3: Proposal 2
At least following values are taken into account for further correction of TBS table in TS38.214 for supporting NR VoIP services
  328 bits, 344 bits, 688 bits, 720 bits, and 752 bits