## Slide 1: WF on antenna port mapping
CATT, ZTE, Qualcomm, LGE, OPPO, CMCC
3GPP TSG RAN WG1 Meeting #92 R1-1803472
Athens, Greece, February 26th – March 2nd, 2018
Agenda Item: 7.1.2.1.1

## Slide 2: Background
Agreement
For NR Rel-15, DMRS port ordering is performed as follows for one-CW transmission (DL)
Simple ordering with increasing index (port number)

## Slide 3: DMRS tables in 212
Configuration type 1
One Codeword: Codeword 0 enabled, Codeword 1 disabled |  | 
Value | Number of DMRS CDM group(s) without data | DMRS port(s)
0 | 1 | 0
1 | 1 | 1
2 | 1 | 0,1
3 | 2 | 0
4 | 2 | 1
5 | 2 | 2
6 | 2 | 3
7 | 2 | 0,1
8 | 2 | 2,3
9 | 2 | 0-2
10 | 2 | 0-3
11 | 2 | 0,2
12-15 | Reserved | Reserved
One Codeword: Codeword 0 enabled, Codeword 1 disabled |  |  |  | Two Codewords: Codeword 0 enabled, Codeword 1 enabled |  |  | 
Value | Number of DMRS CDM group(s) without data | DMRS port(s) | Number of front-load symbols | Value | Number of DMRS CDM group(s) without data | DMRS port(s) | Number of front-load symbols
0 | 1 | 0 | 1 | 0 | 2 | 0-4 | 2
1 | 1 | 1 | 1 | 1 | 2 | 0,1,2,3,4,6 | 2
2 | 1 | 0,1 | 1 | 2 | 2 | 0,1,2,3,4,5,6 | 2
3 | 2 | 0 | 1 | 3 | 2 | 0,1,2,3,4,5,6,7 | 2
4 | 2 | 1 | 1 | 4-31 | reserved | reserved | reserved
5 | 2 | 2 | 1 |  |  |  | 
6 | 2 | 3 | 1 |  |  |  | 
7 | 2 | 0,1 | 1 |  |  |  | 
8 | 2 | 2,3 | 1 |  |  |  | 
9 | 2 | 0-2 | 1 |  |  |  | 
10 | 2 | 0-3 | 1 |  |  |  | 
11 | 2 | 0,2 | 1 |  |  |  | 
12 | 2 | 0 | 2 |  |  |  | 
13 | 2 | 1 | 2 |  |  |  | 
14 | 2 | 2 | 2 |  |  |  | 
15 | 2 | 3 | 2 |  |  |  | 
16 | 2 | 4 | 2 |  |  |  | 
17 | 2 | 5 | 2 |  |  |  | 
18 | 2 | 6 | 2 |  |  |  | 
19 | 2 | 7 | 2 |  |  |  | 
20 | 2 | 0,1 | 2 |  |  |  | 
21 | 2 | 2,3 | 2 |  |  |  | 
22 | 2 | 4,5 | 2 |  |  |  | 
23 | 2 | 6,7 | 2 |  |  |  | 
24 | 2 | 0,4 | 2 |  |  |  | 
25 | 2 | 2,6 | 2 |  |  |  | 
26 | 2 | 0,1,4 | 2 |  |  |  | 
27 | 2 | 2,3,6 | 2 |  |  |  | 
28 | 2 | 0,1,4,5 | 2 |  |  |  | 
29 | 2 | 2,3,6,7 | 2 |  |  |  | 
30 | 2 | 0,2,4,6 | 2 |  |  |  | 
31 | Reserved | Reserved | Reserved |  |  |  | 
DL-DMRS-max-len=1
DL-DMRS-max-len=2

## Slide 4: DMRS tables in 212
Configuration type 2
One codeword: Codeword 0 enabled, Codeword 1 disabled |  |  | Two codewords: Codeword 0 enabled, Codeword 1 enabled |  | 
Value | Number of DMRS CDM group(s) without data | DMRS port(s) | Value | Number of DMRS CDM group(s) without data | DMRS port(s)
0 | 1 | 0 | 0 | 3 | 0-4
1 | 1 | 1 | 1 | 3 | 0-5
2 | 1 | 0,1 | 2-31 | reserved | reserved
3 | 2 | 0 |  |  | 
4 | 2 | 1 |  |  | 
5 | 2 | 2 |  |  | 
6 | 2 | 3 |  |  | 
7 | 2 | 0,1 |  |  | 
8 | 2 | 2,3 |  |  | 
9 | 2 | 0-2 |  |  | 
10 | 2 | 0-3 |  |  | 
11 | 3 | 0 |  |  | 
12 | 3 | 1 |  |  | 
13 | 3 | 2 |  |  | 
14 | 3 | 3 |  |  | 
15 | 3 | 4 |  |  | 
16 | 3 | 5 |  |  | 
17 | 3 | 0,1 |  |  | 
18 | 3 | 2,3 |  |  | 
19 | 3 | 4,5 |  |  | 
20 | 3 | 0-2 |  |  | 
21 | 3 | 3-5 |  |  | 
22 | 3 | 0-3 |  |  | 
23 | 2 | 0,2 |  |  | 
24-31 | Reserved | Reserved |  |  | 
One codeword: Codeword 0 enabled, Codeword 1 disabled |  |  |  | Two Codewords: Codeword 0 enabled, Codeword 1 enabled |  |  | 
Value | Number of DMRS CDM group(s) without data | DMRS port(s) | Number of front-load symbols | Value | Number of DMRS CDM group(s) without data | DMRS port(s) | Number of front-load symbols
0 | 1 | 0 | 1 | 0 | 3 | 0-4 | 1
1 | 1 | 1 | 1 | 1 | 3 | 0-5 | 1
2 | 1 | 0,1 | 1 | 2 | 2 | 0,1,2,3,6 | 2
3 | 2 | 0 | 1 | 3 | 2 | 0,1,2,3,6,8 | 2
4 | 2 | 1 | 1 | 4 | 2 | 0,1,2,3,6,7,8 | 2
5 | 2 | 2 | 1 | 5 | 2 | 0,1,2,3,6,7,8,9 | 2
6 | 2 | 3 | 1 | 6-63 | Reserved | Reserved | Reserved
7 | 2 | 0,1 | 1 |  |  |  | 
8 | 2 | 2,3 | 1 |  |  |  | 
9 | 2 | 0-2 | 1 |  |  |  | 
10 | 2 | 0-3 | 1 |  |  |  | 
11 | 3 | 0 | 1 |  |  |  | 
12 | 3 | 1 | 1 |  |  |  | 
13 | 3 | 2 | 1 |  |  |  | 
14 | 3 | 3 | 1 |  |  |  | 
15 | 3 | 4 | 1 |  |  |  | 
16 | 3 | 5 | 1 |  |  |  | 
17 | 3 | 0,1 | 1 |  |  |  | 
18 | 3 | 2,3 | 1 |  |  |  | 
19 | 3 | 4,5 | 1 |  |  |  | 
20 | 3 | 0-2 | 1 |  |  |  | 
21 | 3 | 3-5 | 1 |  |  |  | 
22 | 3 | 0-3 | 1 |  |  |  | 
23 | 2 | 0,2 | 1 |  |  |  | 
24 | 3 | 0 | 2 |  |  |  | 
25 | 3 | 1 | 2 |  |  |  | 
26 | 3 | 2 | 2 |  |  |  | 
27 | 3 | 3 | 2 |  |  |  | 
28 | 3 | 4 | 2 |  |  |  | 
29 | 3 | 5 | 2 |  |  |  | 
30 | 3 | 6 | 2 |  |  |  | 
31 | 3 | 7 | 2 |  |  |  | 
32 | 3 | 8 | 2 |  |  |  | 
33 | 3 | 9 | 2 |  |  |  | 
34 | 3 | 10 | 2 |  |  |  | 
35 | 3 | 11 | 2 |  |  |  | 
36 | 3 | 0,1 | 2 |  |  |  | 
37 | 3 | 2,3 | 2 |  |  |  | 
38 | 3 | 4,5 | 2 |  |  |  | 
39 | 3 | 6,7 | 2 |  |  |  | 
40 | 3 | 8,9 | 2 |  |  |  | 
41 | 3 | 10,11 | 2 |  |  |  | 
42 | 3 | 0,1,6 | 2 |  |  |  | 
43 | 3 | 2,3,8 | 2 |  |  |  | 
44 | 3 | 4,5,10 | 2 |  |  |  | 
45 | 3 | 0,1,6,7 | 2 |  |  |  | 
46 | 3 | 2,3,8,9 | 2 |  |  |  | 
47 | 3 | 4,5,10,11 | 2 |  |  |  | 
48 | 1 | 0 | 2 |  |  |  | 
49 | 1 | 1 | 2 |  |  |  | 
50 | 1 | 6 | 2 |  |  |  | 
51 | 1 | 7 | 2 |  |  |  | 
52 | 1 | 0,1 | 2 |  |  |  | 
53 | 1 | 6,7 | 2 |  |  |  | 
54 | 2 | 0,1 | 2 |  |  |  | 
55 | 2 | 2,3 | 2 |  |  |  | 
56 | 2 | 6,7 | 2 |  |  |  | 
57 | 2 | 8,9 | 2 |  |  |  | 
58-63 | Reserved | Reserved | Reserved |  |  |  | 
DL-DMRS-max-len=1
DL-DMRS-max-len=2

## Slide 5: Observations & proposals
Observation 1: The values of P0,…,Pv-1 should be specified clearly in specification to avoid any ambiguity in layer-2-port mapping operation
Proposal 1: Replace the label of “DMRS port(s)” with “P0,…,Pv-1” in Table 7.3.1.2.2-1, Table 7.3.1.2.2-2, Table 7.3.1.2.2-3 and Table 7.3.1.2.2-4 of 38.212

## Slide 6: Impact of ordering on 2-CW TX
Observation 2: The ordering of DMRS ports in vector [yP(0)(i)…yP(v-1)(i)]T has impact on 2-CW TX

## Slide 7: Impact of ordering on 2-CW TX w. rank adaptation
Preferred

## Slide 8: Proposals
Proposal 2:
  For Table 7.3.1.2.2-2 (configuration type=1, DL-DMRS-max-len=2) of 38.212, adopt the following changes:
    Reorder 0-4 to 2,3,0,1,4
    Reorder 0,1,2,3,4,6 to 2,3,6,0,1,4,
    Reorder 0,1,2,3,4,5,6 to 2,3,6,0,1,4,5
    Reorder 0,1,2,3,4,5,6,7 to 2,3,6,7,0,1,4,5

## Slide 9: Proposals
Proposal 3:
  For Table 7.3.1.2.2-4 (configuration type=2, DL-DMRS-max-len=2) of 38.212, adopt the following changes:
    Reorder 0,1,2,3,6 to 2,3,0,1,6
    Reorder 0,1,2,3,6,8 to 2,3,8,0,1,6
    Reorder 0,1,2,3,6,7,8 to 2,3,8,0,1,6,7
    Reorder 0,1,2,3,6,7,8,9 to 2,3,8,9,0,1,6,7

## Slide 10: Summary
Observation 1: The values of P0,…,Pv-1 should be specified clearly in specification to avoid any ambiguity in layer-2-port mapping operation
Observation 2: The ordering changes related to 2-CW TX in Table 7.3.1.2.2-2 and Table 7.3.1.2.2-4 of TS 38.212 only. In addition, no extra complexity is induced with such predefined order
Proposal 1: Replace the label of “DMRS port(s)” with “P0,…,Pv-1” in Table 7.3.1.2.2-1, Table 7.3.1.2.2-2, Table 7.3.1.2.2-3 and Table 7.3.1.2.2-4 of 38.212
Proposal 2:
  For Table 7.3.1.2.2-2 (configuration type=1, DL-DMRS-max-len=2) of 38.212, adopt the following changes:
    Reorder 0-4 to 2,3,0,1,4
    Reorder 0,1,2,3,4,6 to 2,3,6,0,1,4,
    Reorder 0,1,2,3,4,5,6 to 2,3,6,0,1,4,5
    Reorder 0,1,2,3,4,5,6,7 to 2,3,6,7,0,1,4,5
Proposal 3:
  For Table 7.3.1.2.2-4 (configuration type=2, DL-DMRS-max-len=2) of 38.212, adopt the following changes:
    Reorder 0,1,2,3,6 to 2,3,0,1,6
    Reorder 0,1,2,3,6,8 to 2,3,8,0,1,6
    Reorder 0,1,2,3,6,7,8 to 2,3,8,0,1,6,7
    Reorder 0,1,2,3,6,7,8,9 to 2,3,8,9,0,1,6,7

## Slide 11: Annex
Text proposal to 38.212