## Slide 1: WF on Delta_PUCCH_TF for NR PUCCH power control
Samsung, CATT
R1-1803477
3GPP TSG RAN WG1 Meeting #92
Athens, Greece, 26th Feb. – 2nd Mar. 2018
Agenda item 7.1.6.1

## Slide 2: Background: Current status
For PUCCH format 2, 3, and 4, for the case of small UCI payload size (less than or equal to 11)
  Alt1: ΔPUCCH_TF,c(i) = 10log10(K2∙BPRES(i))
    FFS: K2
  Alt2: ΔPUCCH_TF,c(i) = α∙nUCI(i) + β + 10log10(Nref/Nsymb) - 10log10(MRB)
    α: a constant that can be different depending on the PUCCH format
    nUCI: the number of UCI bits
    β: an offset value that can be different depending on the UCI types for each PUCCH format

## Slide 3: Observation (1/2)
For Alt1,
  ΔPUCCH_TF,c(i) = 10log10(K2∙BPRES(i))
  = 10log10(K2∙OUCI/NRE)
  = 10log10(K2∙OUCI) – 10log10(NRE)
  = 10log10(K2∙OUCI) – 10log10(MRB∙Nsymb∙12)
  = 10log10(K2∙OUCI) – 10log10(12) – 10log10(MRB∙Nsymb)
For Alt2,
  ΔPUCCH_TF,c(i) = α∙nUCI + β + 10log10(Nref/Nsymb) – 10log10(MRB)
  = α∙nUCI + β + 10log10(Nref) – 10log10(MRB∙Nsymb)
B
C
C
B’

## Slide 4: Observation (2/2)
In LTE
  PUCCH formats, 1, 1a and 1b: h(∙) = 0
  PUCCH format 1b with channel selection: h(∙) = (nUCI – 1)/2  Alt2
  PUCCH formats 2, 2a, 2b: h(∙) = 10log10(nUCI/4)  Alt1
  PUCCH formats 3: h(∙) = (nUCI – 1)/3  Alt2

## Slide 5: Proposal
For PUCCH format 2, 3, and 4, for the case of small UCI payload size (less than or equal to 11)
  ΔPUCCH_TF,c(i) = 10log10(K2∙BPRES(i)) where
    BPRES(i) = OUCI(i)/NRE(i)
    OUCI(i) is the number of actual UCI bits transmitted in i
    NRE(i) = MPUCCH,c(i) x number of subcarriers per PRB x number of DFT-s-OFDM/CP-OFDM symbols excluding DMRS symbols/tones
    FFS: K2 (there is no new RRC parameter introduced)