## Slide 1: Approximate Peak Data Rate and Scaling Factor Use Cases
Intel
R1-183485
3GPP TSG RAN WG1 Meeting #92
Athens, Greece, February 26 ~ March 02, 2018
Agenda 7.1.3.3.1

## Slide 2: Background (1/2)
Approximate Data Rate:

## Slide 3: Background (2/2)
RAN2 LS R1-18013424 ask for the following:
  RAN2 would like to understand the background and the potential scenarios where the UE reports the down scaled value (0.75) per band and per band combination

## Slide 4: Proposed General Use Cases
Use case explicitly discussed in RAN1 #91
  UE supporting 256 QAM, but is to only reach 64QAM peak data rate for a particular #MIMO layer and #CC.
Another Use cases identified
  UE sharing hardware resource between LTE and NR in EN-DC scenario.
    UE in NR SA in FR2 is able to reach 2 Gbps, but in EN-DC with additional LTE link in FR1 and due to sharing of the hardware resources, it is only able to support less than 2Gbps.
    RF capability of FR2 and FR1 might be completely separate, so supporting additional LTE CC in FR1 is possible without reducing #CC in FR2 from RF perspective.
  UE using the same hardware resource to support different UE processing time capability
    Possibility to indicate different peak data rate for the UE process time capability 2 (i.e. aggressive HARQ process times).

## Slide 5: Proposed Changes to Approx. Data Rate
To better address the use cases, and concerns from signaling overhead (from per band and per band combination signaling) the following changes are proposed:
f(j) is the scaling factor:
  The DL scaling factor can at least take are the values {1, 0.8, and0.75, 0.5, reserved}
  The UL scaling factor are the values {1, 0.8, 0.5, reserved}
  f(j) is signalled per CC and per baseband processing combination (BPC)band and per band combination as per UE capability signalling.

## Slide 6: Appendix: Use Cases for Specific Scaling Factors (1/2)
 |  | SCS (kHz) | Maximum CBW (MHz) | Maximum number of Layers | Maximum modulation order | Real Maximum data rate | Calculated with maximum values from BPC and band combination | Scaling factor
BPC |  | N/A | 100 | 4 | 8 | N/A | N/A | N/A
CA_1 | CC1 | 30 | 100 | 4 | 8 | R1 | R1 | 1
CA_2 | CC1 | 30 | 100 | 2 | 8 | R1 | 2*R1 | 0.5
 | CC2 | 30 | 100 | 2 | 8 |  |  | 
CA_3 | CC1 | 30 | 100 | 4 | 6 | 3/4*2*R1 | 2*R1 | 0.75
 | CC3 | 30 | 100 | 4 | 6 |  |  | 
Table from [1]
[1] R1-1801352, “Discussion on NR UE peak data rate,” Huawei, HiSilicon

## Slide 7: Appendix: Use Cases for Specific Scaling Factors (2/2)
NR | FR # | DL/UL | SCS | BW | NRB | #Layer | Mod | #CC | SF | Ts | OH | Approx. Data Rate
 | 2 | DL | 60 kHz | 50 MHz | 66 | 2 | 6 | 4 | 1.0 | 1.79e-5 | 0.18 | 1.616 Gbps
Assume UE is able to support Max 2Gbps in baseband
In NR SA,
In EN-DC, LTE+NR,
LTE | FR # | #CC | BW | Mod | SCS [kHz] | #Layer | T_SF | Max TBS-L1 | Max TBS-L2 | Peak Rate
 | 1 | 2 | 20 | 8 | 15 | 4 | 0.001 | 97896 | 195816 | 0.783 Gbps
NR | FR # | DL/UL | SCS | BW | NRB | #Layer | Mod | #CC | SF | Ts | OH | Approx. Data Rate | Sum of LTE+NR
Not possible | 2 | DL | 60 kHz | 50 MHz | 66 | 2 | 6 | 4 | 1.0 | 1.79e-5 | 0.18 | 1.61 Gbps | 2.39 Gbps
Target with SF | 2 | DL | 60 kHz | 50 MHz | 66 | 2 | 6 | 4 | 0.8 | 1.79e-5 | 0.18 | 1.29 Gbps | 2.07 Gbps
 | 2 | DL | 60 kHz | 50 MHz | 66 | 2 | 6 | 4 | 0.75 | 1.79e-5 | 0.18 | 1.21 Gbps | 1.99 Gbps