## Slide 1: WF on NPUSCH transmission with 3.75kHz subcarrier spacing
LG Electronics, …
R1-1805413
3GPP TSG RAN WG1 Meeting 92bis
Sanya, China, April 16th – 20th, 2018
Agenda item 6.2.7.6.2

## Slide 2: Background
Following agreements were made in previous meetings:
  3.75 kHz is also supported, in UL/DL configurations #1, [#3], #4, with the same definition of NB-slot and resource unit as FDD
  FFS if there any need for any other subcarrier spacing and/or slot structure for TDD
    This needs to take into consideration the co-existence of NPRACH and NPUSCH.
  For NPUSCH in NB-IoT TDD:
    For the NPUSCH transmissions with 15 kHz subcarrier spacing, both Multi-tone (3, 6, 12 subcarriers with RU lengths 4ms, 2ms, 1ms) and single tone (with RU length 8ms) transmissions are supported as in FDD NB-IoT for all the supported TDD configurations in TDD NB-IoT other than the TDD configuration #3 and [#6]. The number of supported subcarriers, and RU lengths for TDD configuration #3 and [#6] is FSS (The number of subcarriers and RU lengths as defined in FDD NB-IoT are not precluded).

## Slide 3: Proposals
Down-select following alternatives for NPUSH transmission with 3.75kHz subcarrier spacing
  Alt. 1: Allow transmission only when both 2 consecutive UL subframes are valid. Postpone transmission if NB-slot overlap with invalid UL subframe.
  Alt. 2: Allow transmission in valid UL subframes. Puncture symbols in NB-slot which overlap with invalid UL subframe.
  Alt. 3: UE assume that eNB would not schedule NPUSCH with 3.75kHz subcarrier spacing if invalid UL subframe is configured.