## Slide 1: RACH MSG2 to MSG3 delay
Ericsson
3GPP TSG RAN WG1 Meeting #92bis R1-1805573
Sanya, China, April 16th – 20th, 2018
Agenda item: 7.1.1.4.2

## Slide 2: Background
Scheduling delay of normal PUSCH in 38.214
  Slot for PUSCH transmission is given by slot delay K2
  K2 is given by table pusch-AllocationList
    Time domain resource assignment in DCI indicates entry in table to be used
    Default table in specification to be agreed
    RMSI can overwrite default table
  K2 can take values of 0,1,2,3,4,5,6,7,8,10,16,20,32 slots

## Slide 3: Background
Handling of large cells for normal PUSCH
  By configuring table with large values of K2, larger delays can be configured to allow large cell size
  No TA term in PDCCH to PUSCH timing delay
    Was removed in a previous version of the specification
  Network makes sure PUSCH preparation time N2 is always available to UE by signaling appropriate value of K2

## Slide 4: Timing of MSG3
RAN1#92 agreed to include time domain resource assignment in UL grant in RAR
  How to apply the time domain resource assignment in case of MSG3 PUSCH needs to be specified
  Time domain resource assignment can be used to support large cells also for MSG3 PUSCH
Difference between normal PUSCH and MSG3 PUSCH delay is the additional N1+L2 delay needed for MSG3
A solution with no RAR/RRC impact is preferred

## Slide 5: Proposal
Align MSG3 PUSCH timing with normal PUSCH timing
  Remove max TA from 38.213
Time domain resource assignment in UL grant uses same table as for normal PUSCH
Additional delay corresponding to N1+L2 is added to the K2 given by the normal PUSCH table
Network makes sure MSG3 PUSCH preparation time N1+N2+L2 is always available to UE by signaling appropriate value of K2

## Slide 6: TP 38.213 section 8.3