## Slide 1: Alignment of TBS and LDPC BG for URLLC NC-JT
Samsung
R1-1906979
3GPP TSG RAN WG1 Meeting #97
Reno, USA, May 13th–17th, 2019
Agenda item: 7.2.8.5

## Slide 2: Motivation (1/3)
TBS determination of UE
  When UE receives a codeword, it determines the TB size from
    The number of REs,
    Code rate R and modulation order
    Number of layers
LDPC base graph (BG) determination
  From the code rate and the determined TB size, BG is determined as follows.
Quantization
(to get proper granularity)
Find the closest value
not smaller than

## Slide 3: Motivation (2/3)
TBS / LDPC BG determination in HARQ
  In HARQ, BG and TBS should be the same for the initial- and re-transmission.
    In TS 38.212 section 7.2.2,
    For retransmission, MCS indices 29-31 are used in MCS table 1 and 3, indices 28-31 are used in MCS table 2
      Those MCSs indicate modulation order only.
      Target code rate information is not needed since the UE already knows the TBS.
Encoded LDPC CW
Systematic bit (TB+CRC)
Parity bit
Initial Tx
1st ReTx
Tx
Rx
Initial Tx
1st ReTx
Same LDPC BG ensured for initial and re-transmission

## Slide 4: Motivation (3/3)
TBS / LDPC BG determination for URLLC NC-JT
  The same principle for HARQ combining should be reused
  Multiple TRPs repeatedly transmit the same TB in different spatial / frequency / time domain.
    If each TRP transmits with independent codeword and UE determines its TBS and LDPC BG independently, misalignment of TBS and LDPC BG may occur at the UE.
    If the TBSs of codewords are misaligned, UE does not know which TBS is correct
      Needs blind decoding, and consequently longer latency, to find the correct TBS.
    If the LDPC BGs of codewords are misaligned, it is hard to achieve the combining gain of codewords since they are determined as ‘different codes’.
PRB 0
PRB 1
PRB 2
PRB 3
PRB 4
PRB 5
PRB 6
PRB 7
TRP 1
TRP 2
Rate matched
CW1
CW2
For 1 layer transmission,
same MCS with 16QAM, target code rate 0.33
* TBS from TRP1 = 768
* TBS from TRP2 = 576
TBS misalignment

## Slide 5: Proposals
Proposal. In URLLC NC-JT where each TRP transmits the same TB repeatedly, it needs to be ensured for a UE to determine the same TBS and same LDPC BG for each PDSCH.
  Above applies at least for Scheme 2b, 3, and 4.