## Slide 1: Summary #3 of Email discussion regarding the out-of-order HARQ issue
Agenda item: 7.2.6.4
Source: Qualcomm Incorporated
Title: Summary of Email discussion regarding the out-of-order HARQ issue
Document for: Discussion
3GPP TSG-RAN WG1 Meeting #96b
April 8th - 12th, 2019
Xi’an, China
R1-1907925

## Slide 2: Overview
This deck summarizes the Rel. 15 NR limitations that allow for perfect UE processing pipelining, and discusses the applicability of Solution 1-4 identified by RAN1 in case the limitations are maintained or relaxed.

## Slide 3: Rel. 15 NR Configuration and Scheduling Limitations
The objective of Rel. 15 NR configuration and scheduling limitations was to allow for perfect processing pipelining at the UE.
  The perfect pipelining means that one processing block is used for processing of one channel at a time, while it is guaranteed that all channels can meet their timeline.
Some examples are as follows:
  If additional DMRS is “configured” on a given cell, all PDSCHs, regardless of their allocation length, i.e., whether the carry additional DMRS or not, will follow the PDSCH processing capability #1 with pos0 != 0.
  If PDSCH timing capability #2 is “configured” on a given cell:
    all PDSCHs should follow the associated cap#2 N1
      Note that the case of pdsch-ProcessingType2-Limited is an exception.
    Additional DMRS cannot be configured on the same serving cell.
  If additional DMRS is not configured on the same cell, both type-A and type-B PDSCH allocations will follow PDSCH processing capability #1; The N1 for type-B PDSCH (2-symb and 4-symb allocations) is padded in case PDCCH and PDSCH are overlapping.

## Slide 4: Illustration of Rel. 15 Limitations
Assuming SCS = 30KHz and additional DMRS on a given serving cell, the UE processing pipelining is illustrated in the figure.
As shown in the figure, N1 of PDSCH2 is selected such that the overall timeline allows for using each processing block to perform processing for one channel at a time, i.e., perfect pipelining is feasible.

## Slide 5: Out-of-Order HARQ under Rel. 15 Limitations
Under the Rel. 15 NR configuration and scheduling limitations, even if the transmissions are out of order, the UE pipelining is not impacted.
In case of out-of-order HARQ, the UE only needs to buffer the low priority HARQ-ACK and report it after the transmission of the high priority HARQ-ACK.

## Slide 6: What if the Rel. 15 Limitations are Relaxed?
If Rel. 15 limitations are relaxed, i.e., different processing timelines can be configured on the same cell for efficient multiplexing of channels with different priorities, the UE pipelining issues should be addressed.
  In such a case, perfect pipelining `may’ not be feasible regardless of whether the transmissions are in-order or out-of-order.

## Slide 7: Description of the Solutions
First, based on the discussions so far, the following conclusions can be drawn:
  Case 1: If the Rel. 15 configuration/scheduling limitations are preserved, the UE pipelining is not impacted even if the transmissions are out-of-order.
  Case 2: If the Rel. 15 configuration/scheduling limitations are relaxed, the UE pipelining may be impacted regardless of whether the transmissions are in-order or out-of-order.
Solution 1: “The UE always processes the second PDSCH. The UE may or may not drop the processing of the first channel.”
  Applicable to Case 2.
  Allows the UE to terminate the processing of the low priority PDSCH in all cases, i.e., regardless of whether the transmissions are in-order or out-of-order.
Solution 2: “The UE processes both the first and second PDSCHs as a UE capability with no condition.”
  Applicable to Case 1.
  If Case 1 is agreed, no other solution is needed.

## Slide 8: Description of the Solutions
Solution 3: “The UE processes both the first and second channels under some conditions, e.g. using the CA capability. The conditions are reported as a UE capability. If the conditions are not satisfied, the UE behavior is not defined.”
  Applicable to Case 2.
  Guarantees the processing of all PDSCHs regardless of whether they are in order or out of order.
  Applicable to UEs with or without the CA capability

## Slide 9: Description of the Solutions
Solution 4-Alt1: “The UE always drops the first PDSCH”.
  Applicable to Case 2.
Solution 4-Alt2: “Some scheduling conditions should be defined. If not satisfied, the UE drops the processing of the first channel.”
  Applicable to Case 2.
  Defining the scheduling limitations based on #RBs/#layers/TBS is challenging.
    For each (#RBs,#layers,TBS), RAN1 should determine the number of symbols needed for processing the low priority channel.
    If for (#RB_i, #layers_i,TBS_i), X_i symbols is needed, then:
      The UE can process both the low and high priority channels if the gap between the two channels is X_i symbols.
      Otherwise, the UE can terminate the processing of the low priority channel.
  A more reasonable scheduling condition is based on the time gap between the two channels:
    The UE processes both channels if the gap between the end of low priority PDSCH and start of the high priority PDSCH is N1 symbols, where N1 is the minimum processing time of the low priority PDSCH.
    Otherwise, the UE can terminate the processing of the low priority channel.

## Slide 10: PDSCH + PDSCH Collision
Regardless of whether the PDSCH-to-PUCCH is in-order or out-of-order, the case of high priority unicast PDSCH overlapping with a low priority unicast PDSCH is allowed in Rel. 16.
Regardless of whether the processing timing capability of the two unicast PDSCHs are the same or different, the collision should be handled by the UE.
The applicability of the Solutions to PDSCH+PDSCH collision scenario:
  Solution 1 and 4-Alt1 allow for dropping the low priority PDSCH under both Scenario 1-1 and 1-2.
  Solution 2 does not address this scenario.
  Solution 4-Alt2 can address the issue if the scheduling condition is defined as “the UE drops the low priority PDSCH in case of collision” for both Scenario 1-1 and 1-2.
  Solution 3 addresses the collision scenario and allows the UE to process both PDSCHs without dropping under both Scenario 1-1 and 1-2.