## Slide 1: Comments to “On PDCCH blind detection for NR-DC: Comparison between Alt 1 and Alt 2”
Qualcomm Incorporated
3GPP TSG RAN WG1 Meeting #97
Reno, USA, May 13th – 17th, 2019
R1-1907946
Agenda Item: 7.1.3
Document for: Discussion & Decision

## Slide 2: Comments
Some essential information is missing in the original slides in R1-1907943
  The mandatory band combination is not included for alt. 1 when the UE does not report pdcch-BlindDetectionCA
  Alt. 2 is missing in the example 1 when the UE reports pdcch-BlindDetectionCA
Those missing information is added in highlighted text in the original slides (the original slides start from slide 3)

## Slide 3: On PDCCH blind detection for NR-DC: Comparison between Alt 1 and Alt 2
Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #97
Reno, USA, May 13th – 17th, 2019
R1-1907943
Agenda Item: 7.1.3
Document for: Discussion & Decision

## Slide 4
Alt 1：both pdcch-BlindDetectionMCG and pdcch-BlindDetectionSCG are always configured and not larger than UE capability pdcch-BlindDetectionMCG-UE and pdcch-BlindDetectionSCG-UE, respectively. Resulting in different NR-CA operation with MCG BC which is derived from NR-DC
  Consequence: UE gains nothing but can limit PDCCH BD configuration by reporting BlindDetectionMCG-UE (e.g. 1) less than the # of CCs in MCG, so does to SCG with BlindDetectionSCG-UE (e.g. 2), even total # of BD < 4
  E.g. Before SCG addition, 2 BDs for MCG as NR-CA
  After SCG addition, 1 BDs for MCG, 1 BD for SCG (total # of BD < 4)
  After SCG release, 2 BDs for MCG
Alt 2：A UE supporting NR-DC is not configured with pdcch-BlindDetectionMCG nor pdcch-BlindDetectionSCG, as same behavior as NR-CA
Consequence: in line with NR-CA in term of PDCCH BD configuration.
E.g. Before SCG addition, 2 BDs for MCG as NR-CA
After SCG addition, 2 BDs for MCG, 1 BD for SCG
After SCG release, 2 BDs for MCG
PDCCH blind detection for NR-DC
[1] R1-1907490 Discussion on PDCCH monitoring for NR-DC
If pdcch-BlindDetectionCA is not reported, e.g. for a NR-DC BC {MCG 2CCs, SCG 1CC} and {MCG 1CC, SCG 2CCs} mandatorily for alt.1

## Slide 5
Proposal
Proposal: For Rel-15 NR-DC, a UE supporting NR-DC without reporting pdcch-BlindDetectionCA is configured with neither pdcch-BlindDetectionMCG nor pdcch-BlindDetectionSCG.
  Send an LS to inform RAN2 (CC: RAN3)

## Slide 6
Annex
Corresponding update to FFS in previous agreement with Alt 2:

## Slide 7
Alt 1：both pdcch-BlindDetectionMCG and pdcch-BlindDetectionSCG are always configured and not larger than UE capability pdcch-BlindDetectionMCG-UE and pdcch-BlindDetectionSCG-UE, respectively. Resulting in different NR-CA operation with MCG BC which is derived from NR-DC
  Consequence: UE gains nothing but can limit PDCCH BD configuration by reporting BlindDetectionMCG-UE (e.g. 2) less than the # of CCs in MCG, so does to SCG with BlindDetectionSCG-UE (e.g. 2), even total # of BD < 4
  E.g. Before SCG addition, 3 BDs for MCG as NR-CA
  After SCG addition, 2 BDs for MCG, 1 BD for SCG (total # of BD < 4)
  After SCG release, 3 BDs for MCG
Alt 2：A UE supporting NR-DC is not configured with pdcch-BlindDetectionMCG nor pdcch-BlindDetectionSCG, as same behavior as NR-CA
Consequence: in line with NR-CA in term of PDCCH BD configuration.
E.g. Before SCG addition, 3 BDs for MCG as NR-CA
After SCG addition, 3 BDs for MCG, 1 BD for SCG
After SCG release, 3 BDs for MCG
Example#2 when pdcch-BlindDetectionCA is not reported
[1] R1-1907490 Discussion on PDCCH monitoring for NR-DC
If pdcch-BlindDetectionCA is not reported, e.g. for a NR-DC BC {MCG 3CCs, SCG 1CC} and {MCG 2CCs, SCG 2CCs} mandatorily for alt. 1

## Slide 8
Alt 1：both pdcch-BlindDetectionMCG and pdcch-BlindDetectionSCG are always configured and not larger than UE capability pdcch-BlindDetectionMCG-UE and pdcch-BlindDetectionSCG-UE, respectively.
  Example:
  If the UE reports BlindDetectionMCG-UE=2 and BlindDetectionSCG-UE=2
  E.g. Before SCG addition, 3 BDs for MCG as NR-CA
  After SCG addition, 2 BDs for MCG, 2 BD for SCG (full # of BD is used)
  After SCG release, 3 BDs for MCG
Alt 2：A UE supporting NR-DC is configured with pdcch-BlindDetectionMCG and pdcch-BlindDetectionSCG
  Example:
  If the UE reports BlindDetectionMCG-UE=2 and BlindDetectionSCG-UE=2
  E.g. Before SCG addition, 3 BDs for MCG as NR-CA
  After SCG addition, 2 BDs for MCG, 2 BD for SCG (full # of BD is used)
  After SCG release, 3 BDs for MCG
Example#1 when pdcch-BlindDetectionCA is reported
If pdcch-BlindDetectionCA is reported as 4, e.g. for a NR-DC BC {MCG 3CCs, SCG 2CC}