## Slide 1: Other issues on Multi-TRP / panel transmission “Alignment of TBS and LDPC BG for URLLC NC-JT”
Samsung
R1-1908504
3GPP TSG RAN WG1 Meeting #98
Prague, CZ, August 26th–30th, 2019
Agenda item: 7.2.8.5

## Slide 2: Motivation (1/3)
TBS determination of UE
  When UE receives a codeword, it determines the TB size from
    The number of REs,
    Code rate R and modulation order
    Number of layers
LDPC base graph (BG) determination
  From the code rate and the determined TB size, BG is determined as follows.
Quantization
(to get proper granularity)
Find the closest value
not smaller than

## Slide 3: Motivation (2/3)
TBS / LDPC BG determination in HARQ
  In HARQ, BG and TBS should be the same for the initial- and re-transmission.
    In TS 38.212 section 7.2.2,
    For retransmission, MCS indices 29-31 are used in MCS table 1 and 3, indices 28-31 are used in MCS table 2
      Those MCSs indicate modulation order only.
      Target code rate information is not needed since the UE already knows the TBS.
Encoded LDPC CW
Systematic bit (TB+CRC)
Parity bit
Initial Tx
1st ReTx
Tx
Rx
Initial Tx
1st ReTx
Same LDPC BG ensured for initial and re-transmission

## Slide 4: Motivation (3/3)
TBS / LDPC BG determination for URLLC NC-JT
  For scheme 3 and 4, it is agreed to have the same TBS and LDPC BG across repetition.
  The same principle should be applied for scheme 2b
    In scheme 2b, multiple TRPs repeatedly transmit the same TB in different frequency domain, possibly with different rate matching pattern, # of RBs, MCS, …
    If each TRP transmits with independent codeword and UE determines its TBS and LDPC BG independently, misalignment of TBS and LDPC BG may occur at the UE.
    If the TBSs of codewords are misaligned, UE does not know which TBS is correct
      Needs blind decoding, and consequently longer latency, to find the correct TBS.
    If the LDPC BGs of codewords are misaligned, it is hard to achieve the combining gain of codewords since they are determined as ‘different codes’.
PRB 0
PRB 1
PRB 2
PRB 3
PRB 4
PRB 5
PRB 6
PRB 7
TRP 1
TRP 2
Rate matched
CW1
CW2
For 1 layer transmission,
same MCS with 16QAM, target code rate 0.33
* TBS from TRP1 = 768
* TBS from TRP2 = 576
TBS misalignment

## Slide 5: Proposals
Proposal. In multi-TRP URLLC scheme 2b, it needs to be ensured for a UE to determine the same TBS and same LDPC BG for each repetition.