## Slide 1: Proposal on UE capability dynamicPowerSharing
Intel Corporation
RP-1909720
3GPP TSG-RAN WG1 #98
Prague, CZ, August 26th – 39th 2019
AI: 7.1.6

## Slide 2: Background
Further offline discussion with R1-1909129 (On UE capability tdm-Pattern and dynamicPowerSharing, Intel) proposing update parameter definitions in TS38.306 for tdm-Pattern and dynamicPowerSharing
Discussion points
  On tdm-Pattern
    No need to change since the definition can be covered by TS38.213
  On dynamicPowerSharing
    Clarify the definition to align with the original agreement (from “it will dynamically share the power between NR and LTE if” to “the UE can perform power scaling in”)
    Delete “PLTE + PNR > PCMAX”

## Slide 3: Proposal
Send an LS to RAN2 to update TS38.306 on UE capability parameter dynamicPowerSharing as following:
dynamicPowerSharing
Indicates whether the UE supports dynamic EN-DC power sharing between NR FR1 carriers and the LTE carriers or not, wherein the UE behaviour is specified in clause 7.6 of TS 38.213 [11]. If the UE supports this capability, the UE can perform power scaling it will dynamically share the power between NR FR1 and LTE if PLTE + PNR > PCMAX, as specified in TS 38.213 [11].