## Slide 1: On center frequency and initial BWP
3GPP TSG RAN WG1 Meeting #98
Prague, Czech Republic, August 26-30, 2019
Agenda Item: 7.1.3
R1-1909896
Huawei, HiSilicon

## Slide 2
For unpaired spectrum, the center frequencies of CORESET#0 and the initial DL/UL BWP configured by SIB1 can be the same or different.
  This does not change the following RAN1 agreement
Agreements in RAN1#94:
For PCell, the initial DL BWP can be configured in SIB1 to be the same as or different with the initial DL BWP as initially defined by CORESET#0
  The initial DL BWP configured in SIB1 includes the bandwidth of CORESET#0
  If the initial DL BWP configured by SIB1 is different with the initial DL BWP as initially defined by CORESET#0, the configuration of the initial DL BWP configured by SIB1 is applicable after the initial access
Proposed conclusion

## Slide 3: From RAN1 point of view, there is no intention/conclusion to change the following RAN1 agreements
Agreements:
For PCell, the initial DL BWP can be configured in SIB1 to be the same as or different with the initial DL BWP as initially defined by CORESET#0
  The initial DL BWP configured in SIB1 includes the bandwidth of CORESET#0
  If the initial DL BWP configured by SIB1 is different with the initial DL BWP as initially defined by CORESET#0, the configuration of the initial DL BWP configured by SIB1 is applicable after the initial access
RAN1 views

## Slide 4: Based on the approved CR in R2-1908285 (cover page copied next page), RAN1 understands that RAN2 has also no intention to change the intended UE behavior that CORESET#0 is active BWP used during initial access procedure until after msg4. - otherwise, there is NBC issue for both RAN1 and RAN2
RAN1 views

## Slide 5
Reason for change: | It is not clear what frequency reference the UE should apply for commonControlResourceSet configured in SIB1. In particular, since the initial DL BWP in SIB1 is only applicable after msg4, the UE may use Coreset#0 BWP in selecting the frequency reference according to frequencyDomainResources. It should be clarified that the UE uses the initial DL BWP after reading SIB1 even though this BWP is not applied immediately.
Summary of change: | Clarify that the the UE applies locationAndBandwidth of initial downlink BWP in SIB1 as frequency reference for commonControlResourceSet but keeps the bandwidth of CORESET#0 until after the reception of msg4. Impact Analysis: Impacted 5G architecture options: Standalone Impacted functionality: Configuration of Initial Downlink BWP Interoperability issue: if the network is implemented according to the CR and the UE is not: the UE may apply the wrong reference point and monitor the wrong coreset. if the UE is implemented according to the CR and the network is not: the UE may apply the wrong reference point and monitor the wrong coreset.
Consequences if not approved: | The UE may not apply the correct frequency reference for commonControlResourceSet configured in SIB1.
For information

## Slide 6
DownlinkConfigCommonSIB field descriptions
initialDownlinkBWP The initial downlink BWP configuration for a SpCell (PCell of MCG or SCG). The network configures the locationAndBandwidth so that the initial downlink BWP contains the entire CORESET#0 of this serving cell in the frequency domain. The UE applies the locationAndBandwidth upon reception of this field (e.g. to determine the frequency position of signals described in relation to this locationAndBandwidth) but it may keep the bandwidth of CORESET#0 until after reception of RRCSetup/RRCResume/RRCReestablishment.
TS 38.331
For information