## Slide 1: WF on RACH preamble format
Samsung, ZTE, Ericsson
3GPP TSG RAN WG1 adhoc
Spokane, Washington, USA, 16th – 20th January 2017
Agenda item: 5.1.1.4.1

## Slide 2: Background
Agreements at RAN1#87:
Following options can be further considered for the consecutive multiple/repeated RACH preambles,
  Option 1: CP is inserted at the beginning of the consecutive multiple/repeated RACH sequences, CP/GT between RACH sequences is omitted and GT is reserved at the end of the consecutive multiple/repeated RACH sequences
  Option 2: The same RACH sequences with CP is used and GT is reserved at the end of the consecutive multiple/repeated RACH sequences
  Option 3: The same RACH sequences with CP/GT is used
  Option 4: Different RACH sequences with CP is used and GT is reserved at the end of the consecutive multiple/repeated RACH sequences
  Option 5: Different RACH sequences with CP/GT is used
  For options 2 and 3, study further that the same RACH sequences with and without GT can be further multiplied with different orthogonal cover codes and transmitted.
  For example, the consecutive multiple/repeated RACH preambles would be used when Tx/Rx beam correspondence does not hold at TRP
  Other options are not precluded
For a single RACH preamble transmission, CP/GT are required
  For example, the single RACH preamble would be used when Tx/Rx beam correspondence held at both TRP or UE for multi-beam operation

## Slide 3
Agreements at RAN1#87:
  The maximum bandwidth for a RACH preamble transmission is not wider than 5 MHz for a carrier frequency of below 6 GHz and not wider than X MHz for a carrier frequency ranging from 6 GHz to 52.6 GHz
    X will be down selected from 5, 10, and 20MHz
  At least, one reference numerology for RACH preamble is defined,
    1.25 x n kHz
    15 x n kHz
      Integer value of n is FFS
    Other values are not precluded
  Based on the reference numerology for RACH preamble, multiple RACH preambles with scalable numerologies are supported depending on the carrier frequency

## Slide 4: Background
A random access preamble format in LTE
  Consist of CP + one or multiple preamble sequence + GT
Preamble transmissions depending on beam correspondence
  For the case that TRP has beam correspondence
    Single transmission should be configured (CP + SEQ + GT)
  For the case that TRP doesn’t have beam correspondence
    Preamble format consisting of repeated preamble sequences should be configured
Note : above two formats don’t happen simultaneously in a cell

## Slide 5: Proposal
For multi-beam operation (# of SS blocks in a burst set >1),
  For multiple/repeated RACH preamble transmissions, consider only option 1 and option 2
  At least one subcarrier spacing value for RACH is the same as the subcarrier spacing value for NR-PUSCH/NR-PUCCH.
For single-beam operation (# of SS blocks in a burst set = 1),
  FFS : Whether to support common or different formats from the multi-beam operation