## Slide 1: WF on LDPC Design for NR
3GPP TSG RAN WG1 Meeting NR Ad hoc
Spokane, USA ,16th - 20th January 2017
Agenda item 5.1.5.1
R1-1701264
Samsung, …

## Slide 2: Background
In RAN1 #85, there was the following agreement on LDPC codes
  For the purpose of study and comparisons, quasi-cyclic like LDPC codes are defined as follows:
    The Parity check matrix of Quasi-cyclic like LDPC Codes is defined at least by a matrix H of size (mb×z)×(nb×z), which consists of sub-block matrices of size z×z, where each sub-block matrix is composed by circularly shifted matrices or zero matrices. Wherein, mb, nb and z are integers larger than 1.
* Parity check matrix consisting of zxz circulant matrices or zero matrices
z1 < z2 < z3

## Slide 3: Background
In RAN1 #87, there was the following agreement on LDPC codes
  Code extension of a parity-check matrix is used for IR HARQ/rate-matching support
    Use lower-triangular extension, which includes diagonal-extension as a special case
  For the QC-LDPC design, the non-zero sub-blocks have circulant weight <=2
    Circulant weight is the number of superimposed circularly shifted ZZ identity matrices
  In parity check matrix design, the highest code rate (Rmax,j ) to design j-th H matrix for is
    Rmax,j <=8/9
    Rmax,j is the code rate of the j-th H matrix before code extension is applied (0 j< J)
    Rmax,j is the code rate after accounting for the built-in puncturing, if this is applied in H matrix design
  Rate matching to support transmission code rate higher than Rmax,j is not precluded

## Slide 4: Definition and Notation
Base parity check matrix
  The parity check matrix which consists of sub-block matrices of size 1×1
Circularly shifted matrix ( )
  The circulant permutation matrix which shifts the identity matrix to the right by times for any integer , .
Shift value
  Exponent value of the circularly shifted matrix
Row-orthogonal structure
  There is no overlapped circularly shifted matrix among the two or more row blocks
Layer
  One or more row blocks which consists of non overlapped circularly shifted matrix

## Slide 5: Proposal 1: Parity Check Matrix Structure
The parity check matrix consist five sub-matrices (A, B, C, D, E)
  C: Zero matrix
  D: Row orthogonal structured matrix (maximum number of layer ≤ [X] )
  E: Identity matrix
Number of base matrices (=NBM)
  NBM ≤ 2
A
C
D
E
B

## Slide 6: Proposal 2: Parity Check Matrix Size
Working assumption:
  max Z = 256 or 512
  min Z = 2

## Slide 7: Proposal 3: Z and Shift values
Z granularity
  Alt 1: Z finer granularity
    1:1:Zmax
  Alt 2: Z coarse granularity
    {1: 1: 8, 8: 1: 16, 16: 2: 32, 32:4:64, 64:8:128, 128:16:256, 256:32:512 } ~ 10% ZP
    {2: 1: 8, 8: 2: 16, 16: 4: 32, 32:8:64, 64:16:128, 128:32:256, 256:64:512} ~20% ZP
    Or Y ~20% max zero-padding
Parity-check matrix for z1 is derived from PCM for z2 using function f
  pij(z1) = f(pij(z2),z1,z2)
    E.g., f = flooring, modulo, offset, combination

## Slide 8: Proposal 4: Evaluation method
Firstly, set up the basic parameters to cover the complexity issue
  PCM size (nb, kb)
  Max. Num layers (or Max. required clock cycles per iteration)
  Max. Z sizes
  Max. nonzero entries
  Lowest rate
  Max. CBS
  …
Performance evaluation
  Set the submission deadline
  Performance comparison at CBLER = 1e-2 and 1e-5 [(or at least lower than 1e-4)]
  New performance evaluation conditions should be defined, e.g. finer granularity