## Slide 1: WF on Polar Coding Design
Huawei, HiSilicon, CATT, CATR, Coherentlogix, Mediatek, ZTE, ZTE Microelectronics
R1-1701301
3GPP TSG-RAN WG1 AH
Spokane, USA, 16th – 20th January 2017
Agenda item 5.1.5.2.1

## Slide 2: Background
RAN1#87 agreement:
  UL control information for eMBB
    Adopt Polar Coding (except FFS for very small block lengths where repetition/block coding may be preferred)
  DL control information for eMBB
    Working Assumption to adopt Polar Coding (except FFS for very small block lengths where repetition/block coding may be preferred)
      To be confirmed unless significant issues are identified by the RAN1 Jan ad-hoc in relation to performance, latency, power consumption and implementation complexity.
The polar code construction has to identify the location of certain bit types (information/frozen/[parity check]) through an ordered sequence S
The Polar code construction in this WF excludes very small block lengths (information block lengths less than K, K is FFS)

## Slide 3: Proposals
A single SNR-independent sequence S of size Nmax is used for polar construction
  Nmax is the maximum mother code length
  Nmax corresponds to the maximum codeword length for eMBB control coding
The sequence S has a nested structure
  For a given (K,R), the mother code length of size 2n, with
  n<=log2Nmax, uses 2n elements from S
The construction of S is FFS
Nmax is FFS