## Slide 1: WF on Paging
Huawei, HiSilicon, Samsung, CATT, Panasonic, NTT DOCOMO, Fujitsu
3GPP TSG RAN WG1 Meeting Ad Hoc for NR | R1-171xxxx
Spokane, USA, 16 – 20 Jan 2017 | Agenda Item: 5.1.1.3

## Slide 2: Proposal
Companies are encouraged to compare the following options for channel design for paging, taking the necessity of beam sweeping into consideration
  Opt-1: Paging message is scheduled by DCI carried by NR-PDCCH and is transmitted over PCH carried by NR-PDSCH
  Opt-2: Paging message is transmitted in a non-scheduled physical channel indicated by NR-PBCH
  Opt-3: Paging message is transmitted over PCH carried by NR-PDSCH without DCI. The resource is semi-statically configured.
Companies are encouraged to provide their views on
  Definitions of paging occasion and paging periodicity
  Content and payload of paging message
RAN1 sends a LS to RAN2, asking about
  Paging payload and capacity requirement