## Slide 1: WF on beam indication
Samsung, Ericsson, KT
R1-171320
3GPP TSG RAN WG1 Meeting #87
Spokane, USA, 16th - 20th Jan 2017
Agenda item 5.1.2.2

## Slide 2: Background
Working assumptions:
  Beam management procedures can utilize at least the following RS type(s):
    RS defined for mobility purpose at least in connected mode
      FFS: RS can be NR-SS or CSI-RS or newly designed RS
        Others are not precluded
    CSI-RS:
      CSI-RS is UE-specifically configured
        Multiple UE may be configured with the same CSI-RS
      The signal structure for CSI-RS can be specifically optimized for the particular procedure
      Note: CSI-RS can also be used for CSI acquisition
  Other RS could also be considered for beam management such as DMRS and synchronization signals

## Slide 3: Background
Agreements:
For downlink, NR supports beam management with and without beam-related indication
  When beam-related indication is provided, information pertaining to UE-side beamforming/receiving procedure used for data reception can be indicated through QCL to UE
    FFS: Information other than QCL
  FFS: When beam-related indication is provided, information pertaining to the Tx beam used for data transmission is indicated to UE
For downlink, based on RS (used for beam management) transmitted by TRP, UE reports information associated with N selected Tx beams
  Study how the N Tx beams can be selected
  Study the case where N comprises of all Tx beams
  Study UE reporting information
  Note: N can be equal to 1

## Slide 4: Proposal 1
For reception of DL control channel, support spatial QCL assumption between an RS antenna port(s), and DMRS antenna port(s) of DL control channel for assisting UE-side Rx beamforming
  FFS: The information indicating the RS antenna port(s) is indicated via DCI or MAC-CE or RRC, and will be assumed until the next indication.

## Slide 5: Proposal 2
For reception of DL data channel, support spatial QCL assumption between RS antenna port(s) of a time unit and DMRS antenna port(s) of DL data channel for assisting UE-side Rx beamforming
  Here the RS can be CSI-RS and/or MRS according to working assumption
  Option 1: Information indicating the RS antenna port(s) is indicated via DCI
    FFS: whether the information indicating the RS antenna port(s) will be assumed only for the scheduled “PDSCH” or until the next indication
  Option 2: Information indicating the RS antenna port(s) is indicated via MAC-CE, and will be assumed until the next indication
  At least one option is supported
    FFS: whether to support either or both options
  FFS: whether the information indicating the RS antenna port(s) for DMRS ports for DL control channel also applies to DMRS ports for DL data channel