## Slide 1
3GPP TSG RAN WG1 NR Ad Hoc Meeting R1-1701352
Spokane, USA, 16th - 20th January 2017
Agenda item: 5.1.2.2
WF on codebook design for
DL multi-panel MIMO
Huawei, HiSilicon, …

## Slide 2: Background
The following agreements are achieved in RAN#87:
Agreements:
For Type I CSI, PMI codebook has at least two stages W = W1W2
  W1 codebook comprises of beam groups/vectors
  FFS structure and configuration of W1 codebook, e.g. number of ports, grid of beams, orthogonal, non-orthogonal, beam broadening, etc
  FFS frequency granularity of W1 and W2 reporting
  FFS on additional support of W3 (location of W3 matrix is FFS), e.g. multi-panel support, analog beam selection
  Note multi-panel support may be captured in W1, W2 and/or W3
Agreements:
Consider the impact of the antenna panel array
  Study the impact of antenna panel array in NR CSI feedback design.
Note: Different antenna panel may or may not be from same TRP.

## Slide 3: Proposals
  For Type I CSI feedback, NR should support multi-panel codebook as the baseline
    If 3-stage multi-panel codebook is supported , FFS which codebook structure is supported, e.g., W1W2W3, W1W3W2 or W3W1W2.
    FFS whether W3 could be considered as a part of W1 and W2 or an independent decoupled codebook
    FFS whether more configurable codebook stages could be supported
    Single panel codebook can be a special case of multi-panel codebook, e.g., Mg=1, Ng=1.
  At least the phase factor across the panels is supported in codebook W3
    FFS the frequency and time granularity of W3 reporting, e.g., wideband or subband/long term or short term
    FFS whether other factors are supported in the codebook, e.g., amplitude factors, beam selection or analog beam selection, etc.
    FFS configurable parameters related to multi-panel codebook, e.g. number of panels, quantization bits for phase factor, etc.