## Slide 1: WF on Multiple RAR
Samsung, ZTE, ZTE Microelectronics, NTT DOCOMO
R1-1701366
3GPP TSG RAN WG1 Meeting #NR Adhoc
Spokane, USA, 16th - 20th January 2017
Agenda item 5.1.1.4.2

## Slide 2: Background (1/3)
2 UE determine the same DL Tx beam as the best one. But the UL Rx beams may be different as shown
One option is that the gNB just sends one RAR, thus another UE will fail.
Another option is that the gNB will transmit two RARs

## Slide 3: Background (2/3)
Both TRP1 and TRP2 receive the same MSG1, but there is not enough time to coordinate the response. Therefore, both TRPs transmit a response each.
UE transmits a second MSG1 before the response to the first MSG1 is received.

## Slide 4: Background (3/3)
Each preamble is received independently by the gNB and has its associated Random Access Response.
To assist the UE in determining which beam to use, in case it receives more than one RAR, the gNB measures the quality of the RACH preamble signal and feedbacks this information to the UE in the RAR.
  The UE uses the beam associated with the RAR that has the best signal quality metric for subsequent transmissions

## Slide 5: Proposal
NR considers multiple RAR reception at the UE.
FFS: 1 or multiple Msg3 from UE