## Slide 1: WF on NR-PBCH Contents
Samsung, NTT DOCOMO, CATT, Convida Wireless, Sony, ITL, InterDigital, [Qualcomm], [LGE], [Intel], …
3GPP TSG RAN WG1 NR_AH Meeting
Spokane, USA, 16th –20th January 2017
Agenda: 5.1.1.2
R1-1701372

## Slide 2: Background
In RAN1#87, we have agreements on PBCH
  Agreements:
    Consider followings for minimum system information transmission:
      NR-PBCH is a non-scheduled broadcast channel carrying at least a part of minimum system information with fixed payload size and periodicity predefined in the specification depending on carrier frequency range
        Alt. 1: NR-PBCH carries a part of minimum system information
          Alt 1-1 : remaining minimum system information is transmitted via other channel at least partially indicated by NR-PBCH
          Alt 1-2: Remaining minimum system information is transmitted via other channel not indicated in NR-PBCH
        Alt. 2: NR-PBCH carries all of minimum system information
  Agreements:
    For study of the cases where NR-PBCH carries a part of minimum system information, consider the following alternatives (or combinations) for the minimum system information other than those included in NR-PBCH :
      Alt. 1: NR defines the additional channel as secondary broadcast channel
        Secondary broadcast channel may be different design from NR-PBCH, e.g. payload size, resource mapping, periodicity and etc.
        FFS on transmission: beam-specific, cell-specific, and/or TRP-specific, etc.
      Alt. 2: The remaining information is transmitted in shared downlink channel similar to ,e.g. NR-PDSCH
        FFS on transmission: UE-specific, UE group-specific, beam-specific, cell-specific, and/or TRP-specific, etc.
    Note: This does not preclude defining of other mechanisms transmitting Other SI

## Slide 3: Proposal
NR-PBCH carries a part of minimum system information (Alt1)
  Remaining minimum system information is transmitted via other channel at least partially indicated by NR-PBCH (Alt1-1)
  Remaining minimum system information is included in
      Alt-a: PDSCH
      Alt-b: Secondary broadcast channel
NR-PBCH contents shall at least include
  SFN (system frame number)
    FFS on the indication number of SFN
  Configuration for
    Control resource set in case of Alt-a
    Secondary broadcast channel in case of Alt-b
    FFS on other parameters
  CRC
    FFS: 16 bits