## Slide 1
3GPP TSG RAN WG1 NR AdHoc #1 R1-1701380
Spokane, USA
January 16th-20th, 2017
Agenda item: 5.1.2.1
WF on CW to layer mapping and RE mapping for data channels
Qualcomm, Ericsson, Intel, Interdigital, …

## Slide 2: Background
Mapping to physical resources:
  Due to early-decoding-constraints layer mapping over frequency should be prioritized over time.
  Mapping across layers of each codeblock provides spatial diversity
Codeword to layer mapping:
  Subcarrier interleaver
    NR shall support large bandwidth allocations.
    CBs span limited frequency bandwidth and additional frequency diversity can be exploited to provide significant gains
      Each OFDM symbol may carry many CBs, especially in regimes of medium and high spectral efficiency

## Slide 3: Proposals
For the DL/UL data channels, layer mapping to physical resources is happening across layer first, then across subcarriers and then across OFDM symbols.
For the DL/UL data channels, RAN1 to study the option of introducing a per-OFDM-symbol subcarrier interleaver in the codeword to layer mapping procedure.