## Slide 1
3GPP TSG RAN WG1 NR Ad Hoc Meeting R1-1701403
Spokane, USA, 16th - 20th January 2017
Agenda item: 5.1.2.2
WF on codebook design for
DL multi-panel MIMO
Huawei, HiSilicon, Intel

## Slide 2: Background
The following agreements are achieved in RAN#87:
Agreements:
For Type I CSI, PMI codebook has at least two stages W = W1W2
  W1 codebook comprises of beam groups/vectors
  FFS structure and configuration of W1 codebook, e.g. number of ports, grid of beams, orthogonal, non-orthogonal, beam broadening, etc
  FFS frequency granularity of W1 and W2 reporting
  FFS on additional support of W3 (location of W3 matrix is FFS), e.g. multi-panel support, analog beam selection
  Note multi-panel support may be captured in W1, W2 and/or W3
Agreements:
Consider the impact of the antenna panel array
  Study the impact of antenna panel array in NR CSI feedback design.
Note: Different antenna panel may or may not be from same TRP.

## Slide 3: Proposals
  For Type I CSI feedback, NR should support multi-panel codebook as the baseline
    At least the phase factor across the panels is supported in codebook W3
    FFS which codebook structure is supported, e.g., W1W2W3, W1W3W2 or W3W1W2.
    FFS the frequency and time granularity of W3 reporting, e.g., wideband or subband/long term or short term
    FFS whether other factors are supported in the codebook, e.g., amplitude factors, beam selection or analog beam selection, etc.
    Support configurable codebook stages
    Single panel codebook can be a special case of multi-panel codebook, e.g., Mg=1, Ng=1.
    FFS configurable parameters related to multi-panel codebook, e.g. number of panels, quantization bits for phase factor, etc.