## Slide 1: WF on NR-PDCCH design for URLLC
Huawei, HiSilicon, CATR, Sony, Samsung, Ericsson, Qualcomm, ZTE, ZTE Microelectronics…
3GPP TSG RAN WG1 NR-Adhoc Meeting R1-1701405
Spokane, Washington, January 16 - 20, 2017
Agenda item: 5.1.3.4

## Slide 2: Background
The ongoing discussion on NR-PDCCH design has not taken URLLC specific aspects into account yet
In general, NR-PDCCH for URLLC have higher reliability requirement than NR-PDCCH for eMBB.
  Even with one retransmission, the 99.999% reliability requirement can never be met if the associated control channel carrying DL assignment is operated at 1% miss detection probability.

## Slide 3: Proposal
To ensure the reliability requirement of NR-PDCCH for URLLC, at least the following aspects should be supported
  Defining a compact DCI format targeting low BLER operation
  The highest aggregation level should target a BLER of Y for this compact DCI format
    FFS Y, Y<1%
    FFS highest aggregation levels, e.g., 16,32
  FFS other enhancements