## Slide 1
3GPP TSG RAN WG1 NR Ad-Hoc Meeting R1-1701461 Spokane, USA, 16th - 20th January 2017
Agenda item: 5.1.2.3.2
WF on Observation of DL DMRS Evaluation
Huawei, HiSilicon, MediaTek Inc.,
Mitsubishi Electric, vivo, CATT, Xinwei, Ericsson, AT&T, CMCC

## Slide 2: Proposals
Preliminary observations on DL DM-RS performance based on the evaluation results provided in this meeting
  For relatively high speed scenarios, additional DMRS in time domain can provide robust performance. (R1-1700068, R1-1700137, R1-1700482, R1-1700578, R1-1700606, R1-1700807, R1-1700875, R1-1701104).
  Performance gain can be obtained with up to 16 orthogonal DMRS ports for MU-MIMO compared to 8 orthogonal DMRS ports (R1-1700068) or 16 quasi-orthogonal DMRS ports (R1-1700068, R1-1700875)
  The optimal frequency density for different deployment varies. ( R1-1700807, R1-1700780, R1-1700931)
Companies are encouraged to provide additional evaluation results in next meeting.
The performance evaluation observations should be considered in DMRS design.

## Slide 3: Observations
HW | 1, For high UE speed, e.g., more than 60km/h, pattern with time density 1 cannot converge due to high Doppler shifts. 2, The pattern with time density 3 performs better than that with density 2 or 1 in terms of BLER, but only little performance gain can be observed by increasing time density 2 to 3. 3, For scenarios with low Doppler shift (e.g., UE speed <=30 km/h with frequency 4G Hz and numerology 15kHz), basic/front-loaded pattern has higher throughput because of low overhead 4, For scenarios with medium to high Doppler shift (e.g., UE speed >30 km/h with frequency 4G Hz and numerology 15kHz), DMRS pattern with higher time density starts to provide higher throughput because of higher accuracy of channel estimation, where the desity-2 seems a good trade-off between RS overhead and performance. | R1-1700068
ZTE | The proposed additional DMRS set provides good performance for high speed scenarios. | R1-1700137
LGE | Additional RS in time domain provides robust performance against high delay spread. | R1-1700482
Time density(high speed)

## Slide 4: Observations
ETRI | 1: In the high speed scenario with UE speed of 500 km/h, dense DMRS allocation (more than 4 DMRSs within a slot) in the time domain shows lower BLER. 2: In the high speed scenario, reduced DMRS allocation does not significantly degrade BLER. 3: In the high speed scenario, reducing DMRS density can be advantageous in enhancing spectral efficiency. | R1-170057 8
Time density(high speed)
DOCOMO | When UE speed becomes larger, the BLER performance degradation is occurred. | R1-1700606
Qualcomm | 1, For low Doppler and low delay spread scenarios, performance is largely impacted by DMRS overhead, with proposed schemes having same overhead have similar performance. 2,Time-domain staggering of the DMRS ports (i.e., applying comb-offsets in multi-symbol DMRS patterns) may provide gains in some medium/high mobility scenarios. | R1-1700807

## Slide 5: Observations
Mitsubishi | In the 30GHz high speed train scenario, when AFC is used, DMRS placed across two symbols yield satisfactory performance | R1-1700875
Nokia | The performance for high speed scenarios is significantly better with the pattern including front-loaded DMRS + PT-RS + additional DMRS | R1-1701104
Time density(high speed)
MTK | Even for the low speed scenario, the 3-set DMRS patterns can still outperform 2-set DMRS patterns in many cases. It is also not practical for the network to allocate different DMRS patterns due to the change of the channel condition. | R1-1700175

## Slide 6: Observations
Xinwei | From above results, it could be seen that for different deployment, the optimal density is different. | R1-1700780
Qualcomm | Supporting a non-uniform DMRS pattern in the frequency domain does not provide gains that justify its adoption in NR. | R1-1700807
Samsung | Rank-1 DMRS RE density should be determined considering robust DMRS performance in low SNR region | R1-1700931
Frequency density

## Slide 7: Observations
HW | Compared to 8 orthogonal DMRS ports, more than 35% mean UPT gain can be obtained with up to 16 orthogonal DMRS ports in MU-MIMO. | R1-1700068
Mitsubishi | 16 orthogonal DMRS ports provide overall and UE-level spectral efficiency gain. | R1-1700875
orthogonal port num