## Slide 1: WF on Shortening of LDPC Codes
Ericsson, Qualcomm, LG, Intel, Nokia, ASB, Samsung
R1-1701464
3GPP TSG RAN WG1 Meeting NR Ad hoc
Spokane, USA ,16th - 20th January 2017
Agenda item 5.1.5.1

## Slide 2: Background
Agreement (RAN1#87):
  UL eMBB data channels:
    Working Assumption to adopt flexible LDPC as the single channel coding scheme for small block sizes (to be confirmed unless significant issues are identified by the RAN1 Jan adhoc in relation to performance, implementation complexity and flexibility)
    (Note that it is already agreed to adopt LDPC for large block sizes)
  DL eMBB data channels:
    Adopt flexible LDPC as the single channel coding scheme for all block sizes
Agreement (RAN1#86):
  Channel coding techniques for NR, should support the following:
    Info block size K flexibility:
      Granularity at lower end of range of K = [D1] bits
        D1 may be different for control and data channels
        FFS whether D1 may be different for different code rates
      FFS whether the granularity is coarser at higher values of K
      Shortening (i.e. assigning info bits to known values, e.g. 0) may be used to provide info block size flexibility

## Slide 3: Proposal: Shortening
Shortening is applied before LDPC encoding when necessary
  Filler bits F are attached at the end of info block B to form vector U = [B F]
  Vector U is the input to LDPC encoding
  The filler bits F are not transmitted