## Slide 1: WF on SCL List Size for Polar Codes
Ericsson, Nokia, ASB, LG , Samsung
R1-1701468
3GPP TSG RAN WG1 Meeting NR Ad hoc
Spokane, USA ,16th - 20th January 2017
Agenda item 5.1.5.2

## Slide 2: Background
Agreement (RAN1#87):
UL control information for eMBB
  Adopt Polar Coding (except FFS for very small block lengths where repetition/block coding may be preferred)
DL control information for eMBB
  Working Assumption to adopt Polar Coding (except FFS for very small block lengths where repetition/block coding may be preferred)
    To be confirmed unless significant issues are identified by the RAN1 Jan adhoc in relation to performance, latency, power consumption and implementation complexity

## Slide 3: Background
Agreed Observation (RAN1#86bis, Lisbon)
Polar:
    For list decoders, the implementation complexity increases with increasing list size, especially with larger block sizes
      Some companies consider that a List 32 decoder is implementable up to a codeword size N of at least 1k (with larger codeword sizes requiring a segmented design), although some other companies have concerns on the achievable performance (including area efficiency, hardware throughput)
      Some companies consider that a List 8 decoder is implementable for codeword sizes N up to 4k (with larger codeword sizes requiring a segmented design)
      List 4 decoder is considered implementable for codeword sizes N up to at least 2k, with some companies considering it implementable up to 8k (with larger codeword sizes requiring a segmented design)
      List 1 is considered implementable

## Slide 4: Proposal
Successive cancellation list (SCL) decoding with List size L={1, 2, 4} are assumed in Polar code discussion and evaluation