## Slide 1: Way Forward on LDPC Comparisons
MediaTek, Huawei HiSilicon, CATT, CATR,
ZTE, LG, ITRI
R1-1701469
3GPP TSG-RAN WG1 NR_AH
Spokane, USA, 16th – 20th Jan 2017
Agenda item 5.1.5.1

## Slide 2: Background (1)
For block parallel decoders, block-by-block processing simplifies the implementation and provides high flexibility to decode any base matrix.
  Processing time is related to both edge number and the parallelism per block processing, Z <= Zmax
Higher T-put can also be achieved with multi-block-processing and proper coordination among the block processing threads
Example of a rate-2/3 base-matrix
  Edge number = 102, Z = 512, Lifted edge number = 52224
Notes: Zmax = 512, Zue = 256 256x2

## Slide 3: Background(2)
For a row-parallel decoder, layer-by-layer processing can realize very high parallelism and very high T-put.
For a given data amount and code rate, a base-matrix design with smaller layer number can realize shorter layer processing time and higher T-put for a row parallel decoder.
  A (quasi) layer includes neighbor rows which are (quasi) row orthogonal to each other.
    Quasi-row orthogonal is row-orthogonal expect for X% of information bit columns
    X = 15 and FFS the value for efficient decoder implementation
Example of another rate-2/3 base-matrix
  Layer number in the following base-matrix is only 9.

## Slide 4: Background (3)
Along the study item phase, the performance difference of different companies’ designs are getting smaller and smaller.
With similar performance, more factors that may benefit or impact the implementation should be considered.
In addition to performance, Zmax, edge number and/or (quasi) layer number should also be specified for understanding the implementation benefits/impacts.

## Slide 5: Proposal
NR eMBB LDPC comparison should provide
  BLER performance according to the latest version of the agreed assumptions
  Zmax of a compared base matrix
  Edge numbers and/or (quasi) layer numbers of a compared base matrix for the considered code rates
  FFS: Design parameter(s)/metric(s) useful for companies to check implementation benefit(s)/impact(s)