## Slide 1: WF on NR SS Periodicity
AT&T, NTT DOCOMO, Samsung, Sierra Wireless
3GPP TSG RAN WG1 Ad Hoc Meeting
Spokane, USA 16th –20th January 2017
Agenda: 5.1.1.1.3
R1-1701500

## Slide 2: Agreement from RAN1#87
From UE perspective, SS burst set transmission is periodic
  At least for initial cell selection, UE may assume a default periodicity of SS burst set transmission for a given carrier frequency
    Exact value of default periodicity of SS burst set transmission for a given carrier frequency needs to be studied
  FFS: UE in CONNECTED or IDLE mode may be provided with updated information regarding the SS burst set periodicity of serving cell and/or neighbor cells by the network
    FFS: Validity duration of information
    Note: Updated periodicity may be shorter or longer than default periodicity assumed by UE
    FFS: Note: This does not imply SS-burst set needs to be always on with the updated periodicity
    FFS: SS burst periodicity assumed by UE if information of neighbor cells is not available
    FFS: Consider idle mode operation performance
    Note: Companies can also consider to support functionality related to LTE DRS and LTE IDLE mode
  Companies are encouraged to investigate the tradeoff between network flexibility/power consumption and UE complexity/power consumption

## Slide 3: Background
A fixed SS burst set periodicity poses problems when considering forward-compatibility
Allowing a UE-specific or at least cell-specific configurability of at least the transmission period of the signals utilized for initial access is beneficial for NR and supports forward compatible introduction of new services with potentially different requirements.
NR should support functionality similar to the LTE DRS, with multiple UE-specific configurable SS burst periodicities defined which can be utilized by at least CONNECTED UEs and possibly IDLE UEs as well depending on the signalling mechanism.

## Slide 4: Proposal
RAN1 aims to select a default SS burst set periodicity for each agreed frequency range category from the following candidate values:
  For carrier frequency range #1 (below 6GHz): [5ms, 10ms, 20ms, 40ms, 80ms, 100ms]
  For carrier frequency range #2 (above 6GHz): [5ms, 10ms, 20ms, 40ms, 80ms, 100ms]
  Note that final set of frequency categories may include more than the above two categories
Companies are encouraged to investigate the candidate default SS burst set periodicity values considering at least the following factors:
  UE IDLE mode and initial cell search power consumption and latency
    Including single/multi-beam operation at Tx and Rx
  NW power consumption
  Inter-RAT/Inter-frequency measurement
  Forward compatibility and deployment flexibility including standalone and non-standalone NR deployments
  Benefits and feasibility of SS burst set configuration assistance signaling (e.g. periodicity indication or measurement window) for CONNECTED and/or IDLE UEs
  NW synchronization requirements/assumptions