## Slide 1: 3GPP TSG RAN WG1 AH_NR Meeting R1- 1701505 Spokane, USA 16th - 20th January 2017 Agenda item 5.1.3.4
WF on retransmission for UL URLLC
ZTE, ZTE Microelectronics, NTT Docomo,Huawei, Hisilicon,Intel,CATT , Nokia,ASB, Sony, CEWiT, IITH, IITM, Tejas Networks,Interdigital

## Slide 2: Background
Agreements:
At least an UL transmission scheme without grant is supported for URLLC
  Resource may or may not be shared among one or more users
    FFS: resource configuration details
  FFS other details of design

## Slide 3: Proposal
• For a UE monitoring UL grant and configured with grant free transmission, the following is supported:
  • If UL grant is received by the UE indicating a retransmission of a TB in a time-frequency resource, the UE uses grant based re-transmission for that TB in the time-frequency resource;
  • If UL grant is received by the UE indicating a new transmission of a TB in a time-frequency resource, the UE uses grant based transmission for that TB in the time-frequency resource;
  • If UL grant is not received by the UE, the UE follows the grant free procedures