## Slide 1: WF on Modulation for NR UL
MediaTek, IITH, CEWiT, IITM, Tejas Networks, NTU, Samsung, AT&T, Xiaomi
3GPP TSG RAN WG1 AH_NR Meeting R1-1701522
Spokane, USA, 16th – 20th January 2017
Agenda item: 5.1.6

## Slide 2: Background
Current Working Assumption
  NR supports 0.5*pi BPSK modulation for DFT-s-OFDM
    While using DFT-s-OFDM, 0.5*pi-BPSK modulation using DFT-S-OFDM with frequency domain spectrum shaping can be further considered at least for eMBB uplink data for up to 40GHz
    FFS
      The details of frequency domain spectrum shaping
      This does not preclude the case where no spectrum shaping is needed

## Slide 3: Background
Limitation of Rotated-QAM as a low PAPR design @ spectral efficiency > 0.5 bit/s/Hz
  In [1]&[2], it is shown that the without Frequency Domain Spectral Shaping (FDSS), MCL advantage of 0.5*pi-BPSK over QPSK vanishes as spectral efficiency increases.
  It is also shown in [1],[2], and [3] that Rotated-QPSK without FDSS does not provide MCL gain over conventional QPSK.
There are Designs that achieve high MCL gain @ spectral efficiency > 0.5 bit/s/Hz
  In [1], it is shown that even without FDSS, the interpolated-QPSK, a special case of low PAPR TCM design, provides MCL gain of 0.8dB across a wide spectrum of spectral efficiency, ranging from 0.25 bit/s/Hz to 1.25 bit/s/Hz.
  In [3], it is shown that with FDSS, significant PAPR reduction could be obtained with rotated-QPSK.
[1] R1-1700164, “Low PAPR Modulation Design,” MeidaTek Inc.
[2] R1-1701039, “Rotated modulations for DFT-S-OFDM uplink,” Nokia, Alcatel-Lucent Shanghai Bell.
[3] R1-1701000, “Performance evaluation results of DFT-s-OFDM with FDSS,” Samsung.

## Slide 4: Proposals
NR Support QPSK based low PAPR modulation for DFT-s-OFDM
  QPSK based low PAPR modulation includes, but not limited to:
    For example: Interpolated-QPSK, Rotated-QPSK, Trellis Coded MPSK
  While using DFT-s-OFDM, QPSK based low PAPR modulation using DFT-s-OFDM with frequency domain spectrum shaping (FDSS) can be further considered at least for eMBB uplink data for up to 40GHz.
  FFS
    The details of frequency domain spectrum shaping
    This does not preclude the case where no spectrum shaping is needed