## Slide 1: WF on NR-SS sequence design
NTT DOCOMO, ZTE, InterDigital
3GPP TSG RAN WG1 Meeting NR-adhoc#2 R1-1711654
Qingdao, China
27th – 30th June, 2017
Agenda item: 5.1.1.1.1
Document for decision

## Slide 2: Background
Agreements:
Confirm following working assumptions on NR-PSS as agreements
  Number of PSS sequences: 3
    PSS sequence details:
      Frequency domain-based pure BPSK M sequence (fixing the time/freq. offset ambiguity)
        1 polynomial: Decimal 145 (i.e. g(x) = x7 + x4 + 1)
        In freq. domain 3 cyclic shifts (0, 43, 86) to get the 3 PSS signals
        Initial poly shift register value: 1110110
Working assumption:
NR-SSS sequence design is 1 polynomial with 127 cyclic shifts, and 1 another polynomial with 9 cyclic shifts
    Two generator polynomials will be defined for m-sequences, and cyclic shift according to NR-cell ID is applied to each m-sequence
    Two polynomials are generated by g0(x) = x7 + x4 + 1 and g1(x) = x7 + x + 1
      Initial state is [0000001]
    The cyclic shift values and are jointly determined by the cell IDs carried by NR PSS (i.e., ) and NR SSS (i.e., )), where the cell ID is given by

## Slide 3: Proposal
Update agreements on NR-PSS with following change
  Number of PSS sequences: 3
    PSS sequence details:
      Frequency domain-based pure BPSK M sequence (fixing the time/freq. offset ambiguity)
        1 polynomial: Decimal 145 (i.e. g(x) = x7 + x4 + 1)
        In freq. domain 3 cyclic shifts (0, 43, 86) to get the 3 PSS signals
        Initial poly shift register value: x(0) = 0, x(1) = 1, x(2) = 1, x(3) = 0, x(4) = 1, x(5) = 1, x(6) = 1

## Slide 4: Proposal
Confirm working assumptions on NR-SSS with following changes
  NR-SSS sequence design is 1 polynomial with 127 cyclic shifts, and 1 another polynomial with 9 cyclic shifts
        Two generator polynomials will be defined for m-sequences, and cyclic shift according to NR-cell ID is applied to each m-sequence
        Two polynomials are generated by g0(x) = x7 + x4 + 1 and g1(x) = x7 + x + 1
            Initial poly shift register value: x(0) = 1, x(1) = 0, x(2) = 0, x(3) = 0, x(4) = 0, x(5) = 0, x(6) = 0
          The cyclic shift values and are jointly determined by the cell IDs carried by NR PSS (i.e., ) and NR SSS (i.e., )), where the cell ID is given by
            Option 1
            Option 2
              , where K > 1 (e.g., 5)
            Down-selection of above options will be done within this meeting

## Slide 5: Proposal
NR-SSS sequence is mapped to consecutive 127 subcarriers as well as NR-PSS
Frequency center of NR-PSS/SSS is aligned with frequency center of NR-PBCH
Update agreements on number of NR-SSS signals with following change
  Number of SSS signals: 1008 post-scrambling
    Note that number of NR physical cell IDs is 1008

## Slide 6: Appendix
NR-PSS/SSS sequences to resource mapping
and
(The value X depends on SS block composition.)