## Slide 1: Measurement window periodicity, duration and offset of CSI-RS for L3 mobility
3GPP TSG RAN WG1 89AH R1-1711864
Qingdao, China
27th – 30th June, 2017
Agenda item: 5.1.1.5.2
Document for Decision
Qualcomm,

## Slide 2: Background - I
Following agreement was made in one of the previous RAN1 meetings [1]
  For CONNECTED mode RRM measurement for L3 mobility based on CSI-RS, NR supports following targets for CSI-RS design and configuration:
  Design:
    Reuse CSI-RS design for beam management as baseline
    Identify additional requirements on the CSI-RS to support L3 mobility
  Configuration:
    Support measurement of a large number of beams
    Minimize configuration overhead, reporting overhead, and UE complexity
    FFS: Detailed signaling or format
1. Chairman's Notes RAN1_88b - final, 3GPP TSG RAN WG1 Meeting #88b, Spokane , USA, 3rd – 7th April 2017.

## Slide 3: Background - II
Following agreement has been agreed for L3 measurement based on SS block in this meeting [2]
  Regarding the SS block based RRM measurement timing configuration (SMTC) i.e., measurement window periodicity/duration/offset information for UE RRM measurement per frequency carrier,
    For intra-frequency CONNECTED mode measurement, up to two measurement window periodicities can be configured
      UE can be informed of which cell(s) is associated with which measurement window periodicity
      For cell(s) that is not listed, longer measurement window periodicity is used
    Single measurement window offset and duration are configured per frequency carrier
  For IDLE mode measurements, only single SMTC is configured per frequency carrier
  For inter-frequency CONNECTED mode measurements, only single SMTC is configured at least per frequency carrier
  RAN1 asks RAN4 if there is any concern for inter-frequency measurement based on single SMTC or multiple SMTCs across different frequency carriers
2. Chairman's Notes RAN1_89AH – v15, 3GPP TSG RAN WG1 Meeting #89AH, Qingdao , China, 27th – 30th June 2017.

## Slide 4: Background - III
Multiple measurement window periodicity, duration and offset lead to potential issues. [3]
  Impacts UE battery life since UE will have to wake and sleep multiple times to measure serving and neighbor cells
    CSI-RS has wider bandwidth than SSS and will lead to more power consumption
    Issue is more significant at over-6 GHz where UE may have to wake up more often to try different RX beams
  Impacts user rate due to scheduling limitations during each measurement window
3. R1-1711150, Measurement based on CSI-RS for L3 mobility consideration, RAN1 89AH

## Slide 5: Proposal
For the CSI-RS based RRM measurement timing configuration (i.e., measurement window periodicity/duration/offset information for UE RRM measurement), only a single measurement window periodicity, duration and offset are configured per frequency carrier
  This applies to both intra-frequency and inter-frequency measurements