## Slide 1: WF on PRACH for beam failure recovery request transmission
Huawei, HiSilicon, LG Electronics, Ericsson, CATT,NTT DOCOMO
3GPP TSG RAN WG1 Ad Hoc Meeting R1-1711928
Qingdao, China, 27 – 30 June 2017
Agenda item – 5.1.2.2.2

## Slide 2: Background
Agreements in RAN1#89 meeting:
Support the following channel(s) for beam failure recovery request transmission:
  Non-contention based channel based on PRACH, which uses a resource orthogonal to resources of other PRACH transmissions, at least for the FDM case
    FFS other ways of achieving orthogonality, e.g., CDM/TDM with other PRACH resources
    FFS whether or not have different sequence and/or format than those of PRACH for other purposes
    Note: this does not prevent PRACH design optimization attempt for beam failure recovery request transmission from other agenda item
    FFS: Retransmission behavior on this PRACH resource is similar to regular RACH procedure
  Support using PUCCH for beam failure recovery request transmission
    FFS whether PUCCH is with beam sweeping or not
    Note: this may or may not impact PUCCH design
  FFS Contention-based PRACH resources as supplement to contention-free beam failure recovery resources
    From traditional RACH resource pool
    4-step RACH procedure is used
    Note: contention-based PRACH resources is used e.g., if a new candidate beam does not have resources for contention-free PRACH-like transmission
  FFS whether a UE is semi-statically configured to use one of them or both, if both, whether or not support dynamic selection of one of the channel(s) by a UE if the UE is configured with both

## Slide 3: Proposal
For beam failure recovery request transmission on PRACH, support using the resource that is CDM with other PRACH resources.