## Slide 1: Summary of Offline Discussions on Single Tx Enhancement
3GPP TSG-RAN WG1 Ad-Hoc 1901 R1-1901424 Taipei, Taiwan, 21st – 25th January, 2019

## Slide 2: Background: RAN4 Decision
Rel-15 Operation – Static, Based on UE SUO capability |  | 
 | 1PA | 2PA
Single Uplink Operation | UE would signal SUO support for the EN-DC band combination. UE expects RAN to schedule Single Tx. | UE could optionally signal SUO support, and would be scheduled for Single Tx.
Simultaneous Dual Tx | UE could potentially not signal SUO support, but would be required to operate with A-MPR defined for 2PA. | A-MPR to be defined for this case.
In RAN4 #86bis, following receiver architecture (R4-1805774) has been agreed EN-DC operation in B41

## Slide 3: Background: Plenary Decision
In RAN #81, following was agreed in the “R16 MR-DC and CA enhancement” WID(RP-182076)
  Study and, if found beneficial over the existing single Tx switched uplink solution, specify enhancements to single Tx switched uplink solution for EN-DC, such as allowing all DL and UL subframes for data transmission for both NR and LTE. [RAN1].
  Note: UE in single Tx switched uplink mode is not expected to be scheduled simultaneous transmission on MCG and SCG

## Slide 4: Background: Existing single Tx solution for TDD intra-band EN-DC
Example assuming LTE TDD Pattern 2
Existing solution: Loss of 1 LTE UL subframe leads to loss of 4 LTE DL subframes
Proposal: Still use all LTE DL subframes even with Loss of 1 LTE UL subframe

## Slide 5: Potential conclusion from Offline Discussion
Compared to the existing UE-transparent single-Tx operation agreed in R15 (i.e. case 2 HARQ timing) for EN-DC with LTE TDD Pcell, there is benefit in terms of allowing all DL subframes for LTE data transmission by configuring the UE with DL-reference UL/DL configuration and apply the associated DL HARQ timing (i.e. case 1 HARQ timing).

## Slide 6: Proposal: enhancement to TDD Pcell case
For single UL operation in EN-DC with LTE TDD PCell, where UE operates on only one carrier at a time
for LTE carrier, UE can be configured with DL-reference UL/DL configuration indicated by RRC signaling “tdm-PatternConfig-r15”
  For DL HARQ timing, the DL-reference UL/DL configuration, i.e. associated with “tdm-PatternConfig-r15”, is applied
  For UL HARQ timing, the PCell’s UL/DL configuration, i.e. associated “subframeAssignment”, is applied
  For UE capable of dynamic power sharing, LTE UL transmission can be scheduled in all UL subframes and UpPTS configured by “subframeAssignment”
    UE is not expected to transmit on the MCG and SCG simultaneously
  For UE not capable of dynamic power sharing, LTE UL transmission is only expected to be scheduled in UL subframes and UpPTS allowed according to the DL-reference UL/DL configuration.

## Slide 7: Proposal: enhancements to FDD Pcell case (Not discussed)
For single UL operation in EN-DC with LTE FDD Pcell configured with case 1 HARQ timing
For UE capable of dynamic power sharing, LTE UL transmission can be scheduled in all UL subframes.

## Slide 8: Proposal: PRACH config (Not discussed)
If a UE is configured with Case1 HARQ timing, UE’s PRACH transmissions are not limited to the UL subframes given by subframe-Assignment-r15 (i.e., for FDD, UE can transmit PRACH in any UL subframe).
  If the UE’s LTE PRACH transmission collides with an NR UL transmission, PRACH transmission is prioritized

## Slide 9: Proposal: PUCCH formats (Not discussed)
(Nokia R1-1900697): If case 1 HARQ timing is introduced for TDD EN-DC, the PUCCH fallback operation is not supported

## Slide 10: Proposal: NR SRS config (Not discussed)
Allow EN-DC UE to transmit NR SRS overlapping in time with the last symbol of a LTE uplink subframe designated by subframeAssignment-r15
  The last LTE symbol thereof is reserved and not transmitted

## Slide 11: Proposal: LTE UL-CA (Not discussed)
Support LTE UL-CA for EN-DC with DL-reference UL-DL configuration on LTE serving cell.
  The subframes available for UL transmission can be common across LTE serving cells.