# 3GPP TSG-RAN2 WG2 Meeting #121bis Electronic									R2-230xxxx

# Online,  17th – 26th April 2023

Agenda Item:		6.1.3.2

Souce:	Samsung

Title:					[AT121bis-e][010][NR17] UE Caps Misc Corrections (Samsung)

Document for:		Discussion and Decision

# 1. Introduction

This report summarizes the following email discussion:

- [AT121bis-e][010][NR17] UE Caps Misc Corrections (Samsung)

Scope: Treat R2-2303882, R2-2302435, R2-2302941, R2-2302575, R2-2302774, R2-2302887
Ph1: Determine agreeable parts, prepare online CB points if any. Ph2: For agreeable parts, if any, reflect these in agreeable CRs.

Intended outcome: Report, If applicable: In-Principle-Agreed CRs

Deadline: Schedule 1

Discussions with Deadline Schedule 1:

A first round with Deadline W1 Thursday April 201th 1200 UTC to settle scope what is agreeable etc

A Final round with Final deadline W2 Wednesday April 26th 1000 UTC (EOM) to settle details / agree CRs etc.

Companies are invited to fill in contact details:

| Company | Name | Email Address |
| --- | --- | --- |
| Samsung | Sangbum Kim | sb07.kim@samsung.com |
| ZTE | Wenting Li | Li.wenting@zte.com.cn |
| OPPO | Qianxi Lu Zhongda | qianxi.lu@oppo.com Zhongda Du <duzhongda@oppo.com> |
| vivo | Xiao XIAO | xiao.xiao@vivo.com |
| Lenovo | Hyung-Nam Choi | hchoi5@lenovo.com |

# 2. Discussion, First Round

##### 2.1 Miscellaneous Correction on UE capability-R17

R2-2303882	Miscellaneous Correction on UE capability-R17	ZTE Corporation,Sanechips	CR	Rel-17	38.306	17.4.0	0900	-	F	NR_feMIMO, NR_pos_enh

This CR mentions reason for change as follows:

(1) The prerequisite “maxNumberMIMO-LayersNonCB-PUSCH” for the mTRP-PUSCH-RepetitionTypeB-r17 is missed. (2) The supportedActivatedPRS-ProcessingWindow-r17 is a value based capability, which indicates the number of supported activated PRS processing windows across all active DL BWPs supportedActivatedPRS-ProcessingWindow-r17 ENUMERATED {n2, n3, n4}

Question 1: Do companies agree with the intent of the CR above?

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | Proponent |
| OPPO (Zhongda) | Yes | maxNumberMIMO-LayersNonCB-PUSCH is part of 2-12, which is prerequisite of mTRP-PUSCH-RepetitionTypeB-r17 |
| Lenovo | Partly | Cover page: wrong meeting start date (“18”). To 1): Agree, but to make the proposed change better understandable we suggest to add the red text below in “Reason for change” on cover page. (1) The prerequisite “maxNumberMIMO-LayersNonCB-PUSCH” (R1 FG 2-15) for the mTRP-PUSCH-RepetitionTypeB-r17 (R1 FG 23-3-1-3) is missed. To 2): No need for the change. The current text is aligned with the RAN1 NR features list, see R1 FG 27-23. Prerequisite of supportedActivatedPRS-ProcessingWindow-r17 is the support of either prs-ProcessingWindowType1A-r17, prs-ProcessingWindowType1B-r17 or prs-ProcessingWindowType2-r17 (R1 FG 27-3-2). So, if the UE supports any of the processing window types but not supportedActivatedPRS-ProcessingWindow-r17, then it is assumed that the UE supports only one activated PRS processing window. |

Rapporteur Summary on Q1:

To be added

##### 2.2 ue-PowerClassPerBandPerBC

In RAN2#119bis, RAN2 sent an LS R2-221023 to RAN4 with the following questions:

1) Whether R4 16-8 is applicable to only inter-band CA? 2) What is the interaction between R4 16-8 and the existing power class capabilities (i.e. ue-PowerClass/ue-PowerClass-v1610/ue-PowerClass-1700, powerClassNRPart-r16 (if R4 16-8 is also applicable to the cases other than inter-band CA) and powerClass/powerClass-v1610)?

RAN4 responsed with the following Reply LS:

R2-2302435	Reply LS on clarification for ue-PowerClassPerBandPerBC-r17 (R4 16-8) (R4-2303630; contact: Samsung)	RAN4	LS in	Rel-17	NR_RF_FR1_enh	To:RAN2

Response to 1): Yes. It is applicable to only NR inter-band UL CA, i.e. when there is uplink configured in two different operating bands. Each uplink band contains only single UL CC or intra-band contiguous UL CA. Response to 2): ue-PowerClassPerBandPerBC-r17 indicates the power class that a UE supports for each individual band within a given band combination, while powerClass or powerClass-v1610 indicates the power class for this band combination, in other words, the maximum total output power. If indicated, ue-PowerClassPerBandPerBC-r17 shall supersede other power class capabilities such as ue-PowerClass/powerClass and its extensions in determining the power class of the individual bands within a band combination.

R2-2302941	Clarification on ue-PowerClassPerBandPerBC	Samsung		CR	Rel-17	38.306	17.4.0	0892	-	F	NR_RF_FR1_enh

This CR mentions to update the current description of ue-PowerClassPerBandPerBC-r17, according to the RAN4 input above.

Question 2: Do companies agree with the intent of the CR above? If required, companies can suggest further update in the Comments.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes |  |
| OPPO (Qianxi) | Not sure, see comment | It is dependent on Q3, i.e., how to understand the ‘supersede’ in the ‘supersede other power class capabilities such as ue-PowerClass/powerClass and its extensions in determining the power class of the individual bands within a band combination.’ |
| vivo | See comments | We share the view from OPPO. “Supersede” may not be simply interpreted as ignoring the legacy capability parameters. |

R2-2302575	Discussion on ue-PowerClassPerBandPerBC-r17	OPPO	discussion	Rel-17	NR_RF_FR1_enh

This discussion paper mentions the following proposal:

Proposal 1 RAN2 confim the new ue-PowerClassPerBandPerBC and the legacy powerClass fields can be both present, and both restrictions should be satisfied. If RAN2 cannot converge on this, send an LS to R4 to confirm.

Question 3: Do companies agree with the intention of the propsal of the document above? and need to send an LS to RAN4?

| Company | Agree with intention (Yes/No) | Send an LS to RAN4 (Yes/No) | Comments |
| --- | --- | --- | --- |
| ZTE | See comments | No | We are not quire sure how to understand “both restrictions should be satisfied” in the proposal, In the LS it said“ If indicated, ue-PowerClassPerBandPerBC-r17 shall supersede other power class capabilities” so if they are both present, the ue-PowerClassPerBandPerBC-r17 shall given the highest priority. |
| OPPO (Qianxi) | Yes | Yes | Proponent. Response to the question by ZTE: if we have a two band BC, band-A + band-B, after double check with our R4 colleagues, we understand both restrictions should be satisfied 1/ restriction-1 is by the R17 per-band-per-BC value, so that power of band-A < the ue-PowerClassPerBandPerBC-r17 for band-A of this BC, and power of band-B < the ue-PowerClassPerBandPerBC-r17 for band-B of this BC 2/ restriction-2 is by the legacy per-BC value, so that the power of band-A and the power of band-B, i.e., the sum < powerClass for this BC So if the ‘supersede’ means when ue-PowerClassPerBandPerBC-r17 is present, the legacy per-BC power restriction (restriction-2) is not needed, we hold different view here. |
| vivo | See comments | Maybe No | We share the view from OPPO above that the sum of the “per band per BC” power upper bounds given by the new ue-PowerClassPerBandPerBC-r17 may not automatically satisfy the “per BC” power upper bound given by the legacy per BC power restriction. It seems to be the case that both the per-band-per-BC power restriction and the per BC power restriction should be satisfied. Perhaps people can check internally with their RAN4 guys to see whether this should be the true intention alternatively. |

Rapporteur Summary on Q2 and Q3:

To be added

##### 2.3 TEI - MaxCCPerFRGap

R2-2302774	Clarification to description of independentGapConfig-maxCC-r17 [MaxCCPerFRGap]	Nokia, Nokia Shanghai Bell	CR	Rel-17	38.306	17.4.0	0889	-	F	TEI17

This CR mentions reason for change as follows:

The description of the field independentGapConfig-maxCC-r17 (introduced by CR#3704 in RP-223486 for the TEI17 ID [MaxCCPerFRGap]) is ambiguous: The description makes it seem like UE could not support FR1/FR2 serving cell configuration, while in fact the capability only indicates whether UE supports per-FR gaps for specific serving cell configurations. The conditions on the absence of the maxCC per-FR gap indications are also unclear since they seem to imply UE would not support per-FR gaps, even though they could be absent in case the legacy capability is indicated. Finally, the interpretation of the value “1” for fr1-AndFR2-r17 is not correct since it implies UE would support PCell and additional CC, which should be the case for only value “2”. If the intent was to say UE should always signal at least “2” for this case, that could be made more explicit and the whole description of what each value means could be simplified to apply in the same manner in all cases.

Question 4: Do companies agree with the intent of the CR above?

| Company | Yes/No | Comments |
| --- | --- | --- |
| OPPO (Zhongda) | Comments | The clarification on fr1-AndFR2-r17 is correct and necessary i.e. the value should be at least 2 since this is for the case both FR1 and FR2 serving cells are configured. The rest is just editorial change and we have no strong opinion |

Rapporteur Summary on Q4:

To be added

##### 2.4 CovEnh

R2-2302887	Clarifying band combination meaning for DMRS Bundling over TBoMS		Ericsson	CR	Rel-17	38.306	17.4.0	0890	-	F	NR_cov_enh-Core

This CR mentions reason for change as follows:

A note for the parameter dmrs-BundlingPUSCH-multiSlotPerBC-r17 tries to clarify how the band combination aspects of DMRS Bundling should be treated together with TBoMS. The note is a bit ambiguous and could lead to confusion, since it could be read that the band outside the band combination. We therefore suggest a slight rephrasing to make it clearer.

Question 5: Do companies agree with the intent of the CR above?

| Company | Yes/No | Comments |
| --- | --- | --- |
| OPPO (Zhongda) |  | A simpler version could be : NOTE 4: If a UE reports support of tb-ProcessingRepMultiSlotPUSCH-r17 and dmrs-BundlingPUSCH-multiSlot-r17 in a band in the band combination and dmrs-BundlingPUSCH-multiSlotPerBC-r17 is supported for the band combination, the UE supports DMRS bundling for the repetitions of TBoMS for that band. |

Rapporteur Summary on Q5:

To be added

# 3. Conclusion

To be added