3GPP TSG-RAN WG2 Meeting#121bis-e	R2-23xxxxx

Electronic Meeting, 17 – 26 April, 2023

Agenda Item: 	6.6.2

Source:	Apple

Title:	Report of [AT121bis-e][102][NR NTN] UP corrections (Apple)

Document for:		Discussion and Decision

# Introduction

This document captures the outcome of the following email discussion:

[AT121bis-e][102][NR NTN] UP corrections (Apple)

Initial scope: Discuss corrections in 6.6.2

Initial intended outcome: Summary of the offline discussion with list of agreeable corrections/CRs

Deadline for companies' feedback: Friday 2023-04-21 08:00 UTC

Deadline for rapporteur's summary (in R2-2304242): Friday 2023-04-21 10:00 UTC

NOTE: Proposals marked "for agreement" in the final report (R2-2304242) not challenged until Monday 2023-04-24 10:00 UTC will be declared as agreed via email by the session chair (for the rest the discussion might continue online).

# Contact Points

Rapporteur encourages the participating delegates to provide their contact information in this table.

| Company | Name | Email Address |
| --- | --- | --- |

# Discussion

## Validity timer expiry

R2-2303413 Clarification on UL operation upon validity timer expiry Apple CR Rel-17 38.321 17.4.0 1588 - F NR_NTN_solutions-Core Summary of change: Add NOTE to clarify UE may suspend all UL operation (e.g. RACH, SR, UL HARQ operation) if receiving the uplink synchornization loss indication. Add the reference section and spec of the UL sync loss indiatin from upper layer.

R2-2303960 UE behaviour related to SR and RACH after validity timer expires Huawei, HiSilicon discussion Rel-17 NR_NTN_solutions-Core Late Proposals: Proposal 1: RAN2 to clarify whether the PUCCH resource is still valid after the validity timer (T430) expires and if valid, what is the intended UE behaviour when there is a pending SR. Proposal 2: RAN2 to clarify the UE behaviour related to RACH after the validity timer (T430) expires.

R2-2303979 Corrections on MAC procedure upon validity timer expiry for NR NTN Nokia, Nokia Shanghai Bell CR Rel-17 38.321 17.4.0 1606 - F NR_NTN_solutions-Core Summary of change: When the MAC entity is not allowed to perform any uplink transmission on the Serving Cell in non-terrestrial network due to T430 expiry: Update section 5.1.3 Random Access Preamble transmission procedure, to suspend premable transmission. Update section 5.1.3a MSGA transmission procedure, to suspend MSGA transmission. Update section 5.4.1 UL Grant reception, to suspend the recevied UL grant process. Update section 5.4.4 Scheduling Request, to suspend the SR transmission.

R2-2304001 Discussion on the UE behaviour when the validity timer expires LG Electronics Inc. discussion NR_NTN_solutions-Core Proposals: Proposal 1. RAN2 confirm all uplink resources for a serving cell are considered as invalid if the MAC entity receives an indication for the uplink synchronization loss for the serving cell. Proposal 2. For proposal 1, the specification is not changed.

Following is the spec description on the UE operation upon the validity timer T430 expiry.

According to current spec, it’s just saying UE doesnot perform any uplink transmission on the serving cell upon the validity timer expiry, but UE operation on the following two issues is not clear, so some clarification is needed.

- Issue 1: whether the uplink resource (e.g. PUCCH and SRS) is still valid or not;

- Issue 2: whether UE needs to suspend all the uplink operations.

On Issue 1, two contributions bring the proposals about the validity of uplink resources upon the validity timer expiry:

- R2-2303960 indicates that SR over PUCCH is not performed so that the validity of PUCCH resource needs to be clarified.

- R2-2304001 proposes to clarify the uplink resources are not released but considered as invalid.

In moderator’s understanding, the key issue is to first clarify whether uplink resources (e.g. PUCCH, SRS) should be released by RRC upon the validity timer expiry, similar as the operation upon TATimer expiry.

### Question 1: Which option of the UE operation on the uplink resources (PUCCH, SRS) do you prefer?

- Option 1: the uplink resources are NOT released by RRC

  - The configuration can be reused when UE acquires SIB19 later.

- Option 2: the uplink resources are released by RRC.

  - Network is required to reconfigure the resources after UE acquires SIB19 later.

| Company | Preferred option? | Comments |
| --- | --- | --- |

On Issue 2, following contributions brings the proposals related to MAC operation upon the validity timer expiry,

- Both R2-2303413 and R2-2303979 propose to suspend all the uplink operation in MAC, including RACH, SR, UL HARQ operation, etc, but the provided TPs are different.

- R2-2303960 would like to clarify UE operation related to RACH.

In moderator’s understanding, the key issue is to first clarify the UE MAC operation and then to check company’s preference on the necessity of the spec change and the preferred TP.

### Question 2: Do you agree that UE MAC should suspend all the UL operation (e.g. RACH, SR, UL HARQ) upon the validity timer expiry?

| Company | Yes or No | Comments |
| --- | --- | --- |

#### Question 2a: If your answer to Question 2 is YES, do you think the MAC spec change for the clarification is needed?

| Company | Yes or No | Comments |
| --- | --- | --- |

#### Question 2b: If your answer to Question 2a is YES, which TP do you prefer?

- Option 1: TP in R2-2303413 (i.e. add a note to clarify the UE operation)

- Option 2: TP in R2-2304001 (i.e. i.e. add a note to clarify the UL resources are invalid)

- Option 3: TP in R2-2303979 (i.e. clarify it in each procedural part)

5.4.1 UL Grant reception

5.4.4 Scheduling Request

| Company | Preferred Option | Comments |
| --- | --- | --- |

#### Question 2c: If your answer to Question 2 is NO, please describe your understanding on the UE MAC operation in the table.

| Company | UE MAC operation upon validity timer expiry |
| --- | --- |

## Other

### R2-2303820 - Clarification on HARQ feedback of the first SPS PDSCH after the activation

R2-2303820 Corrections to NR NTN for 38.321 CATT, Turkcell, Huawei, HiSilicon, Quectel, CAICT CR Rel-17 38.321 17.4.0 1597 - F NR_NTN_solutions-Core Late

Reason for change: Current MAC spec description is not aligned with RRC description on harq-FeedbackEnablingforSPSactive, and UE may feed back ACK/NACK unnecessary for a dynamic HARQ process by mistake.

Summar of change: In 5.3.2.2, adding a description that the first transmission after activation of the configured downlink assignment is the first transmission on the configured downlink assignment after activation of the configured downlink assignment.

MAC TP: (5.3.2.2 HARQ process)

#### Question 3: Do you agree with the CR (R2-2303820)?

| Company | Yes or No | Comments |
| --- | --- | --- |

### R2-2303833 - Correction for R17 NR NTN description of HARQ mode

R2-2303833 Correction for R17 NR NTN description of HARQ mode Ericsson CR Rel-17 38.321 17.4.0 1598 - F NR_NTN_solutions Late

Reason for change: Currently the HARQ mode A and HARQ mode B are not described in RRC, stage 2 nor in MAC. We think it would be benefical to have a description somewhere

Summar of change: HARQ mode is added among the definitions in 3.1.

MAC TP: (3.1 Defitions)

#### Question 4: Do you agree with the CR (R2-2303833)?

| Company | Yes or No | Comments |
| --- | --- | --- |

### R2-2304000 - Restriction on the usage of the same HARQ

R2-2304000 Discussion on the restriction on the usage of the same HARQ mode to the configured grant LG Electronics Inc. discussion NR_NTN_solutions-Core

Proposals: Observation 1. In the current specification, it seems that the configuration of the HARQ process IDs having the different HARQ modes to one configured grant is allowed. Observation 2. In order to generate the MAC PDU containing the MAC SDUs associated with the same service, the HARQ process IDs associated with the same HARQ mode should be configured to a configured grant. Observation 3. The configuration of two configured grant timers causes the backward compatibility issue. Proposal. It should be restricted that the HARQ process IDs having the same HARQ mode should be configured to a configured grant.

RRC TP:

#### Question 5: Do you agree with the proposal?

Proposal. It should be restricted that the HARQ process IDs having the same HARQ mode should be configured to a configured grant.

| Company | Yes or No | Comments |
| --- | --- | --- |

#### Question 5a: Do you agree with the TP in R2-2304000?

| Company | Yes or No | Comments |
| --- | --- | --- |

# Conclusion

Based on the above discussion, we propose that: