3GPP TSG-RAN WG2 Meeting#121bis-e	R2-23xxxxx

Electronic Meeting, 17 – 26 April, 2023

Agenda Item: 	6.6.2

Source:	Apple

Title:	Report of [AT121bis-e][102][NR NTN] UP corrections (Apple)

Document for:		Discussion and Decision

# Introduction

This document captures the outcome of the following email discussion:

[AT121bis-e][102][NR NTN] UP corrections (Apple)

Initial scope: Discuss corrections in 6.6.2

Initial intended outcome: Summary of the offline discussion with list of agreeable corrections/CRs

Deadline for companies' feedback: Friday 2023-04-21 08:00 UTC

Deadline for rapporteur's summary (in R2-2304242): Friday 2023-04-21 10:00 UTC

NOTE: Proposals marked "for agreement" in the final report (R2-2304242) not challenged until Monday 2023-04-24 10:00 UTC will be declared as agreed via email by the session chair (for the rest the discussion might continue online).

# Contact Points

Rapporteur encourages the participating delegates to provide their contact information in this table.

| Company | Name | Email Address |
| --- | --- | --- |
| MediaTek | Abhishek Roy | Abhishek.Roy@mediatek.com |
| Qualcomm | Bharat Shrestha | bshrestha@qti.qualcomm.com |
| Nokia | Ping Yuan | Ping.1.yuan@nokia-sbell.com |

# Discussion

## Validity timer expiry

R2-2303413 Clarification on UL operation upon validity timer expiry Apple CR Rel-17 38.321 17.4.0 1588 - F NR_NTN_solutions-Core Summary of change: Add NOTE to clarify UE may suspend all UL operation (e.g. RACH, SR, UL HARQ operation) if receiving the uplink synchornization loss indication. Add the reference section and spec of the UL sync loss indiatin from upper layer.

R2-2303960 UE behaviour related to SR and RACH after validity timer expires Huawei, HiSilicon discussion Rel-17 NR_NTN_solutions-Core Late Proposals: Proposal 1: RAN2 to clarify whether the PUCCH resource is still valid after the validity timer (T430) expires and if valid, what is the intended UE behaviour when there is a pending SR. Proposal 2: RAN2 to clarify the UE behaviour related to RACH after the validity timer (T430) expires.

R2-2303979 Corrections on MAC procedure upon validity timer expiry for NR NTN Nokia, Nokia Shanghai Bell CR Rel-17 38.321 17.4.0 1606 - F NR_NTN_solutions-Core Summary of change: When the MAC entity is not allowed to perform any uplink transmission on the Serving Cell in non-terrestrial network due to T430 expiry: Update section 5.1.3 Random Access Preamble transmission procedure, to suspend premable transmission. Update section 5.1.3a MSGA transmission procedure, to suspend MSGA transmission. Update section 5.4.1 UL Grant reception, to suspend the recevied UL grant process. Update section 5.4.4 Scheduling Request, to suspend the SR transmission.

R2-2304001 Discussion on the UE behaviour when the validity timer expires LG Electronics Inc. discussion NR_NTN_solutions-Core Proposals: Proposal 1. RAN2 confirm all uplink resources for a serving cell are considered as invalid if the MAC entity receives an indication for the uplink synchronization loss for the serving cell. Proposal 2. For proposal 1, the specification is not changed.

Following is the spec description on the UE operation upon the validity timer T430 expiry.

According to current spec, it’s just saying UE doesnot perform any uplink transmission on the serving cell upon the validity timer expiry, but UE operation on the following two issues is not clear, so some clarification is needed.

- Issue 1: whether the uplink resource (e.g. PUCCH and SRS) is still valid or not;

- Issue 2: whether UE needs to suspend all the uplink operations.

On Issue 1, two contributions bring the proposals about the validity of uplink resources upon the validity timer expiry:

- R2-2303960 indicates that SR over PUCCH is not performed so that the validity of PUCCH resource needs to be clarified.

- R2-2304001 proposes to clarify the uplink resources are not released but considered as invalid.

In moderator’s understanding, the key issue is to first clarify whether uplink resources (e.g. PUCCH, SRS) should be released by RRC upon the validity timer expiry, similar as the operation upon TATimer expiry.

### Question 1: Which option of the UE operation on the uplink resources (PUCCH, SRS) do you prefer?

- Option 1: the uplink resources are NOT released by RRC

  - The configuration can be reused when UE acquires SIB19 later.

- Option 2: the uplink resources are released by RRC.

  - Network is required to reconfigure the resources after UE acquires SIB19 later.

| Company | Preferred option? | Comments |
| --- | --- | --- |
| MediaTek | Option 1 | We think the UL resources are still valid and can be reused when UE acquires SIB19 later. |
| Qualcomm | Option 1 | We simply disagree with the view that there is any confusion on whether the UL resources should be released. Let’s just check the UE behavior upon expiry of such timer, both TAT and for UL synchronization timer, don’t we see the difference here? We didn’t capture release of resource for UL synchronization, and it was by design. We heavily discussed whether to flush the HARQ buffer or not. We wanted to keep the HARQ buffer as it is but finally agreement was to flush HARQ buffer, that’s it. This whole design is that UE just suspends UL, reads SIB19, gets UL synchronization and resumes the UL transmission, continue using UL resources. If clarification is needed for UL operation, we can add. We should NOT just randomly propose new UE behavior as late correction. |
| Nokia | Option 1 | Similar view as Qualcomm. The topic was discussed in several meetings, and we proposed the validity timer expiry should be handled with the similar rule as TAT timer expiry but it was not agreed. It is too late to go Option2 in this late stage. |

On Issue 2, following contributions brings the proposals related to MAC operation upon the validity timer expiry,

- Both R2-2303413 and R2-2303979 propose to suspend all the uplink operation in MAC, including RACH, SR, UL HARQ operation, etc, but the provided TPs are different.

- R2-2303960 would like to clarify UE operation related to RACH.

In moderator’s understanding, the key issue is to first clarify the UE MAC operation and then to check company’s preference on the necessity of the spec change and the preferred TP.

### Question 2: Do you agree that UE MAC should suspend all the UL operation (e.g. RACH, SR, UL HARQ) upon the validity timer expiry?

| Company | Yes or No | Comments |
| --- | --- | --- |
| MediaTek | Yes |  |
| Qualcomm | Yes | We are ok to clarify that UE does not perform UL operations until UL synchronization is restored. |
| Nokia | Yes | Since any UL transmission is not allowed to be performed during the period of UL synchronization loss, the UE should suspend the SR transmission and RACH preamble transmission in RACH procedure to avoid useless RACH or SR transmission attempts which may cause the false RACH/SR failure declaration, even the PUCCH resource is valid. Similarly, it may cause extra delay for UL data transmission to cancel the pending BSR when it is included in the TB while the corresponding PUSCH cannot be transmitted. Therefore, the TB processing upon UL grant reception should be suspended as well. |

#### Question 2a: If your answer to Question 2 is YES, do you think the MAC spec change for the clarification is needed?

| Company | Yes or No | Comments |
| --- | --- | --- |
| MediaTek | Yes |  |
| Qualcomm | Yes |  |
| Nokia | Yes | The MAC specification should be clarified to avoid confusion. |

#### Question 2b: If your answer to Question 2a is YES, which TP do you prefer?

- Option 1: TP in R2-2303413 (i.e. add a note to clarify the UE operation)

- Option 2: TP in R2-2304001 (i.e. i.e. add a note to clarify the UL resources are invalid)

- Option 3: TP in R2-2303979 (i.e. clarify it in each procedural part)

5.4.1 UL Grant reception

5.4.4 Scheduling Request

| Company | Preferred Option | Comments |
| --- | --- | --- |
| MediaTek | Option 1 |  |
| Qualcomm | Option 1 see comments | Option 3 is also Ok but the text does not read very clear. Probably it should be like Except when the UL synchronization is lost in NTN, the MAC entity shall, for each random access preamble: But it seems option 1 requires less specification change, but still wording needs to be further checked as this can be procedural text. We should also clarify then if there is new UL data arrival, should UE trigger BSR when UL synchronization is lost? |
| Nokia | Option 3 or new Option 4 | We are open to discuss how to capture the MAC behavior but we prefer to capture it in procedural text instead of NOTE. As defined in the “Specification drafting rules” TR 21.801, NOTE is for informative elements hence it is up to UE to implement it or not. While the procedure text (Normative elements) is a requirement to UE implementation. We think suspending UE MAC procedures is clearly a UE requirement hence procedure text is preferred. For Option1, the Note does not work with "may" as it should be normative UE behavior. For Option2, it has side effect to consider the UL resource as invalid. For Option3, we are also fine with QC’s rewording. After some offline discussion with companies, we think the below Option4 seems have minimum impact to MAC specification which is also OK to us. 5.2a Maintenance of UL Synchronization The MAC entity shall for each Serving Cell: 1> if an indication of uplink synchronization has been received from upper layers (see clause 5.2.2.6 of TS 38.331 [5]): 2> allow uplink transmission on the Serving Cell. 2> allow deliver of grants to the HARQ entity. 2> resume suspended scheduling request procedure and Random Access procedure, if any. 1> if an indication of uplink synchronization loss is received from upper layers: 2> flush all HARQ buffers; 2> not perform any uplink transmission on the Serving Cell. 2> not deliver any grant to the HARQ entity. 2> suspend any ongoing scheduling request procedure. 2> suspend any ongoing Random Access procedure. |

#### Question 2c: If your answer to Question 2 is NO, please describe your understanding on the UE MAC operation in the table.

| Company | UE MAC operation upon validity timer expiry |
| --- | --- |

## Other

### R2-2303820 - Clarification on HARQ feedback of the first SPS PDSCH after the activation

R2-2303820 Corrections to NR NTN for 38.321 CATT, Turkcell, Huawei, HiSilicon, Quectel, CAICT CR Rel-17 38.321 17.4.0 1597 - F NR_NTN_solutions-Core Late

Reason for change: Current MAC spec description is not aligned with RRC description on harq-FeedbackEnablingforSPSactive, and UE may feed back ACK/NACK unnecessary for a dynamic HARQ process by mistake.

Summar of change: In 5.3.2.2, adding a description that the first transmission after activation of the configured downlink assignment is the first transmission on the configured downlink assignment after activation of the configured downlink assignment.

MAC TP: (5.3.2.2 HARQ process)

#### Question 3: Do you agree with the CR (R2-2303820)?

| Company | Yes or No | Comments |
| --- | --- | --- |
| MediaTek | Yes |  |
| Qualcomm | Yes |  |
| Nokia | Yes |  |

### R2-2303833 - Correction for R17 NR NTN description of HARQ mode

R2-2303833 Correction for R17 NR NTN description of HARQ mode Ericsson CR Rel-17 38.321 17.4.0 1598 - F NR_NTN_solutions Late

Reason for change: Currently the HARQ mode A and HARQ mode B are not described in RRC, stage 2 nor in MAC. We think it would be benefical to have a description somewhere

Summar of change: HARQ mode is added among the definitions in 3.1.

MAC TP: (3.1 Defitions)

#### Question 4: Do you agree with the CR (R2-2303833)?

| Company | Yes or No | Comments |
| --- | --- | --- |
| MediaTek | Yes |  |
| Qualcomm | No | After many rounds of reviews of running MAC CR, nobody raised there was any need to have such. Simply because it is already clear when drx-RetransmissionTimerUL is started. |
| Nokia | No | If we want to clarify HARQ mode A/B, it should include all the impacts caused by different HARQ mode (e.g. LCP, DRX). |

### R2-2304000 - Restriction on the usage of the same HARQ

R2-2304000 Discussion on the restriction on the usage of the same HARQ mode to the configured grant LG Electronics Inc. discussion NR_NTN_solutions-Core

Proposals: Observation 1. In the current specification, it seems that the configuration of the HARQ process IDs having the different HARQ modes to one configured grant is allowed. Observation 2. In order to generate the MAC PDU containing the MAC SDUs associated with the same service, the HARQ process IDs associated with the same HARQ mode should be configured to a configured grant. Observation 3. The configuration of two configured grant timers causes the backward compatibility issue. Proposal. It should be restricted that the HARQ process IDs having the same HARQ mode should be configured to a configured grant.

RRC TP:

#### Question 5: Do you agree with the proposal?

Proposal. It should be restricted that the HARQ process IDs having the same HARQ mode should be configured to a configured grant.

| Company | Yes or No | Comments |
| --- | --- | --- |
| MediaTek | No | We don’t think this is needed. UE implementation can take care of this. |
| Qualcomm | Yes | We are ok to capture as our current understanding is network will do it. See agreement of RAN2#116bis and following note in TS 38.300 v17.0.0. NOTE: It is up to network implementation to ensure proper configuration of HARQ feedback (i.e. enabled or disabled) for HARQ processes used by an SPS configuration and of HARQ mode for HARQ processes used by a CG configuration. |
| Nokia | No | RAN2 discussed the issue with below agreement. It was concluded no specification impact. RAN2 understanding: 1. RAN2 understanding is that: in general, all HARQ processes used by an SPS configuration are configured with the same HARQ feedback enabled/disabled state. No specification impact. 2. RAN2 understanding is that: in general, all HARQ processes used by a CG configuration are configured with the same HARQ state (e.g. A or B). No specification impact |

#### Question 5a: Do you agree with the TP in R2-2304000?

| Company | Yes or No | Comments |
| --- | --- | --- |
| MediaTek | No | We don’t think this is needed. UE implementation can take care of this. |
| Qualcomm | Yes | Better to have same HARQ behavior in every CG occasion for the same LCH traffic using same CG configuration. |
| Nokia | No |  |

# Conclusion

Based on the above discussion, we propose that: