3GPP TSG-RAN WG2 #121bis-e								R2-230xxxx

E-meeting, April 2023

Agenda Item:	7.24.2

Source:	OPPO

Title:	[Draft] [AT121bis-e][415][Relay] Emergency service for relays (OPPO)

Document for:	Discussion, Decision

# Introduction

This document is a report on the following email discussion:

- [AT121bis-e][415][Relay] Emergency service for relays (OPPO)

Scope: Discuss the proposals in R2-2302648 and attempt to develop a CR if the proposals are agreeable in principle.

Intended outcome: Report and agreeable CR

Deadline: Monday 2023-04-24 2359 UTC

# Contact Information

| Company | Name | Email Address |
| --- | --- | --- |
| OPPO | Bingxue Leng | lengbingxue@oppo.com |
| Xiaomi | Xing Yang | Yangxing1@xiaomi.com |
| Ericsson | Nithin Srinivasan | nithin.srinivasan@ericsson.com |
| Qualcomm | Jianhua Liu | jianhua@qti.qualcomm.com |
| ZTE | Mengzhen Wang | Wang.mengzhen@zte.com.cn |
| Huawei, HiSilicon | Rui Wang | Wangrui46@huawei.com |
| CATT | Hao Xu | xuhao@catt.cn |
| Nokia | Gyuri Wolfner | Gyorgy.wolfner@nokia.com |
| Samsung | Hyunjeong Kang | hyunjeong.kang@samsung.com |
| Apple | Zhibin Wu | Zhibin_wu@apple.com |

# Discussion

For the support of emergency for UE-to-Network Relaying, SA2 has made some conclusions for both L2 and L3 relay, which may have RAN2 impacts

SA2 conclusions in TR 23.700 for key issue #7[1]

Key Issue #7: Support of Emergency for UE-to-Network Relaying For Key Issue #7: Support of Emergency for UE-to-Network Relaying, the following are concluded. The following conclusions are common to Layer-2 and Layer-3 UE-to-Network Relaying: - For emergency service, the UE shall prioritise direct connection to network. If direct connection is not possible (including the case that the RAN broadcast SIB indicates no emergency support), the UE shall attempt to obtain emergency service via UE-to-Network Relay. - A 5G ProSe enabled UE acting as Relay shall have a normal registration (including also normal registration for a 5G ProSe Relay enabled UE in Non-Allowed Area). A 5G ProSe Relay enabled UE in limited-service state shall not act as Relay. Mobility Restrictions that are overruled for UE requesting direct emergency service are overruled also for 5G ProSe UE-to-Network Relay that is relaying emergency service. - A 5G ProSe enabled UE without direct connection to the network for emergency service may request emergency service via the 5G ProSe Relay. - RSC(s) dedicated for emergency service needs to be provisioned in the 5G ProSe enabled Ues with capability of Relay UE and Remote UE using procedure as specified in clause 5.1.4 of TS 23.304 [3]. The dedicated RSC(s) are used by the 5G ProSe UE-to-Network Relay UE and Remote UE during discovery and PC5 link establishment. - A dedicated PC5 link associated with an emergency RSC is only used for emergency service. A 5G ProSe enabled UE shall not advertise its support for relaying emergency service unless the serving network has provided an indication of support of relaying of emergency service. NOTE 1: Whether a 5G ProSe Layer-2 UE-to-Network Relay needs the indication of support of relaying emergency services from its serving PLMN before advertising its support of relaying emergency services is to be determined in normative phase. - If the 5G ProSe Relay needs to establish RRC Connection when the 5G ProSe Remote UE has requested emergency service over PC5, the 5G ProSe Relay shall use “Emergency” RRC Establishment Cause. - Emergency call back for 5G ProSe UE-to-Network Remote UE regulatory requirements will be supported using existing functionality defined for Emergency Services. - The existing positioning function are reused for the 5G ProSe Remote UE. If no other information is available, the location of the 5G ProSe UE-to-Network Relay can be used as Remote UE location estimate. NOTE 2: Whether and how PC5 security is used for emergency services is to be determined in the normative phase as part of SA3 alignment. The following conclusions apply to Layer-2 UE-to-Network Relaying: - For a 5G ProSe Layer-2 UE-to-Network Relay to advertise its support of emergency service, the serving NG-RAN support of emergency services is required as the Layer-2 Remote UE may select a different PLMN from the Layer-2 Relay. - A 5G ProSe Layer-2 Remote UE will set its RRC establishment cause to “emergency” when establishing RRC connection from RRC_IDLE. - When NG-RAN receives an emergency RRC establishment from a 5G ProSe Layer-2 Remote UE it may need to direct the initial UE message towards its PLMN as in legacy. The following conclusions apply to Layer-3 UE-to-Network Relaying: - A 5G ProSe Layer-3 UE-to-Network Relay participates the relay discovery procedure for emergency service only when it receives the Emergency Service Support indicator in Registration Accept. - If PC5 connection was requested using emergency RSC, then the 5G ProSe Layer-3 Relay sets the RRC Establishment cause to “emergency” when establishing an RRC connection from RRC_IDLE. - The emergency number(s) may be preconfigured in the 5G ProSe Remote UE - For Layer-3 UE to Network Relaying, the Remote UE may obtain P-CSCF address from the Relay UE via DHCP or may be preconfigured with P-CSCF address. NOTE 3: Remote UE obtaining P-CSCF address via DHCP is specified in clause 14A.2.1 of TS 24.379 [26]. - A Layer-3 UE-to-Network Relay sets up or modifies an emergency PDU session to support the Remote UE’s emergency service. - When a 5G ProSe Layer-3 UE-to-Network Relay UE initiates emergency service, the 5G ProSe Relay UE shall not advertise its support of emergency service and reject any Remote UE’s requests for relaying emergency services. The 5G ProSe Layer-3 UE-to-Network Remote UE can attempt to select other 5G ProSe Layer-3 UE-to-Network Relay. - If the 5G ProSe Layer-3 Relay is relaying an emergency service for a 5G ProSe Layer-3 Remote UE, then it shall prioritise its own emergency service establishment and stop relaying the Remote Ues emergency service. Editor’s note: SA WG1 is expected to verify the service requirement for pre-empting relayed emergency service. - A 5G ProSe Layer-3 Remote UE should attempt to use 5G ProSe Communication via 5G ProSe Layer-3 UE-to-Network Relay without N3IWF procedures before attempting to establish an emergency PDU Session via 5G ProSe Layer-3 UE-to-Network Relay with N3IWF support. - The 5G ProSe Layer-3 UE-to-Network Remote UE set the access type to NG-RAN via 5G ProSe Layer-3 UE-to-Network Relay to P-CSCF. NOTE 4: This access type indication is required for all IMS services and is not specific for emergency service. It will be introduced by CT WG1.

SA2 specification of supporting emergency in U2N relay in TS 23.304[2]

.5.4.4.1 General When a 5G ProSe enabled UE does not have direct connection to the network for emergency service, the UE may attempt to obtain emergency service via 5G ProSe Layer-2 or Layer-3 UE-to-Network Relay. NOTE: Direct connection refers to the UE connected to the network via Uu or WLAN. No direct connection to the network for emergency service includes also the case that the RAN broadcast SIB indicates no emergency support as specified in TS 23.122 [14]. A 5G ProSe enabled UE acting as 5G ProSe UE-to-Network Relay shall have a normal registration (including also normal registration for a 5G ProSe Relay enabled UE in Non-Allowed Area). A 5G ProSe enabled UE in limited-service state shall not act as 5G ProSe UE-to-Network Relay. Mobility Restrictions that are overruled for UE requesting direct emergency service are overruled also for 5G ProSe UE-to-Network Relay that is relaying emergency service as specified in clause 5.4.3. A 5G ProSe enabled UE shall only advertise its support for relaying emergency service when the serving network has indicated support of relaying of emergency service. RSC(s) dedicated for emergency service needs to be provisioned in the 5G ProSe enabled Ues with capability of 5G ProSe UE-to-Network Relay and/or 5G ProSe Remote UE as specified in clause 5.1.4. The dedicated RSC(s) are used by the 5G ProSe UE-to-Network Relay and 5G ProSe Remote UE during discovery and PC5 link establishment. A PC5 link associated with a dedicated emergency RSC is only used for emergency service.

According to the above SA2 specs, the PC5 link with emergency RSC can only be used for emergency service, and it has been further discussed in R2-2302648 that since emergency service and non-emergency service cannot share the same relay link, E.g.,

- In case a remote UE has connected to network via a relay link associated with an emergency RSC, and then it switches to other services type (non-emergency coming), the UE needs to trigger a new PDU Session establishment procedure for the non-emergency service, and according to SA2 conclusion, it cannot use the current emergency-dedicated relay link, i.e., reconfiguration on the path is needed.

- Or on the other hand, initially the UE is served via direct path, and later the network would like to offload the UE to an indirect path, yet without knowing whether it is performing emergency or non-emergency service, the network cannot decide which type of relay/RSC to offload the UE to.

Since it is network who controls the path switching of RRC_CONNECTED UE, the impact is to let remote UE report its initiation/stop on the (non-)emergency service, i.e., remote UE needs to report to network on the coming non-emergency service.

And the following Proposal1 is for this

- Remote UE indicates to network on the start/stop of emergency and non-emergency service.

The following Qs are to check companies’ view on the above Proposal 1:

Question 1a: Do you agree the network has to base on remote UE service type information (emergency or non-emergency) to decide on indirect / relay path (re)configuration?

| Company | Yes/No | Comments |
| --- | --- | --- |
| OPPO | Yes | Updated comment: Based on the companies replies so far (and some offline discussions), seems there is a majority preference on reusing the existing mechanisms, the following WFs are proposed by companies Remote UE requests to release the connection with NW via NAS release request for the old service, and initiate a new connection for the new coming service with a cause value to indicate the intended service; Rely on CN to indicate the coming service to gNB For the above 2 directions, we are open to follow majority view as long as we have a common understanding on this issue, and if RAN2 made conclusions have impact on other WGs (e.g., SA/RAN3), a LS may be required. |
| Xiaomi | Yes |  |
| Ericsson | No, see comments | The SA2 spec only talks about “the PC5 link associated with a dedicated emergency RSC is only used for emergency service”. There is no information on path (re)configuration or link modification. But the question seems to indicate that this is a requirement. From a remote Ues perspective, once the emergency service is finished and a non-emergency service is to be started, the remote UE can tear down the PC5 connection (used for emergency) and initiate a new connection for non-emergency. In which case, the remote UE will indicate during the RRC connection establishment procedure the cause and then the network can set the necessary configurations for the paths. [OPPO] ‘In which case, the remote UE will indicate during the RRC connection establishment procedure the cause’ seems you are assuming the UE is experience an IDLE/INACTIVE-to-CONNECTED state change in this case, what if there is no such transition? [Ericsson, additional response] As mentioned above, the SA2 spec only talks about having a dedicated PC5-link for emergency services. But there is no information that the UE in RRC_CONN needs to stay in that state and then perform a path (re)configuration. The remote UE can tear down the connection once the emergency service is done i.e., move to RRC_IDLE. Then, setup the connection again for non-emergency service i.e., transition to RRC_CONN state and indicate the cause value in MSG3. [OPPO2] just to catch up with you: “tear down the connection once the emergency service is done” does it mean the UE autonomously enters into RRC_IDLE without network indication? |
| Qualcomm | No | There is no such service switching or service continuity requirement from SA2 spec. If interested, companies can firstly discuss in SA2 if there is any gap from system level point of view. Currently, there are some existing methods to be reused, e.g. based on ARP info, gNB know the service is emergency service; Remote UE can deactivate emergency and non-emergency service PDU sessions to trigger service change. [OPPO] For “there are some existing methods to be reused, e.g. based on ARP info, gNB know the service is emergency service”, according to the following SA2 spec, the gNB can only know the service is emergency via ARP info after the RAN resource has been established, the case we are talking about is how establishing a new path (RAN resource) for the new coming service due to the old path is not able to carry any information related to the new service. Reference from SA2 spec TS23.501 When the ®AN resources for Emergency Services are established, the ARP value for Emergency Services indicates the usage for Emergency Services to the 5G-AN. |
| Vivo | YES, but with comments | We see its benefits for gNB to know the start/stop of emergency service at remote UE side in order to prioritize path switch to direct path over indirect path. However, we think how gNB would know the start/stop of emergency and non-emergency service at remote UE side can be fulfilled by current mechanism without the need of additional enhancements to Uu interface. For the start of emergency service at remote UE side, the gNB would know there is emergency service arrival according to the cause value of remote UE’s own RRCSetupRequest or RRCResumeRequest message. For the stop of emergency service at remote UE side, as the emergency PDU session established for remote UE’s emergency service would be released by CN. So, our understanding is that it’s up to interaction between RAN and CN on how the gNB would know the stop of emergency service at remote UE side. No need to report assistance information from remote UE via Uu. |
| Lenovo | Yes | We agree some indirect path configuration should be updated when the emergency service is started based on the SA2 specification. However, how to indicate to gNB can rely on the existing mechanism e.g cause value in RRC message from idle/inactive sate or CN indicate to gNB. We would like to reduce the impact on AS specification. |
| ZTE | comments | Since the emergency service and non-emergency service use different PDU sessions, when remote UE trigger a new PDU session for non-emergency/emergency service, the CN is able to identify the new PDU session is for non-emergency/emergency. And then the CN initiates PDU session establishment for non-emergency/emergency service to gNB. So gNB can know the service type by PDU session establishment procedure from CN, no need remote UE to report. On the other hand, the support of emergency service is mainly in SA2, if RAN support is needed, SA2 should send LS to trigger RAN discussion. |
| Huawei, HiSilicon | See comments | In general, we understand how to support emergency service via relay is still under-discussion in SA2. To us, it is premature to analyze RAN2 impact without SA2 final conclusion and official LS to RAN2. Then regarding the question whether gNB is aware that emergency service is ongoing or not for a Remote UE, we share the same view with Qualcomm that network has some tools (e.g. ARP, QCI) to know there is emergency service. |
| CATT | See comments | Same view as Huawei and QC. |
| NEC | See comments | There is no such service switching or service continuity requirement from SA2 spec. |
| Nokia | No, comments | The SA2 specification does not specify the AS layer behaviour, it only creates the requirement that “A PC5 link associated with a dedicated emergency RSC is only used for emergency service.”. As ZTE commented above there are dedicated PDU sessions for emergency sessions and thus the gNB can learn from the CN which PDU sessions are for emergency sessions. |
| Samsung | See comments | There may be no need of AS signalling. |
| Apple | See comments | We have doubts about the exact meaning of “A PC5 link associated with a dedicated emergency RSC” . it is not clear to us whether this is a categorical requirement or a status description. In general, we think SA2 allows the PC5 link to be multiplexed with different service types. We are open to have a LS to SA2 to check this. |
| Intel | See comment | For the case where the UE switches from direct path to indirect path, it is our understanding that the RSC is already considered during the discovery phase and the list of candidate relay UEs contains only those that support the RSC associated with emergency service. We think that the remote UE need not explicitly report to the network about the switch to non-emergency service. In that sense, since different PDU sessions are established for emergency and non-emergency services, some indication from CN to RAN during this establishment may be utilized by the gNB to learn the service type. |

Question 1b: If yes to Q1a, do you agree with the above P1 from R2-2302648?

| Company | Yes/No | Comments |
| --- | --- | --- |
| OPPO | Yes | Since otherwise gNB cannot know the change of service at the remote UE. And one may propose to rely on CN to indicate the start/stop of emergency/non-emergency service to gNB, which is also a feasible way-out in our view. Yet in that case, we need to make our down-selection more visible to S2/R3, and thus a LS is preferred to notify S2/R3 on our assumption since finally there would be impact to architecture / system but not just a R2-only issue that we can make our decision. Updated comment: Based on the companies replies so far (and some offline discussions), seems there is a majority preference on reusing the existing mechanisms, the following WFs are proposed by companies Remote UE requests to release the connection with NW via NAS release request for the old service, and initiate a new connection for the new coming service with a cause value to indicate the intended service; Rely on CN to indicate the coming service to gNB For the above 2 directions, we are open to follow majority view as long as we have a common understanding on this issue, and if RAN2 made conclusions have impact on other WGs (e.g., SA/RAN3), a LS may be required. |
| Xiaomi | No with comments | We prefer to rely on CN to indicate the start/stop of emergency service, which is aligned with legacy behaviour. In legacy, emergency service is also supported on Uu, but no such start/stop indication was introduced in AS. However, CN may not able to acknowledge IDLE/INACTIVE remote UE selects which relay UE. Therefore, Relay UE in RRC_CONNECTED shall report the emergency indication associated with the remote UE ID to gNB, if IDLE/INACTIVE remote UE with emergency service RSC established PC5 connection with relay UE. [OPPO] Can Xiaomi further clarify why we want to do “Relay UE in RRC_CONNECTED shall report the emergency indication associated with the remote UE ID to gNB”, since the problem we are facing up with is network need to base on the service type of remote UE to choose proper relay, if the remote UE has connected to relay UE (the scenario you referred to?), the relay down-selection has happen already? [Xiaomi] maybe we have different understanding about the issue. For the relay selection part, it’s discussed in P2. In P1, I understand P1 focus on how to notify NW there is emergency remote UE connected, so corresponding connected relay UE can be prioritized, i.e. Relay UE in RRC_CONNECTED shall not be released due to load control. If remote UE is in RRC_CONNECTED, NW can acknowledge the emergency remote UE by CN indication. But CN is not aware of IDLE/INACTIVE remote UE with emergency SRC has selected which relay UE. Relay UE may be released due to load control. That’s why we propose “Relay UE in RRC_CONNECTED shall report the emergency indication associated with the remote UE ID to gNB” [OPPO2] Firstly just try to clarify: the 2 proposals (P1/P2) are for the same issue, i.e., NW needs to know when(P1) and how/which relay(P2) to configure the path switching for remote UE to due to change of service type (i.e. between emergency and non-emergency service); it is not necessary that “corresponding connected relay UE can be prioritized, i.e. Relay UE in RRC_CONNECTED shall not be released due to load control”, it could be that another relay is to be used/prioritize, where the key is to let gNB know the service type, and then gNB can decide which relay UE (the serving one or another one) is the best choice considering the on-going service type. And we do not understand why the concern is for ‘But CN is not aware of IDLE/INACTIVE remote UE’, since to us the IDLE/INACTIVE UE has not initiate service, either emergency or non-emergency.. |
| Qualcomm | No | As commented for Question 1a |
| vivo | No | See comments for Question 1a |
| Lenovo | No | see comments for Q1a. |
| ZTE | No | See comments for Question 1a |
| vivo | No | See comments for Question 1a |
| Nokia | NO | See comments for Q1a |
| Intel | No | See comment for Q1a |

[Rapp summary]

Among the 14 companies replied Q1a/1b, 13 companies prefer reusing legacy/high-layer tools, i.e., gNB may know the service type info based on

- cause value from remote UE with the assumption that When remote UE is initially doing service-type-1 and later service-type-2 comes, it would tear down service-type-1 autonomously (e.g., using NAS release request, as suggested by company), and will go to RRC_IDLE, and then use the cause value in RRC setup to notify gNB on the service-type-2 (as suggested by company);

- or CN indication (e.g., ARP, as suggested by company)

If the answer to Q1b is “Yes”, i.e., Remote UE needs to indicate to network on the start/stop of emergency and non-emergency service, the spec impact should be discussed.

One simple solution is that we use the RRC signalling, e.g., add a new field in SUI to indicate, as shown in the below TP:

SidelinkUEInformationNR-v1800-IEs ::= SEQUENCE { emergencyService-r18 ENUMERATED {true} OPTIONAL, nonEmergencyService-r18 ENUMERATED {true} OPTIONAL, nonCriticalExtension SEQUENCE {} OPTIONAL } …

The following Q is to check companies’ view on the spec impact of Proposal 1 of R2-2302648 on the message.

Question 1c: If yes to Q1b, what is your view on the spec impact of Proposal 1 of R2-2302648 regarding the message?

Option-1: Using SUI to indicate, e.g., as the above TP;

Option-2: Others;

| Company | Which RRC message to use | Comments |
| --- | --- | --- |
| OPPO | Option-1 |  |

The following Q is to check companies’ view on the spec impact of Proposal 1 of R2-2302648 on the code-point.

Question 1d: If yes to Q1b, what is your view on the spec impact of Proposal 1 of R2-2302648 regarding the code-point?

Option-1: Using optionality of “ENUMERATED {true}” to indicate for emergency and non-emergency separately, e.g., as the above TP;

Option-2: Others;

| Company | What code-point to introduce | Comments |
| --- | --- | --- |
| OPPO | Option-1 |  |

Then, in R17 U2N relay service continuity, the measurement reports from remote UE to network was defined to indicate the candidate relay UEs information as follows.

SL-MeasResultListRelay-r17 ::=                  SEQUENCE (SIZE (1..maxNrofRelayMeas-r17)) OF SL-MeasResultRelay-r17

SL-MeasResultRelay-r17 ::=                      SEQUENCE {

cellIdentity-r17                                CellAccessRelatedInfo,

sl-RelayUE-Identity-r17                         SL-SourceIdentity-r17,

sl-MeasResult-r17                               SL-MeasResult-r16,

...

}

While in R18, differentiation of emergency and non-emergency relay link is needed. Hence, the remote UE also needs to indicate whether each candidate relay supports emergency or non-emergency service so that network can decide on the proper configurations. The following Proposal2 from R2-2302648 has discussed this issue

- Remote UE indicates to network on the supported service of candidate relay. FFS on the detailed report form, e.g., RSC or service type (emergency, non-emergency).

The following Qs are to check companies’ view on the above Proposal 2:

Question 2a: Do you agree the network has to base on candidate relay UE service type information (emergency or non-emergency) to decide on indirect / relay path (re)configuration?

| Company | Yes/No | Comments |
| --- | --- | --- |
| OPPO | Yes | Since otherwise gNB cannot decide a proper target relay UE. And one may propose to rely on remote UE’s higher layer to filter the candidate relay UE before reporting to network, i.e., only report the emergency or non-emergency relay UE based on the UE’s on-going traffic type. For this method, our understanding is in case the UE is doing both emergency and non-emergency service types simultaneously, 1/ Either the UE implements it in a way that only RSC supporting both emergency and non-emergency would be reported, but S2 has not concluded whether there is such case, and it makes network incapable to configure the remote UE on a relay UE supporting emergency traffic only, when there is no RSC supporting both. 2/ Or the UE implements it in a way that both RSC supporting emergency only and supporting non-emergency only would be reported, but network would not be able to differentiate between the two. So it is not a feasible solution in the end regardless how UE implements it. Updated comment: Based on companies replied so far, it seems companies believe rely on remote UE’s higher layer to filter the candidate relay UE before reporting to network is sufficient since there is either no-going emergency service or non-emergency service but not both. We are open to follow majority view on this as long as we have the same understanding on the assumption, i.e., RAN2 confirms to rely on remote UE’s higher layer to filter the candidate relay UE supporting emergency or non-emergency service before reporting to network based on the assumption that there is either no-going emergency service or non-emergency service. RAN2 would not consider / optimize for the case where both emergency and non-emergency service types are running (simultaneously) at remote UE. |
| Xiaomi | No | In SA2’s spec 23.304, it specifies the PC5 link with emergency RSC is only used for emergency service. Therefore, emergency and non-emergency service would not reside on the same PC5 link. 5.4.x Support of emergency service from 5G ProSe Remote UE via 5G ProSe UE-to-Network Relay 5.4.x.1 General … A PC5 link associated with a dedicated emergency RSC is only used for emergency service. … In current measurement report, UE would only consider relay UE fulfilling upper layer criteria as applicable as following. Therefore, if relay UE doesn’t support correct service type information (emergency or non-emergency), relay UE would not be fulfil the upper layer criteria. UE would not report such relay UE in the measurement report. 5.5.4 Measurement report triggering 5.5.4.1 General … 3> else if the corresponding measObject concerns L2 U2N Relay UE: 4> if eventY1-Relay or eventY2-Relay is configured in the corresponding reportConfig; or 4> if corresponding reportConfig includes reportType set to periodical: 5> consider any L2 U2N Relay UE fulfilling upper layer criteria detected on the associated frequency to be applicable for this measId; [OPPO] As we already clarified in our reply above, it is unclear what is the companies view on the remote UE behavior when it is performing both emergency and non-emergency service, can Xiaomi further clarify this point? [Xiaomi] according to SA2 spec, I understand the relay UE and remote UE shall not reuse the same PC5 link for emergency and non-emergency service. So, upper layer can filter the candidate relay UE according to emergency SRC. Remote UE only report the emergency or non-emergency relay UE based on the remote UE’s on-going traffic type, i.e. either emergency or non-emergency. [OPPO2] The intended case for both emergency and non-emergency service here is for remote UE, i.e., the remote UE can have emergency and non-emergency service initiated, we did not try to hint whether to run them on the same PC5 link.if there is such PC5 link, we can do it. If no (as suggested by you), only one of the two service type can be supported – yet the premise of that is to let gNB knows the service type(s) which are running, and the service type(s) of each relay UE supports. |
| Ericsson | No, see comments | It is unclear which scenario is being targeted here. Our understanding is that it is under the scenario where a relay UE supports non-emergency services but not emergency services. Given the importance of emergency services, this is a corner case. [OPPO] We did not point to the scenario of ‘a relay UE supports non-emergency services but not emergency services’. Either 1) remote UE is doing 1) emergency only, 2) non-emergency only, or 3) both emergency and non-emergency are all being considered here. In the case of RRC connection establishment, it is up to the remote UE to decide on the appropriate relay UE. Then, in MSG3 include the cause for establishment i.e., emergency/non-emergency. The network will know from MSG3 the appropriate configuration. [OPPO] What about the case where the remote UE initiates one additional service type when performing one service type already, e.g., the remote UE is in RRC_CONNECTED, doing emergency, and initiating an additional non-emergency service, or vice versa. [Ericsson, additional response] Like in the above case, the remote UE can always tear down the connection and set it up again. There is no specific requirement in SA2 to (re)configure or maintain the existing link. I am not sure about the scenario where a remote UE doing emergency will add a non-emergency session. Our understanding is that emergency services will always be prioritized over all other services. In the case of path switch, the remote UE can indicate to the source gNB a list of candidate relay UEs. This can be based on the existing service at the remote UE i.e., emergency/non-emergency. In which case, for emergency, the remote UE can only report those candidates to the gNB which support emergency. Hence, the gNB will always choose a candidate which supports emergency. Soon, if the remote UE chooses to switch to non-emergency, it can tear down the connection (as in Q1a) and initiate connection establishment again via the same or a different relay UE. [OPPO] Same question here as in Q1a, what if the remote UE does not experience an RRC state transition here? I.e., the UE is still in RRC_CONNECTED (not released to RRC_IDLE/INACTIVE), and initiate the non-emergency (either when the emergency service is still on-going, or when the emergency service has ended). [Ericsson, additional response] As again, there are no requirements in SA2 for the UE to always stay in RRC_CONN. In addition, in our understanding, emergency services are always prioritized over all non-emergency services. In general, the remote UE in all cases can go to IDLE and transition back to CONN state for the required (emergency/non-emergency) service. |
| Qualcomm | No | When the Remote UE (re)selects a candidate Relay UE, the supported RSC is already considered. It is unclear whether it is possible Remote UE has two PC5 links (one is for emergency, another is for non-emergency) towards one Relay UE with on Uu connection. [OPPO] As we have replied to Xiaomi above, the intended case for both emergency and non-emergency service here is for remote UE, i.e., the remote UE can have emergency and non-emergency service initiated, we did not try to hint whether to run them on the same PC5 link or have 2 PC5 link simultaneously, yet the premise of that is to let gNB knows the service type(s) which are running, and the service type(s) of each relay UE supports. |
| vivo | NO | Same view as Qualcomm. We also think that, if there is on-going emergency service at the remote UE side, the upper layer criterion for suitable relay guarantees that the remote UE will only include the candidate relay UE which supports emergency service in sidelink measurement report. No extra RAN2 impact. |
| Lenovo | No | Before reporting measurement result, the remote UE needs to perform discovery procedure. During discovery procedure, the remote UE can filter the candidate relay UE. |
| ZTE | comments | Agree with the above comments that the supported service is already considered when remote UE reporting candidate relay UEs. On the other hand, gNB can let remote UE to select the relay UE in this case (i.e. when a new PDU session establishment for emergency/non-emergency service is initiated). |
| Huawei, HiSilicon | See comments | What we learned from SA2 discussion is that the emergency specific RSC is configured to relay/remote UE by CN, after that relay/remote UE can involve in a discovery procedure using this RSC. In this sense, it seems network can make sure that the RSC(s) is configured to the remote UEs and relay UEs in the same area. So we are not sure if there is a need to differentiate the UE capability from RAN2 perspective. |
| CATT | See comments | More interaction with SA2 on this topic is needed. |
| NEC | NO |  |
| Nokia | NO | Agree with the comments above: for emergency services the remote UE will only consider relay UE candidates that support emergency services based on RSC. |
| Samsung | No | We share the views that candidate relay UE reported by Remote UE was already filtered based on RSC. |
| Apple | No | Agree with other companies that filtering based on RSC is done in remote UE before sending measrementReport. |
| Intel | No | As we hinted in the comment to Q1a and other company comments as well, we think that the RSCs supported by the relay UE would be already considered during discovery by the remote UE. Agree to the following aspect as part of the summary from email Rapporteur “RAN2 would not consider / optimize for the case where both emergency and non-emergency service types are running (simultaneously) at remote UE.” |

[Rapp summary]

Among the 14 companies replied Q2, 13 companies prefer reusing legacy/high-layer tools, i.e., remote UE’s higher layer would filter the candidate relay UE before reporting to network based on no-going emergency service or non-emergency service.

Based on companies reply to P1 and P2, the following way forward is suggested:

R2 assume no additional R2 impact for gNB to know the initiated service-type of remote UE, and to select proper relay UE serving the initiated service-type of remote UE, without consideration / optimization of remote UE doing both emergency and non-emergency simultaneously (when it happens, R2 assume UE would tear down one service-type by using NAS release request).

Question 2b: If yes to Q2a, do you agree with the above P2 from R2-2302648?

| Company | Yes/No | Comments |
| --- | --- | --- |
| OPPO | Yes | Since otherwise gNB cannot decide a proper target relay UE. |

Then if the answer to Q2b is “Yes”, i.e., Remote UE needs to indicates to network on the supported service of candidate relay.

Similar to Q1c, the simple solution is also using the RRC signalling, e.g., add a new field in SL-MeasResultRelay to additionally indicate the supported service of each candidate relay UE, the spec impact should be discussed as shown in the below TPs:

SL-MeasResultRelay-r17 ::= SEQUENCE { cellIdentity-r17 CellAccessRelatedInfo, sl-RelayUE-Identity-r17 SL-SourceIdentity-r17, sl-MeasResult-r17 SL-MeasResult-r16, ..., [[ sl-RelayUE-Service-r18 ENUMERATED {emergency, non-emergency} OPTIONAL ]] }

The following Q is to check companies’ view on the spec impact of Proposal 2 of R2-2302648 on the message.

Question 2c: If Yes to Q2b, what is your view on the spec impact of Proposal 2 of R2-2302648 regarding the message?

Option-1: Add a new field in SL-MeasResultRelay, e.g., as the above TP;

Option-2: Others;

| Company | What code-point to introduce | Comments |
| --- | --- | --- |
| OPPO | Option-1 |  |

The following Q is to check companies’ view on the spec impact of Proposal 2 of R2-2302648 on the code-point.

Question 2d: If Yes to Q2b, what is your view on the spec impact of Proposal 2 of R2-2302648 regarding the code-point?

Option-1: Using service type to indicate, e.g., as the above TP;

Option-2: Others;

| Company | What code-point to introduce | Comments |
| --- | --- | --- |
| OPPO | Option-1: ENUMERATED {emergency, non-emergency} |  |

According to the above SA2 specs, relay UE shall set its cause value as “emergency” when the relay connection was requested using emergency RSC. This issue has been discussed in last RAN2 meeting with no clear conclusion

R2-2300129 Discussion on emergency service OPPO discussion Rel-18 NR_SL_relay_enh-Core Proposal 1 To align with S2, Relay UE set the cause value to ‘emergency’ based on RSC instead of SL-RLC0 message reading. And leave the AS/NAS layer interaction to UE implementation. Discussion: Xiaomi think this is not exactly alignment with SA2, and the existing mechanism can already fulfil the requirement. They think this is not the intended use of the RSC. LG think we already made the emergency cause value available in Rel-17, and changing the mechanism now may not be helpful. OPPO understand that SA2 have specified a mechanism to know from the discovery procedure when the service is for emergency, and we left it to UE implementation in Rel-17. Qualcomm think the remote UE should be the one to determine the emergency cause value, not the relay UE. Xiaomi understand it is up to UE implementation to set values other than emergency. Ericsson wonder if the relay UE gets the RSC and then initiates an SRB0 message, or if this relates to the relay UE’s handling of the cause value from the remote UE. OPPO clarify that when the relay UE gets a message from the remote UE, if the relay UE is in idle/inactive, the relay UE needs to set some cause value; in Rel-17, we specified the behaviour based on SL-RLC0 contents, and in Rel-18, their understanding is that SA2 have said it should depend on the RSC. Nokia think either we say that when the remote is using emergency RSC it should also set the emergency cause value (and we can use the Rel-17 mechanism), or we say that we have a new requirement for the relay UE to check the RSC instead. They think the Rel-17 mechanism works without additional burden to the relay. Ericsson have a similar concern to Nokia. They do not see the advantage of changing. NEC think we may need more time to understand the SA2 situation. We already have a Rel-17 mechanism, and if SA2 want to change it, it’s not very clear why. They think we could postpone the discussion. OPPO understand that companies would like to rely on the Rel-17 solution, but we should be aware of the SA2 status. InterDigital recall us spending quite a bit of time on this discussion, and the solution we have seems to work; so they are a bit sceptical. Kyocera think it can be left for relay UE implementation whether to use the RSC. Qualcomm are not sure if SA2 are aware of our current solution; they think we could send an LS to SA2 to inform them. Apple think we don’t need to send an LS and we can agree with NEC’s suggestion to postpone this proposal.

And there are proposals on the disconnect concern between SA2 and RAN2 on how to set the cause value from the relay for emergency service

Proposal 3 RAN2 to confirm that the relay UE cause value setting behaviour for emergence service relaying is based on SL-RLC0 message from remote UE as Rel-17. Proposal 4 Inform SA2 on RAN2 conclusion based on above Proposal 3 and it’s up to SA2 how to update their specification.

So the follow Q is to check companies view on the need for RAN2 to align with SA2 on relay setting of the cause code for emergency service.

Question 3: Do you there is a need for RAN2 to align with SA2 on relay setting of cause value for emergency service?

Option-1: Yes;

Option-2: No, and the LS to SA2 to indicate the mis-match between SA2 and RAN2 conclusion;

| Company | Option | Comments |
| --- | --- | --- |
| Ericsson | See comments | No strong opinion. But P3 as such as agreed in Rel-17 does not follow the L2 relaying principles of transparent forwarding of data between remote UE and gNB. Okay to follow majority view. |
| Xiaomi | 2 with comments | We understand the SA2 requirement can already fulfilled by RAN. |
| Qualcomm | See comments | There are two cases here. For the SL-RLC0 message, then Rel-17 mechanism can be reused. But for the case that Remote UE is switched to indirect path, there is no cause value in SL-RLC1 message, then it should be Relay UE to set the cause value in Request or Resume message based on the RSC info. It is suggested to discuss this issue in RAN2. |
| Vivo | Option-2 with comments | For the SL-RLC1 case as mentioned by Qualcomm (i.e. relay UE’s RRC connection stablishment triggered by RRCReconfigrationcomplete), we think it’s not touched in SA2 specification and thus no mismatch between RAN2 and SA2. Moreover, for the SL-RLC1 case as currently in Rel-17 it’s up to relay UE implementation how to set cause value, therefore it can be up to relay UE implementation to take the RSC info from remote UE into account. |
| ZTE | comments | No need LS to SA2, RAN2 could update RRC spec on how the relay UE sets the establishment cause for SL-RLC1 case if needed. |
| OPPO | See comments | Based on the reply so far, seems the key point here is the cases when there is no “cause value” in remote UE’s first RRC message to relay UE, i.e., SL-RLC1, the WFs for this issue can be limited to SL-RLC1 (to avoid backwards compatibility issue at RAN2 side), and the option-1 and option-2 in Q3 can be limited to the delta part, i.e., SL-RLC1 case. |
| Huawei, HiSilicon | See comments | In our understanding what to be defined by SA2 seems to be that a discovery/DCR using emergency service RSC will bring relay UE to connected state, in which case, the cause value should be set to emergency. At least the current wording in RRC is not against the new case defined by SA2. And if SA2 can capture such case in CT1/SA2 spec, maybe RAN2 do not need to change RRC. But we are open to further discuss. |
| CATT | Option-2 | In Rel-17 U2N relay, we raised that once the relay UE received the first RRC message to relay UE, the relay UE will send one indication to Upper layer, then upper layer trigger the AS layer to establish the Uu connection. This is one unify procedure. But unfortunately, R2 reached that the relay UE can directly establish the Uu connection, which causes the current issue. |
| Nokia | 2, Comments | Our view is that for the L2 relay scenario SA2 could create requirements (“the L2 relay UE shall use “emergency cause value”), but it is in the scope of RAN2 to specify how (based on what information) the L2 relay UE performs the setting. We think that the SA2 specification does not specify how (based on what information) the L2 relay UE sets the cause value, and thus it is not necessary to send an LS to SA2. At the previous RAN2 meeting it was agreed to re-use the Rel-17 mechanism when the remote UE provides a cause value. Further RAN2 discussion is needed how to handle the case when it is not there (during path switch). |
| Apple | Option-2 | We are fine to send a LS to SA2 to further check how to resolve this. |
| Intel | Option-2 | From the discussion above, we understand that whether it is via SL-RLC0 or SL-RLC1, the relay UE can consider the RSC information (from discovery/PC5 link establishment) and correspondingly take it into account or not based on implementation to set its own cause value. No strong view about the LS. |

[Rapp summary]

Seems the key point here is the cases when there is no “cause value” in remote UE’s first RRC message to relay UE, i.e., SL-RLC1, the WFs for this issue can be limited to SL-RLC1 (to avoid backwards compatibility issue at RAN2 side), and among 11 companies replied this question,

2 companies prefer Option-1: change the RRC spec to align the SL-RLC1 case with SA2

7 companies prefer Option-2: no need to change RRC spec (yet since there is no cause value in SL-RLC1 messages, so reusing R17 solution, based on Rapp understanding, means it would be up to relay UE to set the cause value, and would not set it as emergency since R17 spec says: NOTE 2:	In case the L2 U2N Relay UE initiates RRC connection establishment triggered by reception of message from a L2 U2N Remote UE via SL-RLC0 or SL-RLC1 as specified in 5.3.3.1a, the L2 U2N Relay UE sets the establishmentCause by implementation, but it can only set the emergency, mps-PriorityAccess, or mcs-PriorityAccess as establishmentCause if the same cause value is in the message received from the L2 U2N Remote UE via SL-RLC0.)

2 companies seem open to further discuss this issue/follow majority view.

Rapp would like to suggest follow majority view on this, i.e., no change of RRC spec and send LS to SA2 to indicate this mis-match.

R2 confirm R18 relay UE sets cause value for emergence service relaying as in Rel-17 for both SL-RLC1 and SL-RLC0 traffic (i.e., for SL-RLC1, relay UE would not set cause value as emergency).

R2 sends LS to S2 to notify the conclusions above.

# Conclusion

We have the following proposals:

Proposal 1	R2 assume no additional R2 impact for gNB to know the initiated service-type of remote UE, and to select proper relay UE serving the initiated service-type of remote UE, without consideration / optimization of remote UE doing both emergency and non-emergency simultaneously (when it happens, R2 assume UE would tear down one service-type by using NAS release request).

Proposal 2	R2 confirm R18 relay UE sets cause value for emergence service relaying as in Rel-17 for both SL-RLC1 and SL-RLC0 traffic (i.e., for SL-RLC1, relay UE would not set cause value as emergency).

Proposal 3	R2 sends LS to S2 to notify the conclusions above.

# Reference

- TS 23.700 Proximity based Services (ProSe) in the 5G System

- 3GPP TS 23.304 V18.1.0

- R2-2302648	Discussion on emergency service for SL Relay	OPPO	discussion	Rel-18	NR_SL_relay_enh-Core, TEI18

- R2-2303341	Remaining issues on service continuity enhancement for L2 U2N relay	vivo	discussion